## Slide 1: Developing & Evaluating Space-Based Earth Observation Data Requirements for GEOGLAM
Alyssa K. Whitcraft et al.
GEOGLAM Secretariat akwhitcraft@GEOGLAM.org
CEOS LSI-VC-3 Meeting
ESA ESRIN, Frascati, Italy – 21 March 2017

## Slide 2: The GEOGLAM Requirements Process
WHY do we need to monitor?  Information Needs, Supporting Decisions
  e.g. Production & supply outlooks; Early warning; Precision agriculture/farmer information
WHAT variables?  Monitoring application’s data Needs, to derive Information
WHAT instrument characteristics?  Spatial, Spectral
WHERE?  Target features
  e.g. major croplands; S/M/L fields; rangelands
WHEN?  Target periods
HOW OFTEN?  Two time scales
  Every year? Every 5 years? Every decade?
  How many times per year? [more common for ag applications]
PRIORITY?
1. Policy Driver
2. Tabular Best Practices, Community Insight
3. Tabular
+
Spatial Datasets
Spatial Datasets:
Cropland mask
Field Size Distribution
Crop Calendars
Cloud coverage (impact on optical)
Priority Croplands
4. Mission capacity & gap analyses
Notes: This process might be a bit different for Carbon – seems like the main goal is inventory (on what time step?).
- You are not likely reporting multiple times per year, but you may need to monitor certain highly dynamic events (e.g. fires) as input to a larger inventory.

## Slide 3
Observation
Requirements
Table
Note:
Optical = Reflective & Emissive (Thermal)
State of the Science as
2012-2015
Currently undertaking “reboot” of best-practices, polling community
Notes: TALKING POINTS
In 2012, GEOGLAM scientists & CEOS representatives met at CSA in Montreal to develop a refined and set of EO requirements which are necessary to generate a variety of target products or applications (crop mask, crop type area, crop condition, crop yield, crop biophysical variables (LAI), environmental variables, and information on cropping system (crop cycles).
The requirements (such as these [ANIMATION] for moderate resolution instruments like Sentinels and Landsats) are broken down by spatial and spectral ranges (the “what?”), each with a corresponding temporal requirement for cloud free data (sometimes different revisit frequencies are needed during the season vs. out of season) as well as information on the geographic extent to which the data are necessary (all croplands? Or just a sample? Are the data necessary for just small and medium fields, or for all fields?).

## Slide 4: Key Components of Spatially Explicit EO Requirements
Where to image?
When to image?
How frequently to image?
At what spatial & spectral resolution [instrument type] to image?
‘best-available’ cropland mask + field size distribution (e.g. Fritz et al., 2015)
Agricultural growing season calendars (e.g. Whitcraft et al., 2014)
Cloud cover info (e.g. Whitcraft et al., 2015a)
+
GEOGLAM Requirements Table
(How) can we meet these requirements?
(Whitcraft et al., 2015c)
Notes: The key components of EO requirements include where to image (as in where the crops of interest are – as indicated by information on crop location and field size distribution), when to image (clarified by when crops are growing), and how frequently/at what spatial resolution to image – determined by the applications of these data (such as crop type and crop condition) and the methods used to derive that information. We combined all of these together for the different requirements in the table, to see where, when, and how frequently we’d really have to image (incorporating cloud cover, as necessary) to meet our EO requirements.

## Slide 5
What is the revisit frequency required (RFR) to probabilistically return
a reasonably cloud free clear view within 8 days over croplands of all sizes? (Req #5)
[GSCs] + [crop mask + field size] + [cloud cover impacts + req table]
Two thresholds of acceptable clarity: ≥ 70% or ≥ 95%
When?
Where?
Revisit Frequency Required?
Notes: At this point, we need to place these requirements in the spatial context – what do we need, when, and where? Again, we’re drawing on the two perspectives of cloud cover

## Slide 6
Chart: % of Cells
| 0-1 | 1-2 | 2-3 | 3-4 | 4-5 | 5-6 | 6-7 | 7-8 | 8
Jan | 3.9567 | 15.6177 | 14.6961 | 10.4296 | 8.945 | 8.4954 | 9.5008 | 5.3261 | 23.0326
Feb | 3.2183 | 10.3356 | 13.2973 | 16.9622 | 13.0578 | 13.3534 | 4.9009 | 2.7235 | 22.151
Mar | 1.8128 | 7.9287 | 18.0505 | 19.9146 | 17.268 | 12.6365 | 8.2097 | 2.4609 | 11.7183
Apr | 1.2561 | 6.9387 | 12.9876 | 30.5166 | 21.2279 | 11.6119 | 7.4012 | 3.723 | 4.3369
May | 0.74734 | 6.2862 | 11.9297 | 26.4754 | 25.1729 | 13.2419 | 5.3237 | 2.851 | 7.9719
Jun | 2.2018 | 9.0053 | 14.6282 | 24.3061 | 20.071 | 8.8867 | 5.2495 | 2.9524 | 12.6989
Jul | 8.1567 | 11.5968 | 16.0743 | 17.4982 | 13.8608 | 11.0371 | 6.5884 | 3.0247 | 12.163
Aug | 9.4472 | 13.0988 | 14.1732 | 17.9887 | 14.1481 | 11.7665 | 7.496 | 4.2162 | 7.6654
Sep | 2.0347 | 10.3066 | 14.1804 | 20.4977 | 16.8944 | 15.613 | 9.065 | 3.5836 | 7.8244
Oct | 1.0133 | 9.153 | 18.4652 | 16.8832 | 14.5688 | 14.2137 | 6.7791 | 3.4937 | 15.4301
Nov | 2.1698 | 19.8732 | 13.5007 | 9.8005 | 10.7774 | 9.5082 | 7.4224 | 3.2307 | 23.7171
Dec | 3.6293 | 17.5467 | 13.1646 | 11.2718 | 7.798 | 5.6222 | 6.3527 | 3.3883 | 31.2265
Chart: Revisit Frequency Required (Days)
| 0-1 | 1-2 | 2-3 | 3-4 | 4-5 | 5-6 | 6-7 | 7-8 | 8
Jan | 28.4349 | 25.2103 | 20.9829 | 8.0155 | 4.7332 | 6.5235 | 4.0688 | 1.4424 | 0.58853
Feb | 20.5399 | 36.3314 | 19.7475 | 5.1701 | 4.7155 | 4.3578 | 3.2129 | 3.0235 | 2.9015
Mar | 19.0788 | 45.8959 | 22.1658 | 4.531 | 2.6005 | 2.8453 | 1.4744 | 0.96017 | 0.4482
Apr | 13.933 | 58.9939 | 21.0086 | 4.8348 | 1.0168 | 0.19557 | 0.01069 | 0.0026286 | 0.0040306
May | 12.3205 | 58.2911 | 19.9617 | 5.8471 | 2.3826 | 0.80779 | 0.19492 | 0.061339 | 0.13307
Jun | 17.5913 | 52.6212 | 15.6583 | 6.3379 | 3.4528 | 2.0342 | 1.001 | 0.63356 | 0.66973
Jul | 27.4328 | 39.7541 | 19.2197 | 5.9245 | 2.9717 | 1.8774 | 0.86443 | 0.74619 | 1.2093
Aug | 29.6371 | 39.2188 | 21.5772 | 5.4706 | 1.1236 | 0.77568 | 0.51966 | 0.47608 | 1.2012
Sep | 18.6077 | 45.3062 | 26.6223 | 5.4491 | 1.4191 | 0.793 | 0.64993 | 0.45083 | 0.70192
Oct | 18.7835 | 41.3001 | 22.7065 | 7.7606 | 3.0343 | 2.141 | 2.4284 | 1.1823 | 0.6633
Nov | 30.0715 | 26.0501 | 18.6408 | 6.7783 | 6.351 | 6.3297 | 3.578 | 0.74652 | 1.454
Dec | 28.2737 | 25.1366 | 13.6789 | 8.6972 | 6.6909 | 6.7411 | 6.5756 | 2.8182 | 1.3878
≥ 70% Clear
≥ 95% Clear
What is the revisit frequency required (RFR) for a view at least 70% or 95% cloud-free within 8 days over in-season global croplands?
Whitcraft et al., (2015a), Rem. Sens.
Requirement #5
Notes: The maps show what revisit frequency would be required to yield a view at least 70% (top) or 95% (bottom) cloud free within 8 days over in season croplands. For 70% clear, 8 days is sometimes sufficient, but generally most areas are in the 3-5 day range. For 95% clear, a much more frequent revisit is required.
- Determining acceptable cloud cover thresholds is a priority research area

## Slide 7
 | Agency, Satellite, Sensor | Revisit | Spatial Res
L7 | NASA/USGS Landsat 7 ETM+ | 16 Days | 30-60 m
L8 | NASA/USGS Landsat 8 OLI, TIRS | 16 Day | 30-100 m
S2A | ESA Sentinel-2A MSI | 10 Days | 10-20 m
S2B | ESA Sentinel-2B MSI | 10 Days | 10-20 m
R2 | ISRO Resourcesat-2 AWiFS | 5 Days | 56 m
Overpass Analysis:
CEOS SEO
(How) can we meet these requirements for
optical, moderate resolution (10-70m)
data within 8 days during the growing
season with current & planned missions?
Revisit Capabilities
of the
7 Hypothetical
Constellations
Whitcraft et al., (2015b), Rem. Sens.
Notes: To evaluate our ability to meet these requirements, Brian Killough’s group at the CEOS SEO (NASA Langley) have utilized their COVE tool to model coincident overpasses of hypothetical constellations of polar-orbiting, optical, moderate resolution (10-100m) systems.
Most of these constellations have a revisit of less than a day to 4.5 days (the two present Landsat are at 8 days almost everywhere)  these are acquisition opportunities, mind you, not necessarily acquisitions… only the 2 Sentinels are claiming to have systematic acquisitions, L7+L8 are close, SLC-off issues not withstanding.
Constellation #7 is what we have now… 8 days in most locations
Constellation #3 is what we could have if AWiFS had systematic acquisition/and we could gain access to the data… 1-3 days
Constellation #5 is what we’ll have in ~2 years when the 2 Sentinel missions are lost (#4 if L7 is still functional at that point) … 1.5-4 days

## Slide 8
Meeting the Requirement for a view ≥ 70% Cloud Free within 8 days
(over global in season croplands)
# | Satellites
1 | L8, S2A, S2B, R2
2 | L7, L8, S2A, R2
3 | L7, L8, R2
4 | L7, L8, S2A, S2B
5 | L8, S2A, S2B
6 | L7, L8, S2A
7 | L7, L8
Meeting the Requirement for a view ≥ 95% Cloud Free within 8 days
(over global in season croplands)
Whitcraft et al., (2015b), Rem. Sens.
Requirement #5
Notes: We compared these overpass capabilities with the revisit frequency requirements for moderate spatial resolution within 8 days during the growing season.
Where you see any color, one or more of these constellations can meet the revisit frequency required to meet a 70% clear view (top) or 95% clear view (bottom)
Constellations are ranked – 1 is best performing, can meet everything 2-7 can
Where you see dark blue, all of the constellations can meet it, because 7 has the least frequent revisit
Where you see red, only that constellation (#1 – L8, S2A, S2B, R2) can meet
Where you see gray… none of these constellations can meet. Obviously, because the bottom is a more stringent requirement, you see more gray there.
The plots show you global success rates (where the hypothetical constellations can meet the revisit frequency requirements), and regional success rates for southeast Asia – the point being during certain times, obtaining at least 70% clear is not even possible with these constellations.
The last map shows you the number of months where these revisit frequencies exceed the capabilities of the hypothetical constellations – this is where we will have gaps and need to consider alternative data types (like SAR).

## Slide 9: Some thoughts on the value of this activity for LSI-VC & agencies
Tabular & spatial representation of common needs
  Where do we have critical gaps across MULTIPLE applications?
  Which observations have a high bang-for-their-buck return on investment?
  Acquisition planning for non-systematic sensors across multiple apps
  Future mission design & justification
Tie-ins to ARD work  what standard pre-processed products have utility across multiple activities?
  A “common denominator” of sorts