## Slide 1
Future US Land Imaging Jeffrey Masek, NASA GSFC
NASA Agency Update – CEOS LSI-VC-2
July 20-22, 2016
Dave Jarrett, NASA HQ
Jeff Masek, NASA GSFC
Harmonized Landsat/Sentinel-2 (HLS) Project
Jeff Masek, Junchang Ju, Eric Vermote, NASA GSFC
Martin Claverie, Jean-Claude Roger, Sergii Skakun, University of Maryland
Jennifer Dungan, NASA ARC
CEOS Joint Meeting, Frascati, September 2017

## Slide 2: Harmonized Landsat Sentinel-2 (HLS) Project
Merging Sentinel-2 and Landsat data streams can provide 2-3 day global coverage
Goal is “seamless” near-daily 30m surface reflectance record including atmospheric corrections, spectral and BRDF adjustments, regridding
Project initiated as collaboration among GSFC, UMD, NASA Ames

## Slide 3: HLS Test Sites
North America: 95
Alaska / NW Canada: 16
South America: 28
South-Africa: 166
Tanzania: 121
Germany: 62
Europe: 15
(w/o Germ.)
Africa: 6 (w/o SA and TZ)
S Asia: 122
NE Asia: 11
SE Australia: 141
69 Test sites (45 from NASA MuSLI team)
783 MGRS tiles
>7.5 million sq. km2
Landsat-8 data set: 147k products From Mar-2013 to Dec-2016
Sentinel-2 data set: 47k products From Jun-2015 to Dec-2016

## Slide 4: Expected Cloud-Free Observations
36
18
72
Observations/yr
Sentinel-2a + Landsat-8 revisit w/ cloud cover from MODIS CMG

## Slide 5: HLS Algorithm Flow
Atmospheric Correction | LaSRC/6S approach (image-based aerosol) | Vermote et al. (2016)
BRDF | corrected to nadir view / latitude-dependent solar angles using fixed coefficients | Roy et al. (2016)
Spectral bandpass | Linear regression using global training set from EO-1 Hyperion | Claverie et al., (in review)
Cloud/shadow mask | Landsat: output from LaSRC; S2: Boston University Fmask algorithm | Zhu et al. (2015)

## Slide 6: Results

## Slide 7
Grassland
Alfalfa
+
Sentinel-2 Landsat-8
Harmonized Landsat / Sentinel-2 Products
Laramie County, WY
NDVI
Day of Year
mowing
3km
May 4, 2016 (S2)
Aug 8 (L8)
Aug 17 (L8)
Sep 1 (S2)
Oct 20 (L8)
0.1 NDVI 0.9
Seasonal phenology (greening) for natural grassland (blue line) and irrigated alfalfa fields (red line) near Cheyenne Wyoming observed from Harmonized Landsat/Sentinel-2 data products. The high temporal density of observations allows individual mowing events to be detected within alfalfa fields. HLS Products available from https://hls.gsfc.nasa.gov

## Slide 8
55
Schuyler,
Nebraska
USDA 2016 Cropscape
5km

## Slide 9
Schuyler,
Nebraska
HLS NDVI
Filtered, interpolated to daily time step
0.0
1.0

## Slide 10
Crop NDVI Phenology
DOY (2016)
NDVI
Delaware, USA - crop type examples from USDA Cropland Data Layer (CDL)
HLS data interpolated and smoothed (10-day window)
Corn
Soybean
Double (Wheat/Soy)
Deciduous Forest

## Slide 11
4km
Crop Classification
Supervised classification (SVM) of HLS NDVI trajectories in Delaware, using USDA CDL as training
RGB image
USDA CDL
HLS Classification
water
corn
wheat/soy
soybean
wetland
forest
developed

## Slide 12: Crop Type Map for Germany
Crop type map derived from analysis of HLS imagery by Humboldt University/P. Griffiths (ESA Living Planet Research Fellow)
Based on data from Oct 2015-Dec 2016
21 land cover classes, 15 crop types
Overall accuracy 76%, several crop types >90% accuracy
http://www.esa.int/spaceinimages/Images/2017/08/Mapping_Germany_s_agricultural_landscape

## Slide 13: QA/QC & Validation
We distinguish between:
Product QA/QC – should the granule (or pixel) be flagged as of low or questionable quality?
Validation or Uncertainty Estimation – what is the uncertainty (bias, precision) of any observation relative to a standard?
HLS currently implements Product QA via three methods:
Comparison with daily MODIS CMG NBAR products
  Dataset & granule level metric
  Used to eliminate HLS granules with high number of discrepant 0.05° CMG reflectance values
Per-pixel time series smoothness
Other per-pixel attributes (cloud mask, shadow mask)

## Slide 14: QA: HLS v1.3 MODIS CMG Comparison
~1% S2a tiles rejected due to cloud mask

## Slide 15: HLS Uncertainty Estimation
Component “roll up” uncertainty budget based on:
LaSRC/6S atmospheric correction results (Vermote et al., 2016)
Roy et al (2016) BRDF error relative to MODIS MOD43
Calibration uncertainties
Spectral band regression tree errors
Note: BRDF uncertainty includes errors due to atmospheric correction as well, and thus could be overestimated.

## Slide 16: HLS Crosswalk to MRI Framework
Included as Appendix to Draft MRI Framework Document

## Slide 17: Lessons Learned / Issues
NASA/USGS/ESA collaboration on Landsat & Sentinel-2 radiometric calibration extremely valuable
Geolocation errors
  Landsat GLS Errors
  S2 yaw problem (pre-2.04 processing)
  HLS co-registers all data to a “reference” MSI image (~GRI)
S2 cloud masking problematic without thermal IR
  ACIX extension to cloud masks will be useful
Validation framework for surface reflectance products is weak
  In-situ data lacking
  BRDF-adjustments to NBAR may confound problem

## Slide 18: Status and Future Directions
Version 1.3 released July 2017
  Paper submitted to RSE special issue on Sentinel-2 Applications (Claverie et al, in review)
Version 1.4 to be released end-2017
  Wall-to-Wall North America + global test sites
  Incorporates Collection 1 Landsat and S2b data
  < 7 day latency
  Processing & data access via Amazon Web Services (AWS)
2018: global processing?

## Slide 19: Websites and Public Interface
HLS website
https://hls.gsfc.nasa.gov
Public access
Sample data available (via FTP)
Algorithm & Product descriptions
Request new sites
NEX project page
https://nex.nasa.gov/nex/projects/1371
Registered user access
All HLS data available
Documents (slides, user guides)

## Slide 20
Thank You
Delaware / New Jersey

## Slide 21
Backup

## Slide 22: HLS Products Specification
S10
Spatial: 10m, 20m, 60m
Spectral Bands: All MSI
Temporal: All Sentinel-2 L1C granules
NBAR: No
S30
Spatial: 30m
Spectral Bands: OLI-like + MSI Red Edge
Temporal: All Sentinel-2 L1C granules
NBAR: Yes
L30
Spatial: 30m
Spectral Bands: All OLI
Temporal: All Landsat-8 L1T granules
NBAR: Yes
M30
Spatial: 30m
Spectral Bands: OLI-like + MSI Red Edge + TIRS TOA
Temporal: 5-day “best pixel” based on min AOT
NBAR: Yes
All 4 products are aligned on the S2 Tiling system (Military Grid Reference System), following UTM zones + 3 letters defining a grid
Tiles are 110km square with 10km overlap for same UTM zone adjacent tiles
109,080m
UTM zone 35
UTM zone 36
Overlap area
S2 Tiles system

## Slide 23: HLS Algorithm Flow
Atmospheric Correction
BRDF Adjustment
S10 (MSI SR 10m)
S30
(MSI NBAR 30m)
L30
(OLI SR 30m)
M30
(5-day composite NBAR)
Landsat-8 (L1T)
Temporal Compositing
Geographic registration
Geometric Resampling
Sentinel-2 (L1C)
Offset
coefficients
BRDF Adjustment
Geometric Resampling
Band Pass Adjustment
Atmospheric Correction
Algorithm | Current (V1.2) | Other Options
Geographic registration | AROP (Gao et al. 2009, JARS) | -
Atmospheric Correction | OLI and MSI: Landsat-8 6S algorithm | CNES MACCS
Cloud/Shadow Mask | OLI: Landsat-8 6S algorithm output MSI: BU MSI Fmask | CNES MACCS
BRDF Adjustment | Fixed BRDF (Roy et al. 2016, RSE) | Downscaling MODIS BRDF + Fixed BRDF as Backup
Band Pass Adjustment | Fixed, per-band linear regression | Regression-tree (based on spectral shape)
Temporal Compositing | TBD | -

## Slide 24: HLS Algorithms
Atmospheric Correction
  Uses operational Landsat LaSRC approach (Vermote et al., 2016)
  Based on 6S radiative transfer model w/image-based aerosol retrieval
BRDF (view/solar angle) adjustment
  Uses Roy et al (2016) fixed BRDF shape
  Adjusted to nadir view and fixed, latitude-dependent solar angle (aka NBAR)
Spectral adjustment uses linear regression based on Hyperion hyperspectral images
Cloud mask
  Landsat: output from LaSRC atmospheric correction
  Sentinel-2: Boston University Fmask (non-TIR)

## Slide 25
Mis-registration between Landsat and Sentinel-2
  Up to 35m mismatch due to some areas of relatively poor Landsat ground control (Storey et al, 2016, RSE)
  USGS will improve Landsat ground control in ~2018-19
  For now, users can use automated cross-correlation algorithms to co-register and/or resample L8 to S2.
Mis-registration among early Sentinel-2
  S2a data (processed before June 2016) showed relative misregistration between adjacent orbits due to error in yaw processing
  Corrected with Sentinel-2 v2.04 processing
HLS uses a single Sentinel-2 image as reference for each time series & AROP to co-register
S2 / L8 Registration Issues
Improvement in Landsat L30 registration after referencing to MSI

## Slide 26
LaSRC Atmospheric Correction
Similar to MODIS Collection 6 approach & previous LEDAPS
Uses 6S radiative transfer model to correct for scattering (Rayleigh, Mie) and gaseous absorption
  MODIS water vapor
  NCEP GDAS ozone and surface pressure
  Aerosol optical thickness derived via fixed red/blue ratio observed in MODIS SR for every land location
Red/Blue ratio derived from MODIS (Vermote et al., 2016, RSE)

## Slide 27: BRDF Correction
Uses “fixed” coefficients of Roy et al (2016)
  Over narrow view angles, little improvement with using local or landcover-dependent kernel
Corrects to a fixed view (nadir) and solar (latitude-dependent) solar elevation
  Similar to MODIS NBAR but variable solar elevation

## Slide 28: HLS QC: Temporal Smoothness
day
VI (y)
Noise
Approach based on variance among cloud-free VI triplets (Vermote et al., 2009)
Per-pixel metric calculated from median of all triplets (N>6) in time series

## Slide 29: Why 30m HLS?
Example of reflectance time series from fine-resolution sensor (Sensor A) and coarser-resolution sensor (Sensor B). Over heterogeneous areas, the native-resolution time series shows temporal variability for pixels 1 and 2 even though the landscape is not changing, simply due to the fact that Sensor B averages the spatial response. Instead, HLS elected to average Sentinel-2 MSI data to the coarser, 30m resolution of Landsat-8 OLI.