## Slide 1: KARI’s Satellites & ARD
Chiho KANG & Daehoon YOO, KARI
CEOS LSI-VC-8
Agenda Session 9
Anchorage, USA
3-5 September 2019

## Slide 2: KARI’s LEO Missions
1999
EO, 6.6m
KOMPSAT-1
2006
EO, 1m
KOMPSAT-2
2013
SAR(X), 1m
KOMPSAT-5
2012
EO, 0.7m
KOMPSAT-3
(2021)
EO < 0.3m
KOMPSAT-7
(2020)
SAR(X), 0.5m
KOMPSAT-6
2015
EO, 0.55m
IR, 5.5m
KOMPSAT-3A
(2019/2020)
EO, 0.5m
CAS500-1/2
Low
Earth
Orbit
2022/2025
EO, 1m
SAR(C)
CAS500-4/5
2024
EO < 0.3m
KOMPSAT-7A
2024~2027
EO, 1m (10)
SmallSat
On Orbit
Not Working
Under Development
Planned

## Slide 3: Characteristics & Advantages of KOMPSAT: Fast Revisit
LTAN : 13:30
KOMPSAT-3
KOMPSAT-3A
EROS-B (Mono)
LTAN : 11:00
KOMPSAT-2
WorldView-1/2/3
Pleiades-1/2
LTAN : 06:00
KOMPSAT-5
COSMO-SkyMed
TerraSAR-X
LTAN : 18:00
KOMPSAT-5
COSMO-SkyMed
TerraSAR-X

## Slide 4: KARI Ground Stations with Global Networks
WENO Ground Station
(TT&C)
KARI Ground Station
(TT&C/Data Downlink)
SEJONG Ground Station
(TT&C)
Svalvard Ground Station
(TT&C/Data Downlink)
Neustrelitz Ground Station
(TT&C/Data Downlink)
Jeju Ground Station
(TT&C/Data Downlink)
S-band: TT&C
X-band: Science Data Downlink
HQ

## Slide 5: KARI Ground Station & Antenna Systems
13m Antenna
GEO-K1 Operation
GEO Support
9m Antenna
Backup
13m Antenna
KOMPSAT Operation
LEO Support
7.3m Antenna
KOMPSAT Operation
LEO Support
9m Antenna
GK-2 Operation
GEO Support

## Slide 6: Scene Acquisitions
KOMPSAT-3: ~1.37M Scenes (’12/05 ~ ’18/12)
KOMPSAT-5 : ~152K Scenes (’13/09 ~ ’18/12)
KOMPSAT-3A: ~400K Scenes(’15/03 ~ ’18/12)
KOMPSAT-2: ~3.17M Scenes (’06/08~ ’18/12)

## Slide 7: KOMPSAT Images: Spatial Resolution
KOMPSAT-2
KOMPSAT-3
KOMPSAT-3A
Resolution (Pan/MS: 1/4m)
Resolution (Pan/MS: 0.7/2.8m)
Resolution (Pan/MS 0.55/2.2m)

## Slide 8: KOMPSAT Images: Integrated Operations
KOMPSAT-5
2015/05/11
KOMPSAT-3
2014/02/07
KOMPSAT-3, EO
March, 2013
KOMPSAT-5, SAR
May, 2015

## Slide 9: KOMPSAT Images: Optical & SAR Sensors
KOMPSAT-3
Oct. 16th, 2013
KOMPSAT-5
Oct. 16th, 2013
Paris, France
Paris, France
Tour Eiffel

## Slide 10: KOMPSAT Images: Change Detections
KOMPSAT-3
Apr. 5, 2014
Google Maps
Tornado, Louisville Mississippi, USA

## Slide 11: ARD-Related Activities in KARI
We’ve only just begun!
Works in progress
  Review on ARD-related documents
    CEOS/LANDSAT/CQC Documents
  Check KARI’s status & readiness for ARD product generation
    Initial self-assessment on standard products of KOMPSAT-3 system
      Level 1R (radiometric corrected) & 1G (geometric corrected) product
      Using CARD4L-OSR self-assessment sheet
  Inspection & analysis on works to be done for ARD product generation
    Driving requirements & specification
    Checking additional process & processors
  Preparation for sample product generation

## Slide 12: Analysis on Works for ARD

## Slide 13: Classification of Works to Be Done (As of Aug. 2019)
Classification | Class | Functions needed | Description
Radiometric | Optical Surface Reflectance | 1-1) TOA Radiance Estimation | From DN of level 1R product DN->radiance conversion DN to radiance considering Gain/Offset
 |  | 1-2) Surface Radiance Estimation | Design of atmospheric correction module Selection of radiative transfer model
 |  | 1-3) Surface Reflectance Estimation | Considering solar irradiance
 | Land Surface Temperature | 2-1) TOA Temperature Estimation | From DN of level 1R product DN->temperature conversion DN to radiance considering Gain/Offset
 |  | 2-2) Surface Temperature Estimation | Design of atmospheric correction module Select of radiative transfer model Considering emissivity
 | Normalised Radar Backscatter | 3-1) SAR Backscatter Intensity Estimation | From DN of level 1D product
Geometric | All | 1-4) Tiling 2-3) Tiling 3-2) Tiling | Selection of map projection Design of grid structure Selection of resampling method

## Slide 14: Initial Self-Assessment (As of Aug. 2019, 1/3)
# | General Metadata | Threshold | Target
1.1 | Traceability | Not required | O
1.2 | Metadata Machine Readability | O | O
1.3 | Data Collection Time | O | X
1.4 | Geographical Area | O | X
1.5 | Coordinate Reference System | O | O
1.6 | Map Projection | O | O
1.7 | Geometric Correction Method | Not required | X
1.8 | Geometric Accuracy of the Data | Not required | X
1.9 | Instrument | O | O
1.10 | Spectral Bands | O | O
1.11 | Sensor Calibration | Not required | O
1.12 | Radiometric Accuracy | Not required | X
1.13 | Algorithms | X | X
1.14 | Ancillary Data | O | X
1.15 | Processing Chain Provenance | Not required | X
1.16 | Data Access | X | X
1.17 | Overall Data Quality | Not applicable | X
 | Total | 8/10 | 7/17

## Slide 15: Initial Self-Assessment (As of Aug. 2019, 2/3)
# | Per-pixel Metadata | Threshold | Target
2.1 | Metadata Machine Readability | O | O
2.2 | No Data | X | X
2.3 | Incomplete Testing | X | X
2.4 | Saturation | X | X
2.5 | Cloud | X | X
2.6 | Cloud Shadow | X | X
2.7 | Land/Water mask | Not required | X
2.8 | Snow/Ice mask | Not required | X
2.9 | Terrain Shadow Mask | Not required | X
2.10 | Terrain Occlusion | Not required | X
2.11 | Illumination and Viewing Geometry | O | X
2.12 | Aerosol Optical Depth Parameters | Not required | To be determined
 | Total | 2/7 | 1/11

## Slide 16: Initial Self-Assessment (As of Aug. 2019, 3/3)
# | Radiometric and Atmospheric Correction | Threshold | Target
3.1 | Measurement | X | X
3.2 | Measurement Uncertainty | X | X
3.3 | Measurement Normalization | Not required | X
3.4 | Directional Atmospheric Scattering | X | X
3.5 | Water Vapour Corrections | X | X
3.6 | Ozone Corrections | Not required | X
 | Total | 0/4 | 0/6
# | Geometric Correction | Threshold | Target
4.1 | Geometric Correction | X | X
 | Total | 0/1 | 0/1
Requirements | Self-Assessment
General Metadata | ∆
Per-Pixel Metadata | X
Radiometric and Atmospheric Corrections | ∆
Geometric Corrections | ∆

## Slide 17: Considerations & Questions
Items | Questions
General | Due to various objects and unwanted features (e.g. shadow, off-nadir pointing imaging) shown in high resolution imagery, we expect that it is difficult to estimate each object’s physical value (e.g. surface reflectance) even with coarse accuracy.
General Metadata | N/A
Per-Pixel Metadata | N/A
Radiometric and Atmospheric Corrections | N/A
Geometric Corrections | How to get the sub-pixel accuracy of PFS for high resolution imagery - Optic: 0.5 pixel (rRMSE), SAR: 0.2 pixel (rRMSE)

## Slide 18
Questions