## Slide 1: NSSC Update of EO Missions and CAL/VAL
Xiaolong DONG
National Space Science Center
Chinese Academy of Sciences
(NSSC,CAS)
Contributors:
Qifeng LU, NSMC/CMA
Qitao SONG, Wu ZHOU, NSOAS/SOA
Yunhua Zhang, MiRS/NSSC/CAS
CEOS WGCV-42
Sioux Falls, SD, USA
May 16-19, 2017

## Slide 2
Planning, Development, Management & Operation
of Space Science Missions
(2011~)
NSSC,CAS
National Space Science Center
Chinese Academy of Sciences
Research & Development of
Space Science and Applications （1958~)

## Slide 3
SPP on Space Science (I)
2011-2016
Hard X-ray Modulation Telescope (HXMT)
QUantum Experiments at Space Scale (QUESS)
DArk Matter Particle Explorer
(DAMPE)
ShiJian-10 (SJ-10)
Intensive Study of Future Space Science Missions
Advanced Research of Space Science Missions and Payloads
Strategic Priority Program on Space Science

## Slide 4: Update of NSSC: Space Science Missions
DAMPE
(2015.12)
QUESS
(2016.8)
Black Hole
Quantum
Experiment
Dark Matter
Particle Exploration
Mission
Objective
Microgravity / Life Science
HXMT
(2017.6)
SJ-10
(2016.4)

## Slide 5
SPP on Space Science (II)
2016-2022
Solar wind Magnetosphere Ionosphere Link Explorer (SMILE)
Einstein Probe (EP)
Advanced Solar Observatory in Space (ASO-S)
Water Cycle Observation Mission (WCOM)
Magnetosphere-Ionosphere-Thermosphere Coupling Constellation (MIT)
Advanced Research of Space Science Mission Concepts and Payload Technology
Intensive Study of Future Space Science Missions

## Slide 6
NSSC: Contributions to Oceanographic and Meteorological Satellites
Oceanography and Meteorology
  HY-2 (A, B, C and Follow-on): ALT+ACMR
  COSM: MICAP
  FY-3 and follow-on:
  MWHS/MWHTS(MWHS-II), GNOS
  space environment package
  CFOSAT: radar scatterometer
  FY-4 (optical and microwave):
  Microwave imager, space environment package

## Slide 7: Oceanographic Satellite of China 2016~ (by Q.Song, NSOAS/SOA)

## Slide 8
HY-2 update
HY-2A：in orbit >5yrs (2011.08.16)
  New version of ALT data
HY-2B/C：start satellite and payload
  DFRA: dual frequency radar altimeter：Ku (13.58GHz) & C (5.25GHz)
  ACMR: atmospheric correction microwave radiometer: 18.7，23.8，37GHz
  SCAT: radar scatterometer: Ku-band (RF switch network & receiver
  MWRA: microwave imager (6.6-37GHz): L1 data production
  Launch Plan:
    HY-2B: 2nd half of 2018
    HY-2C: 1st half of 2019 (inclined orbit)

## Slide 9
CFOSAT update
Payloads:
  SWIM: multiple beam radar for ocean surface wave spectrum (Ku band, by CNES)
  SCAT: rotating fan-beam scatterometer of ocean surface wind vector (ku band, by NSSC)
Schedule
  delivery of flight model: 2017.06-07
  Launch: 2018

## Slide 10
COSM update
Chinese Ocean Salinity Mission
Mission requirements:
– 0.1psu, 200km, monthly
– With Simultaneous observation of ocean surface roughness and SST
Schedule
– 2011~2014:grounddemonstration
on different payload technology
– 2015: mission definition, preliminary design, risk mitigation
– 2016: preparation and submission of mission proposal for approval
– Estimated launching: 2019~2020
2 payloads:
MICAP: microwave imager combined active passive (L, C, X, K band) (NSSC)
MiR2D: microwave 2-D interferometric imager (CAST-Xian)

## Slide 11
Meteorological Satellite of China 2016~
(by Q. Lu, NSMC/CMA)
National Program for Fengyun Meteorological Satellite from 2016-2021
LEO: AM+PM+Dawn Dusk; GEO: optical+microwave (under development)
2012FY-2F(Op)
2010FY-3B (R&D)
2013FY-3C(Op)
2016FY-3D(Op)
2014FY-2G(Op)
2017FY-2H(Op)
2018 FY-3E(Op)
2020FY-Rain(Op)
2018FY-4B (Op)
2019FY-3F(Op)
2020FY-4C(Op)
2016FY-4A (R&D)
2021 FY-3G(Op)
Up to 2021 there are 9 satellites planned to be launched
Notes: 11

## Slide 12
12
ok
Microwave
Temperature
Sounder (MWTS)
4 channel (~MSU)
13 channels
Microwave
Humidity
Sounder (MWHS)
5 channel (~MHS)
15channels with channels at
118 GHz
Infrared
Atmospheric Sounder
(IRAS)
20 channels
(~HIRS/3)
Microwave
Radiation Imager
10 channels
(~AMSR-E)
The FY-3A/B/C/D Instrument Suite
GNSS
Radio-Occultation
Sounder (GNOS)
(~GPS)
Notes: 12
12
12
12

## Slide 13
FY-3 update
FY-3A/B
  MWHS: Microwave humidity Sounder
  5 Channels: 150GHz: H, V-pol; 183GHz: 3channels for vapor
  FY-3A ended (launched 2008)
  FY-3B in good status (from 2010)
FY-3C/D
  MWHTS: Microwave Humidity and Temperature Sounders
  15Channels: 90GHz, 150GHz, 118GHz, 183GHz
  FY-3C: MWHTS in good status since 2013
  FY-3D: to be launched in September, 2017

## Slide 14
Tiangong -2 Interferometric Imaging Radar Altimeter (InIRA)
Calibration Activities (by Yunhua Zhang)
Calibration of 0 by Amazon Tropical Rain Forest.
Calibration of Antenna Pattern by Amazon Tropical Rain Forest.
Resolution and Height accuracy verified by Conner Reflectors.
Buoy calibration of sea surface height (SSH) measurement.

## Slide 15: Tiangong-2 WSRA Wide-Swath Radar Altimeter 2016.10

## Slide 16
Observation of Amzazon Tropical Rain Forest: Mean 0: -6.4500dB, Std 0: 0.2221dB,
Based on TRMM data.
Calibration of 0 by Amazon Tropical Rain Forest.

## Slide 17
Calibration of Antenna Pattern by Amazon Tropical Rain Forest.
Data 1: The measured boresight deviates 0.5º from the supposed boresight of installation.

## Slide 18
Calibration of Antenna Pattern by Amazon Tropical Rain Forest.
Data 2: The measured boresight deviates 0.5º from the supposed boresight of installation.

## Slide 19
索利蒙伊斯
亚马逊河
亚马逊河
雅瓦里河
秘鲁
巴西
巴西
哥伦比亚
索利蒙伊斯
亚马逊河
巴西, 秘鲁和哥伦比交界的亚马逊热带雨林地区, 图像大小: 79.3km x 33.6km, 图像中心经纬度: 西经 70.0533 南纬 4.2122,获取时间: 2016.09.23,10:56
Notes: 巴西, 秘鲁和哥伦比交界的亚马逊热带雨林地区, 图像大小: 79.3km x 33.6km, 图像中心经纬度: 西经 70.0533 南纬 4.2122,获取时间: 2016.09.23,10:56
20160923105609_000_0MC_ROM_1南美tg1_ampHR(-70.0533 -4.2122)

## Slide 20
Resolution and Height accuracy verified by Conner Reflectors —2 Square trihedrals of 2m and 5 Triangular trihedrals of 1.5m
Range resolution: 31.85m @  = 6.7º,
Azimuthal resolution: 32.98m.

## Slide 21
Resolution and Height accuracy verified by Conner Reflectors — 2 Square trihedrals of 2m and 5 Triangular trihedrals of 1.5m
（1）P11 Measured: Lonv = 109.56967593, Latv = 40.88254630，
Height = 1282.58596373m
Ground truth: Lonv = 109.56971520, Latv = 40.88229469， Height = 1284.31870000m
Error: Position = 28.31303714m, Height = -1.73273627m
（2）P10 Measured: Lonv = 109.56875000, Latv = 40.87976852, Height = 1281.12053632m
Ground truth: Lonv = 109.56888970, Latv = 40.87965754, Height = 1280.61470000m
Error: Position = 19.83679609m, Height = 0.50583632m
（3）P6 Measured: Lonv = 109.56791667, Latv = 40.87643519, Height = 1277.25688838m
Ground truth: Lonv = 109.56810350, Latv = 40.87627489, Height = 1276.68870000m
Error: Position = 27.37019857m, Height = 0.56818838m
（4）P7 Measured: Lonv = 109.56652778, Latv = 40.87365741, Height = 1272.83573639m
Ground truth: Lonv = 109.56672650, Latv = 40.87346279, Height = 1272.89070000m
Error: Position = 30.92525972m, Height = -0.05496361m
（5）P6 Measured: Lonv = 109.56652778, Latv = 40.86995370, Height = 1269.87419245m
Ground truth: Lonv = 109.56660090, Latv = 40.86971393, Height = 1269.64370000m
Error: Position = 27.87077518m, Height = 0.23049245m

## Slide 22
Buoy calibration of sea level measurement.
A
C
B
A (109.348,18.1356): -10.4m
B (109.2056,18.2484): -11.21m
C (109.2345,18.1012): -10.92m
Absolut error: about 0.3m.
Relative error: about 0.05m.