## Slide 1: Geoscience Australia Report on Cal/Val Activities
Medhavy Thankappan
Geoscience Australia
WGCV Plenary # 43
Sao Jose dos Campos, Brazil
April 10-13, 2018

## Slide 2: Digital Earth Australia
Australian digital infrastructure for analysis of Earth observations
Operational implementation of the Australian Geoscience Data Cube
Aims to streamline government business and support economic growth
Standardised, analysis ready data for innovative products / services
Australian Government funding of $15.3M over two years
Focus on calibration / validation to support the initiative (QA4EO, WGCV, LPV, GSICS)
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
http://www.ga.gov.au/about/projects/geographic/digital-earth-australia

## Slide 3
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Continental scale validation of surface reflectance
Continental scale validation of surface reflectance
Project Agreement with GA (16 Feb 2018), for CSIRO to coordinate field data collection
Two phases of field data acquisition, near-coincident with satellite overpass (L8,S2)
Good practice protocols for validation
Coordinated multi-temporal data acquisition by team members from multiple organisations

## Slide 4
National spectral data repository
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Proposal to establish a national spectral library for validation
Host field and reference spectral data obtained by spectroradiometers using SPECCHIO
Community based governance model with open access

## Slide 5
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Proposed validation system elements
Protocols and sampling strategy
1
Field sites for observing multiple variables (Supersites) and instruments
Upscaling
2
Field instrument calibration / cross calibration
Field / airborne measurements at different scales
3
4
Sampling strategy for field measurements
Scheme for airborne measurements
Validation system
Database sub-system
Scale transform sub-system
Accuracy evaluation sub-system
QA4EO protocols, best practice guidelines for EO validation
Validation campaigns
Coordinated ground airborne and satellite based data collection in line with sampling strategy and protocols

## Slide 6: Validation of Land Surface Brightness Temperature
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Planning validation of land SBT retrieved from Landsat data
Project agreement for validating SBT being developed with CSIRO
Initial phase of validation for three sites
Historical in situ thermal data (1998-2002) for validating corresponding epoch of Landsat derived SBT

## Slide 7: Interoperability of multi-source Analysis Ready Data
Sensitivity Analyses
Solar angle: BRDF normalized to 25, 45 (control) and 70 degrees.
Aerosol change: aerosol optical depth 0.05, 0.15, 0.25. 0.5 (control: best observed)
Water vapour: 0.5, 2, 3.5 (control: NCEP)
BRDF: temporal average (control: MODIS MCD43)
Temporal stability of ARD
Comparison with field data
Tools for ARD intercomparisons
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43

## Slide 8: Pandora spectrometers
Collaborative operation of two ESA Pandora spectrometers at Canberra and Alice Springs: Pandora #129 has been installed at Canberra and part of the Pandonia network
The second spectrometer is being prepared for deployment at Alice Springs
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Pandora #129 at Geoscience Australia, Canberra

## Slide 9: Corner Reflectors for SAR calibration
Surat Basin , Queensland - 40 CRs spread over 100km x 100km
Details of individual CR sites available from the Point and Distributed Targets Database maintained by the CEOS WGCV SAR Subgroup at http://sarcv.ceos.org/targets/target_group/4/
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43

## Slide 10: Sentinel-1 Geometric Cal/Val
40 permanently deployed corner reflectors in QLD
Research supporting routine S1 geometric cal/val under ESA “FRM4SAR” project (DLR, University of Zurich, TUM, GA)
Consistent results from independent ALE analysis of S1 data over CR
Compared S1 IWS data and TDX ScanSAR data for the CR array(next slide)
Image courtesy C. Gisinger, TUM
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43

## Slide 11
Sentinel-1 / TanDEM-X Absolute Location Error with and w/o correction for CR apex coordinates
Images courtesy C. Gisinger, TUM/DLR
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Sentinel-1A IWS
TanDEM-X ScanSAR

## Slide 12: New activity supporting SAR calibration
Based on the modelling work with CR apex coordinates, re-surveying of CRs to get apex coordinates will begin next month
Two new 1.5 m corner reflectors are being installed at the Yarragadee geodetic observatory in Western Australia, to co-locate multiple geodetic techniques - VLBI, GPS, SLR, DORIS (cf Metsahovi, Wettzell)
DLR have expressed an interest in regular monitoring of the two new CR to perform geometric calibration of TerraSAR-X
Ongoing discussion with NASA-JPL for supporting NISAR calibration
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43

## Slide 13
Open Data Cube
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43
Initiated though a CEOS Data Cube meeting in Canberra in February 2017
Building off active collaborations between GA, CSIRO, NCI, USGS, NASA and CEOS
The foundation of Project participation is openness and transparency
Software developed using tools like github, released under open source license to support local regional national and international capabilities
The community governs itself through:
    a Steering Council made up of active contributors (i.e. individuals, not institutions)
    engagement in public forums to discuss and debate the direction of the Project
2nd Open Data Cube Conference hosted by GA and CSIRO in Feb 2018

## Slide 14: Satellite Altimeter Cal/Val: Bass Strait, Australia
The Bass Strait calibration and validation facility has provided a sustained contribution to satellite altimetry mission science teams for over 25 years.
Primary focus is the ‘Jason-series’ sea level reference missions. Recently added in situ observations in support of the Sentinel-3 missions.
In situ instrumentation includes numerous moored oceanographic instruments at various
comparison points (CPs), high resolution regional ocean modelling, and GNSS equipped buoys.
We are developing the capability to undertake calibration and validation of the game changing SWOT interferometric mission set to launch in 2021.
STLY
(GPS)
RKCP
(GPS)
(JAS)
TOPEX / Poseidon
Aug 1992 -
Jason-1
Dec 2001 -
OSTM/Jason-2
June 2008 -
Jason-3
Jan 2016 -
Sentinel-3A
Feb 2016 -
Sentinel-3B
Launching
25 Apr 2018 -
Effort shifting towards understanding improved noise characteristics of SAR altimeter data in preparation for SWOT in 2021.
Sustained cal/val continues to be essential.

## Slide 15: Thank you
medhavy.thankappan@ga.gov.au
Geoscience Australia
Report on Cal/Val Activities WGCV Plenary # 43