## Slide 1: Sentinel-5p Mission Performance Centre Operational Validation Facility
  J.-C. Lambert, B. Langerock, S. Compernolle, Y. Geunes, J. Granville, D. Hubert,
  A. Keppens, O. Rasson, and T. Verhoelst / BIRA-IASB, Brussels, BE
  S. Niemeijer and B. Rino / s[&]t, Delft, NL
  A. Dehn (ESA), K.-U. Eichmann (IUP-UB), G. Jaross (NASA/GSFC), M. Sneep (KNMI), T. Wagner (MPI-C), C. Zehner (ESA)
  + many others from BIRA-IASB, DLR, ESA, IUP-UB, KNMI, MPI-C, NILU, RAL, SRON

## Slide 2: S5P operational data production since July 13 This talk: 1. S5P TROPOMI Validation Plan 2. Automated Validation Facility - Architecture - Data streams - Output 3. Initial validation results 4. Conclusion

## Slide 5: S5P Mission Performance Centre - Validation
S5P Mission Performance Centre (MPC) to provide operational validation service during Copernicus S5P Routine Operation Phase
Human based
 MPC VAL Team
Validation-based monitoring of L2 products health
Generation of quarterly consolidated validation reports
Generation of quality info articles on validation website
Validation support to Level-1-to-2 algorithm QA & evolution
Machine based  VDAF
Automated, routine comparison of S5P data vs. FRMs
Generation of S5P validation database for MPC Teams
Automated generation of on-line quick-look reports

## Slide 6: S5P MPC Validation Data Analysis Facility (VDAF) System Architecture
FRMs + Other Validation Data

## Slide 7: S5P VDAF S5P TROPOMI and Validation Data Streams
FRMs + Other Validation Data

## Slide 8: S5P L2 Product Requirements
Sentinel-5 Precursor Cal/Val Plan for Operational Phase - ESA-EOPG-CSCOP-PL-0073 (11/2017)

## Slide 9: Validation Data Streams into S5P VDAF
Tropospheric Ozone LIDAR Network
ID | S5P Data Product | Validation Measurements
A | O3 total column | Brewer, Dobson, ZSL-DOAS, MAX-DOAS, Pandonia
B | O3 profile (incl. troposphere) | ozonesonde, stratospheric DIAL, tropospheric DIAL
C | O3 tropospheric column | ozonesonde
D | NO2 stratospheric column | ZSL-DOAS
 | NO2 tropospheric column | MAX-DOAS
 | NO2 total column | Pandonia (PGN)
E | SO2 total column | Pandonia (PGN)
F | HCHO total column | MAX-DOAS, Pandonia
G | CO total column | TCCON FTIR (NIR), NDACC FTIR (MIR)
H | CH4 total column | TCCON FTIR (NIR), NDACC FTIR (MIR)
I | Cloud Fraction | not available
 | Cloud Height (pressure) | Cloudnet lidar/radar
 | Cloud Optical Thickness | not available
J | Aerosol Absorbing Index | not available
 | Aerosol Layer Height | EARLINET aerosol lidar
ESA FRM programme + WMO GAW contributing networks

## Slide 10: Status of Validation Data Streams into VDAF O3 column data from NDACC and WMO GAW (WOUDC)

## Slide 11: Status of Validation Data Streams into VDAF CO column (FTIR) from NDACC and TCCON
Faster delivery organised through CAMS-27/84
Waiting for future ESA FRM4GHG data streams
NDACC and TCCON
standard archiving rate < 1-2 years

## Slide 12: S5P Data Streams into MPC VDAF
Overpass data extractor in S5P PDGS
Generic approach, specific parameters
Optimization of data volumes !
AMT 2015

## Slide 13: S5P MPC Validation Data Analysis Facility (VDAF) Core System
FRMs + Other Validation Data

## Slide 14: State-of-the-Art Validation Chain, Co-locators, Comparators…
Cross GEOSS
EO Cal/Val
Prototyping ESA Multi-TASTE and CCI_Ozone
Community feedback / endorsement
Implemention in FP7 QA4ECV-AVS, H2020 GAIA-CLIM, C3S_312a#ozone,
S5P MPC/VDAF, CAMS-84/27, CCI+
cci
ozone
ACC-8/…/11
WGCV-28/…/31

## Slide 15: Data Handling, Co-location and Comparison Toolset
https://cdn.rawgit.com/stcorp/harp/master/doc/html/index.html
harp documentation
HARP

## Slide 16: S5P VDAF MPC dedicated Automated Validation Server and Public Validation Website
Synergies with similar developments for
AC-SAF, QA4ECV and CAMS-84/27
FRMs + Other Validation Data

## Slide 17: S5P VDAF Automated Validation Server

## Slide 18: S5P MPC L2 Validation Planning
Launch
13 OCT 2017
COPERNICUS, PUBLIC SERVICES, POLICY MAKING
AIR QUALITY, CLIMATE, OZONE, UV RESEARCH
Prototype
Validation
OCT 2018
ALH UV
Validation
Prototype
Validation
Prototype
Prototype
O3 NO2 CO AAI CLOUD
JUL 2018
Lot #1
SEP 2018
HCHO SO2 O3-TRC
Lot #2
Lot #4
DEC 2018
CO CH4
Lot #3
Provisional planning for S5P L2 products public release
O3P
Lot #5
COMMISSIONING PHASE RAMP-UP
…
WGCV-44

## Slide 19: First release of S5P Ozone column data Initial validation w.r.t. NDACC DOAS/SAOZ, MAX-DOAS and Pandora qa_value > 0.75 (without clouds) / qa_value > 0.5 (including clouds and snow/ice)

## Slide 20
Courtesy T. Verhoelst, BIRA-IASB

## Slide 21
2-sigma combined ex-ante uncertainty
Courtesy T. Verhoelst, BIRA-IASB

## Slide 22: First release of S5P NO2 column data Initial validation w.r.t. NDACC DOAS/SAOZ, MAX-DOAS and Pandora qa_value > 0.75 (without clouds) / qa_value > 0.5 (including clouds and snow/ice)

## Slide 23: First release of S5P NO2 column data Initial validation w.r.t. NDACC DOAS/SAOZ, MAX-DOAS and Pandora qa_value > 0.75 (without clouds) / qa_value > 0.5 (including clouds and snow/ice)

## Slide 24: First release of S5P CO column data w.r.t. TCCON qa_value > 0.5 / cloud OD < 0.5 / cloud height < 5000 m
NYALESUND
SODANKYLA
EASTTROUTLAKE
BIALYSTOCK
ZUGSPITZE
BREMEN
PARKFALLS
LAMONT
JPL
Courtesy M. Kumar Sha, BIRA-IASB, AO Project TCCON4S5P
REUNION
LAUDER
DARWIN
ASCENSION
BURGOS
PASADENA
SAGA

## Slide 25: First release of S5P Carbon Monoxide column data Initial validation w.r.t. TCCON and NDACC
Courtesy M. Kumar Sha, BIRA-IASB, AO Project TCCON4S5P

## Slide 26: First release of S5P Carbon Monoxide column data Stripes in L2_CO
From S5P CO Product Readme File, July 2018

## Slide 27: S5P MPC Validation Website

## Slide 28
Where to find S5P Product Details and Quality Information
Product Readme File
PRF
All available on http://sentinels.copernicus.eu and http://www.tropomi.eu
Product User Manual Algorithm Theroretical Basis
PUM ATBD

## Slide 29: Conclusion (1/2)
S5P MPC operates an Automated Validation Server built upon heritage validation systems (long-term support from BELSPO, EC, ESA, EUMETSAT, ECMWF)
VDAF-AVS = core of S5P MPC routine validation service
    implemented in MPC environment, dependent on external data streams
    initially Envisat products, now expanding to all S5P products (UV to SWIR)
    tailored to S5P and Copernicus needs
    developed in synergy with other Copernicus elements
Started on July 13, 2018, routine validation service with first release of S5P data, incl. continuous survey of L2 health and quarterly consolidated validation reporting

## Slide 30: Conclusion (2/2)
Approach combining MPC VAL and S5PVT AO activities successful
Valuable synergies between Copernicus space, CAMS/C3S data procurement and CAMS/C3S service components
Underlying systems (e.g. Multi-TASTE) are mature, however, ad hoc support required for:
  operationalization of scientific validation systems
  service set-up
  tools and methods for new validation paradigms and challenges
  harmonization of uncertainties, closure of comparison error budget…
  FRM/validation data availability (and timeliness)
Automated or not, EO (L1/L2/L3/L4) data validation always requires substantial interpretation by (human) scientific experts.

## Slide 31: Thank you !