## Slide 1: AEROSPAN
Australia’s contribution to AERONET
CSIRO Centre for earth observation
Dr Ian C Lau| Senior Experimental Scientist – Mineral Resources
16th July 2019

## Slide 2: AEROSPAN (Aerosol characterisation via Sun Photometry: Australian Network)
Formerly Aerosol Ground Station Network (AGSNet), setup by Ross Mitchell and Susan Campbell.
Australia’s contribution to AERONET
First site: Tinga Tingana in April 1998
Recent site: Tumbarumba July 2019

## Slide 3: Current sites: 7+1+1
Jabiru, NT (2000- 14.2 years)
Lake Argyle, WA (2002- 13.99 years)
Birdsville, QLD (2005-)
Lucinda, QLD (2009-2010, 2013-)
Fowlers Gap, NSW (2013-
Lake Lefroy, WA (2012-
Learmonth, WA (2017-
Tumbarumba, NSW (2019-
Past sites:
Tinga Tingana (1998-2012)
Canberra, ACT (2003-2017)
Future sites:
Pinnacles, WA (12 band BRDF instrument, may not be on/suitable for AERONET)

## Slide 4: Site Locations
Jabiru
Lucinda
(Canberra)
Tumbarumba
Aspendale
(testing)
Lake Argyle
Birdsville
(Tinga Tingana)
Fowlers Gap
Lake
Lefroy
Learmonth
(Pinnacles)

## Slide 5: Lake Lefroy
Salt lake and clay pans
Mining operations (gold)
5km

## Slide 6: Pinnacles
Bare sand dunes surrounded by
coastal ‘kwongan’ vegetation
2km
200 km

## Slide 7: Operations
Aspendale (VIC)
  Equipment maintenance, testing and development
  Central sites
  Data download and data management
Townsville (QLD):
  Lucinda site maintenance
Perth (WA):
  Western Australian sites and Tumbarumba, NSW

## Slide 8: Aims
High level of instrument maintenance
Continuous measurement at all sites >360 days a year (yearly swap outs) providing high quality data
Uploads weekly (or fortnightly) to GSFC

## Slide 9: Legacy
CSIRO-built logger for acquiring extra instrumentation
Weekly downloads
Satellite modems at 4 sites, which could be reduced to 2 due to recent improvements in cellular coverage.
Sites located in areas of significance for research into continental aerosol monitoring
Logger
3G modem
Older-style CIMEL
control box
Custom wiring

## Slide 10: Persistent obstacles
Aging instrument pool, need for renewal to replace older instruments.
CSIRO-loggers nearing retirement, no longer need extra measurements (nephelometers).
Small staffing %
Cost of ongoing maintenance, including fieldwork and development.
Cost of data downloads and multiple cellular connections
Science output and external revenue pressures

## Slide 11: Future focus
Shift towards remote sensing and optical satellite cal/val after loss of aerosol scientist PI.
Rationalise sites to ones of significance for cal/val and easy access.
  Lake Argyle – TIR/dark target
  Lake Lefroy – Bright VNIR target
  Tumbarumba – dark/veg target
  Pinnacles – instrumented calibration site* (may not be suitable with BRDF instrument alone, may require second ‘standard’ CIMEL Sun photometer)
Replacement and/or upgrade of older CE-318-N photometer heads and control boxes to CE-318-T.
->Upgrade of communications.
->Automated daily uploads

## Slide 12
CSIRO Mineral Resources
  Ian C Lau Senior Technical Scientist
    t +61 8 6436 8646
    e Ian.Lau@csiro.au
    w www.csiro.au/lorem
CSIRO Oceans and Atmosphere
  David Barker Technician
    t +61 2 9123 4567
    e David.barker@csiro.au
    w www.csiro.au/
CSIRO Centre for earth observation