## Slide 1: Surface Reflectance Validation [CV-17]
Medhavy Thankappan
Team: Guy Byrne, Andrew Walsh, Mark Broomhall, Tim Malthus, Cindy Ong, Ian Lau, Peter Fearns + many others

## Slide 2
Team members and reviewers
Janet Anstee
Hannalie Botha
Anjea Byrne
Mike Caccetta
Alicia Caruso
Laurie Chisholm
Ken Clarke
Neil Sims
Kylie Smith
Liam Stephen
Lola Suarez
Dan Tindall
Lan-Wei Wang
Claire Fisk
Erin Kenna
Fuqin Li
Stefan Maier
Glenn Newnham
Simon Oliver
Peter Scarth
Dennis Helder
Chris Maclellan
Kurt Thome
Stuart Phinn
Andreas Hueni
David Jupp

## Slide 3
Project Background
Field data collection for continental scale validation of surface reflectance
Coordinated by CSIRO under a Project Agreement, funded through Digital Earth Australia (DEA)
Field data acquisition, near-coincident with satellite overpass (L8, S2a, S2b), from March 2018 to June 2019 – Phase 1
Phase 2 to cover more complex sites
Field based validation using best practice protocols seen as critical to ensure generation of consistent multi-sensor SR products
Reliability, consistency of downstream products, user confidence and uptake

## Slide 4
Surface types
‘mostly’ flat
bare or low vegetation
homogeneous
spectrally diverse
Phase 1 Surface Reflectance Validation Sites

## Slide 5
All instruments / panels were characterised by CSIRO
100x100m sites
6 transects in each site oriented on the solar azimuth
Atmospheric readings coincident with overpass using either MicroTops or ASD
Transects bookended by panel readings
SR field validation protocols documented
Field Sampling Protocols

## Slide 6
55 individual overpasses, multiple dual overpasses, and trial UAS acquisition.
Weather, site proximity, trafficability, equipment and staffing impacted on number of actual opportunities to deploy.
Work on characterising measurement uncertainty in progress, final report ready
Total field data acquisitions at all sites
Phase 1 Field Data Collection Status

## Slide 7
Coincident measurements with two ASDs
GA ASD
GA ASD
CSIRO ASD
CSIRO ASD
Coincident measurements with two instruments at Pinnacles site
Landsat 8 overpass on 20 May 2018
Sentinel-2A overpass on 22 May 2018

## Slide 8
Pinnacles 2 April 2018
L. Lefroy 25 June 2018
Dookie 2 June 2018
Validation for L8 and S2 Tandem Overpasses
Dookie 2 June 2018
Longreach 23 June 2018
Mullion 10 April 2019

## Slide 9
Dookie 2 Jun 18
Dookie 14 Mar 18
Longreach 23 Jun 18
Longreach 29 May 18
Lake George 12 Feb 18
Lake George 3 May18
Mullion 29 Dec 18
Mullion 10 Apr 19
Pinnacles 2 Apr 18
Temporal measurements for Landsat 8
Pinnacles 20 May 18
Winton 21 Jun 18
Winton 20 Oct 18

## Slide 10
Dookie 14 Mar 18
Dookie 18 Apr 18
Dookie 2 Jun 18
Fowlers Gap 21 Jun 18
Fowlers Gap 18 Dec 18
Temporal measurements for Sentinel-2
Longreach 9 May 18
Longreach 9 May 18
Longreach 23 Jun 18
Lake George 4 Jul 18
Mullion 8 Apr 19
Pinnacles 2 Apr 18
Pinnacles 22 May 18
Pinnacles 28 Nov 18
Winton27 May 18
Winton21 Jun 18
Winton 19 Oct 18
Lake George 5 Apr 18
Mullion 10 Apr 19
Mullion 29 Dec 18
Lake George 17 Sep 18

## Slide 11
Site overview (Litchfield, NT)
Measuring direct irradiance
Pre-flight reference panel measurement
Miniature Spectrometer
Drone Based Validation at Litchfield
Drone based spectral data collection trial over Litchfield site, synchronous with a Sentinel-2A overpass

## Slide 12
Sentinel-2B
Landsat-8
Sentinel-2A
Field Validation Summary Results

## Slide 13
Sensitivity Analyses for SR
Mean surface reflectance at different aerosol values
Mean surface reflectance at different values of solar angle normalisation
Mean surface reflectance at different water vapour values
Parameters | Low | Medium | High
Aerosol optical depth | 0.05 | 0.25 | 0.50
Water vapor (g/cm2) | 0.5 | 1.5 | 3.5
Solar angle | 25 | 45 | 70
BRDF | low | medium | high
Mean surface reflectance at different BRDF levels

## Slide 14: Phase 2 Validation of SR
Scoping for Phase 2 has begun, use of instrumented sites and automation for data over complex sites; will explore cross-over with new LPV, IVOS initiatives
Staff training to fly UAS completed; UAS platform and payload acquired
Validation sites being determined

## Slide 15
Summary
Ongoing field based validation is critical to ensure consistency in generation of SR products from multiple sensors
Protocols developed for continental-scale field validation of SR in Phase 1, could be adapted for developing global protocols
Sensitivity analyses highlight the relative importance of parameters used for generating SR, and their impacts
Planning for Phase 2 SR validation is underway, synergies with new LPV, IVOS initiatives will be explored for collaboration