## Slide 1: JAXA Agency Report
Committee on Earth Observation Satellites
Akihiko KUZE
(Earth Observation Research Center, Japan Aerospace Exploration Agency)
CEOS WGCV
CSIRO Perth
July 17, 2019

## Slide 2
2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Japanese Fiscal Year
ALOS-2/PALSAR-2
ALOS-4 (SAR)
ALOS-3
(Optical)
GPM/DPR
GCOM-W/AMSR-2
Climate
Change
Water Cycle
Precipitation
Vegetation,
Aerosol
GCOM-C/SGLI
EarthCARE/CPR
Clouds
AMSR-2’s Successor Sensor onboard GOSAT-3
Greenhouse
Gases
GOSAT/FTS
GOSAT-2/FTS-2
GOSAT-3 (tentative name)
ALOS-4 Follow-on
ALOS-3 Follow-on
Land Monitoring
National Security
Disaster
JAXA’s Earth Observation Schedule

## Slide 3
Surface | Upper-air | Composition
Air temperature | Temperature | Carbon dioxide
Wind speed & direction | Wind speed & direction | Methane
Water vapour | Water vapour | & other long-lived GHGs *
Pressure | Cloud properties | Ozone & Aerosol
Precipitation | Earth radiation budget (including solar irradiance) | supported by their precursors **
Surface radiation budget |  | 
River discharge
Water use
Groundwater
Lakes
Snow cover
Glaciers and ice caps
Ice sheets
Permafrost
Albedo
Land cover (including vegetation type
Fraction of absorbed photosynthetically active radiation (FAPR)
Leaf area index (LAI)
Above-ground biomass
Soil carbon
Fire disturbance
Soil moisture
Atmospheric
Terrestrial
Surface | Sub-surface
Sea-surface temperature | Temperature
Sea-surface salinity | Salinity
Sea level | Current
Sea state | Nutrients
Sea ice | 
Surface current | 
Ocean colour | 
CO2 partial pressure | CO2 partial pressure
Ocean acidity | Ocean acidity
Phytoplankton | 
 | Oxygen
 | Tracers
Oceanic
Total Essential Climate Variables (ECVs) (ECVs largely dependent on satellite observations identified by CEOS and GCOS are shown in bold.) | 50
ECVs measured by GCOM-C&W, GPM/DPR and GOSAT | 23
* including N2O, CFCs, HCFCs, SF6, PFCs
** in particular NO2, SO2, HCHO, CO
Essential Climate Variables measured
by GCOM-C & W, GPM/DPR, GOSAT
Measured by GCOM-C
Measured by GCOM-W
Measured by GOSAT
Measured by GPM/DPR
Climate Change
3

## Slide 4
GCOM-C/SGLI
Global Change Observation Mission – Climate (GCOM-C),
Second-generation Global Imager (SGLI)
GCOM-C SGLI characteristics | 
Launch Date | 23 Dec. 2017
Weight | 2,000kg
Orbit | Sun-synchronous (descending local time: 10:30), Altitude: 798km, Inclination: 98.6deg
Mission Life | 5 years (3 satellites; total 13 years)
Scan | Push-broom electric scan (VNR) Wisk-broom mechanical scan (IRS)
Scan width | 1150km cross track (VNR: NP & POL) 1400km cross track (IRS: SWIR & TIR)
Spatial resolution | 250m (land and coast), 500m (TIR), 1km
Polarization | 3 polarization angles for POL
Along track tilt | Nadir for VN, SW and TIR, & +/-45 deg for POL
An example of SGLI/VNR daily coverage (5 Jan2018)
Visible and Near-infrared Radiometer (VNR)
InfraRed Scanner (IRS)
All standard products (Level-1, 2, and 3) have been open to the public via JAXA data portal, “G-Portal” (GUI data search and direct FTP are available; https://gportal.jaxa.jp/gpr/)
4

## Slide 5
Wavelength nm | 380 | 412 | 443 | 490 | 530 | 670 | 763 | 865 | 1050 | 1630 | 2200
RadCalNet(in)+Pstar4 | 0.982 | 1.023 | 0.997 | 1.010 | 1.041 | 1.000 | NA | 1.008 | 1.050 | 1.007 | 1.028
In-situ surface reflectance
In-situ
AOT, 
Simulated TOA reflectance
SGLI TOA reflectance
comparison
Radiative transfer
(Pstar4)
RadCalNet
Gobabeb, RRV, LCFR* (* can be influenced by the small structures)
Samples from Jan 2018 to May 2019
SGLI vical by RadCalNet
(Gobabeb, LCFR, RRV)
5

## Slide 6: Global Change Observation Mission - Water "SHIZUKU" (GCOM-W)
Successor of Aqua/AMSR-E (launched in May 2002), providing continuous data for climate studies and operational applications
Joining A-train constellation and also GPM constellation
Carrying AMSR2, a multi-polarization and multi-frequency microwave imager
Observing various water-related ECVs over atmosphere, land, ocean and cryosphere in high spatial resolution
Improving on-board calibration target has resulted reduction of annual TB variation due to calibration and improvement of TB stability
Achieved designed mission life (5-year) on May 18, 2017, and continues observation.
AMSR2 follow-on (AMSR3) has been in Pre-project phase (Phase A) since Sep. 2018.
AMSR2 Products | 
STD | Brightness Temperature
 | Total Precipitable Water (over Ocean)
 | Total Cloud Liquid Water Content
 | Precipitation
 | Sea Surface Temperature
 | Sea Surface Wind Speed
 | Sea Ice Concentration
 | Snow Depth
 | Soil Moisture Content
RES | All-weather Sea Surface Wind Speed
 | 10-GHz Sea Surface Temperature
 | Land Surface Temperature
 | Thin Ice Detection
 | Total Precipitable Water over Land
6

## Slide 7
Decade-long Observation by GOSAT
10th anniversary on Jan. 23, 2018
7
Global CO2 density
https://data2.gosat.nies.go.jp/gallery/fts_l3_swir_co2_gallery_en.html
Toward 20-year operation
enough fuel for another decade operation
no significant degradation in classic four NiCd batteries.
Radiance degradation and TIR non-linearity correction tables for 20-year operation are ready in new Level V220. (assuming very slow degradation in 0.76 µm and no degradation in 1.6 and 2.0 µm.

## Slide 8: GOSAT (2009-) new products Partial column density using both SWIR and TIR
http://www.eorc.jaxa.jp/GOSAT/CO2_moitor/index.html
8
Local Emission
GOSAT measures both solar reflected light from the Earth’s surface (SWIR) and thermal emission from the Earth’s atmosphere (TIR) providing CO2 partial-column densities of UT and LT.
Upper Troposphere (UT)
Lower Troposphere (LT)
AJAXA vertical profile vs. 4 GOSAT retrieval at RRV, NV
Coutesy of R. Kawa
Needs more validation data of vertical CO2 and CH4

## Slide 9: Greenhouse gases Observing SATellite-2 “IBUKI-2” (GOSAT-2) (2018-)
TANSO-CAI-2 first light
(Nov. 5)
Iran
Dubai
Pakistan
GOSAT-2 CAI-2-forward
Arabian Sea
GOSAT-2 CAI-2-Backward
GOSAT CAI Nadir
GOSA-2 launch on Oct. 29, 2018
TANSO-FTS-2
Adding Carbon Monoxide (CO) measurement to identify CO2 enhancement by combustion
Wider pointing angles
Fully customized observation pattern
Cloud avoiding pointing
Dec. 13, Nagoya
CH4
CH4
CH4
CO2
CO2
CO2
CO
O2
TANSO-CAI-2 (1) 10 bands
(2) Multi-viewing capability improved aerosol detection
TANSO-FTS-2 first spectra Dec. 13, 2018 Nagoya
9

## Slide 10: ALOS-2 “Daichi-2”
Mission sensor | PALSAR-2 (Phased Array type L-band Synthetic Aperture Radar 2)
Launch | May 24, 2014 H-IIA launch vehicle FY24
Mass | 2.1 tons
Lifetime | 5 years (target: 7 years)
Orbit | Sun-synchronous, 628 km altitude, 14 days revisit, Orbit control: ≦ +/- 500 m
Local sun time | 12:00±15 min (descending) 24:00±15 min (ascending)
Mission data transmission | X-band: 800 Mbps (16 QAM), 200/400 Mbps (QPSK)
PALSAR-2
(Phased Array type L-band Synthetic Aperture Radar 2)
Mission objectives:
Disaster monitoring (Earthquake, Volcano, Landslide, Flooding, …)
Environmental monitoring (Forest, Ice sheet, …)
Agriculture, natural resources, and ocean
Technology development
PALSAR-2 antenna
X-band downlink antenna
Solar Arrays
X
Y
Z
The compact infrared camera (CIRC) and SPAISE2 for detecting ships are carried as a technology demonstration payload.
10

## Slide 11
ALOS-2 Mission Operation
JFY2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Launch
Initial C/O
Initial Cal-Val
Product release
Mission operation (5 years)
Post-mission operation
ALOS-3
(Optical)
May 24, 2014
ALOS-2
(L-SAR)
ALOS-4
(L-SAR)
Development
Development
Nominal Operation Review Meeting
11

## Slide 12
Items | Results | 
Geometry (RMSE) | [Stripmap and Spotlight] 6.38 m (L1.1) / 6.73 m (L2.1) [ScanSAR] 60.77 m (L1.1) / 29.33 m (L2.1) | 
Radiometry | RCS accuracy (1σ) | 0.57 dB (corner reflectors) 0.41 dB (Amazonian forests)
Polarimetry | VV-HH amplitude ratio | 1.000 (σ=0.012)
 | VV-HH phase difference | 0.137 deg (σ=4.42)
 | Cross talk | [HV/HH] -41.90 dB (σ=5.264) [VH/VV] -41.56 dB (σ=4.953)
Calibration summary as of August 2018.
> PALSAR-2 keeps good conditions and performances.
On-board internal calibration is performed every 3 months.
Product quality of major observation modes is evaluating regularly using SAR data over calibration sites.
The standard product processing software was updated on June 2018 (radiometric calibration) and on Nov. 2018 (correction of range offset).
PALSAR-2 Calibration Summary
12

## Slide 13: PALSAR-2 Radiometric Calibration
13
Digital number of PALSAR-2 product can be converted to sigma-zero value by using the following equation.
The Calibration Factor (CF) in the equation is evaluated by measuring CRs.
DN: digital number
CF = -83 dB
A = 32 dB
Time trend of radiometric accuracy.
Ave.= -82.96 dB, RMSE = 0.57 dB
No. = 248 CRs
Corner Cube reflector in Gotenba-city
13

## Slide 14
PALSAR-2 Geometric Calibration
Ionosphere effects on geometric accuracy.
N=180
Geometric error in slant range (m).
Range difference estimated by TEC (m)
Time series in global average TEC.
PALSAR
PALSAR-2
Time trend of geometric accuracy (SM mode).
Mode | Beam | dx (EW direction) |  |  | dy (NS direction) |  |  | No.
 |  | Ave. (m) | STDEV (m) | RMSE (m) | Ave. (m) | STDEV (m) | RMSE (m) | 
Spotlight | - | -5.423 | 4.278 | 7.140 | 2.540 | 2.439 | 3.622 | 10
SM 3m | U2-6～U3-14 | -0.546 | 3.636 | 3.677 | -0.926 | 4.053 | 4.159 | 141
SM 6m | FP6-3～7 | -4.310 | 3.495 | 5.569 | 3.667 | 1.743 | 4.080 | 83
SM 10m | F2-5～7 | -4.201 | 3.151 | 5.279 | -0.995 | 2.793 | 2.968 | 60
ScanSAR | W2 | -7.977 | 7.864 | 10.987 | 4.838 | 4.757 | 6.656 | 13
Geometric error
in EW direction.
Geometric accuracy is evaluated at the point targets i.e. CRs, ARCs, GCs.
● Asc.
● Desc.
(b) Geometric error
in NS direction
14

## Slide 15
Continuity of the GPM/DPR and the TRMM/PR
Both GPM/DPR’s calibration factors and TRMM/PR’s calibration factors were changed in 2017.
After the algorithm update in Oct. 2018, the GPM/KuPR V06 and the TRMM/PR V8(GPM TRMM V06) show better continuity on surface precipitation rate.
KuPR V6
KuPR V5
PR V7
PR V8
Over-land surface precipitation rates averaged in 35S-35N.
KuPR V6
KuPR V5
PR V7
PR V8
Over-ocean surface precipitation rates averaged in 35S-35N.
15

## Slide 16
Future JAXA Earth Observation Satellites
AMSR3 additional higher frequency channels of 166 & 183 GHz for snowfall retrievals)
New products: TPW over land, high-resolution SST, all-weather sea surface wind speed & high-resolution sea ice concentration
GOSAT-3: GHG + NO2, Global coverage and targeting anthropogenic emission sauces with high spatial resolution imaging capability
16

## Slide 17: IGARSS 2019 Yokohama
17
See you again in 10 days!