## Slide 1: JAXA Agency Report
Keiji Imaoka
Japan Aerospace Exploration Agency (JAXA)
CGMS-CEOS Joint Working Group on Climate
Darmstadt, Germany
March 5, 2014

## Slide 2: JAXA Satellite Programs
Late 1990s
2000s
2003 (JAXA established)
ADEOS
TRMM/PR
GCOM-W
GPM/DPR
GCOM-C
EarthCARE/ CPR
ADEOS-Ⅱ
Earth Observation
Global Warming
Aqua/
AMSR-E
Land Use
GOSAT
Disaster
Monitoring
ALOS-2
ALOS
Communications
COMETS
DRTS
WINDS
Technology
Development
ETS-Ⅵ
ETS-Ⅶ
ETS-Ⅷ
OICETS
Positioning
QZSS
Climate Change/Water
2
Next Gene.
(optical)
GOSAT-2
Notes: As you may know, Advanced Land Observing Satellite, ALOS was launched successfully on January 24th in 2006, and renamed Daichi.
Calibration and Validation were done in the following months after the launch, and its regular operation started on October 24.
ALOS is a follow-on satellite to the Japanese Earth Resources Satellite-I, JERS-I and the first Advanced Earth-Observing Satellite, ADEOS, with significantly enhanced land-observation capability and technology.
ALOS has three remote-sensing instruments, PRISM, PALSAR and AVNIR-2 that enable precise land-coverage observation.
It will be used for disaster monitoring, cartography, and regional observation and resource surveying, and will address global warming.

## Slide 3
3
GPM Core Observatory was successfully launched on February 28, 2014 (JST)
Notes: GPM core observatory is nearly ready for launch at the Tanegashima Space Center in Japan. The satellite was transported by a large aircraft from the United States, shipped via sea to the Tanegashima Island, and transported to the Tanegashima Space Center by land. This is the photo of the GPM core observatory with two project managers from NASA and JAXA. The large and small rectangular boxes are Ku- and Ka-band radar, respectively.

## Slide 4
International mission for high accurate / frequent global precipitation observation.
  Core Observatory: developed under NASA and JAXA equal partnership.
  Constellation Satellites: utilization of international partners’ satellites with precipitation measurement capability.
Dual-frequency Precipitation Radar (DPR)
  Developed by JAXA and National Institute of Information and Communications Technology （NICT）
  DPR is composed of KuPR and KaPR
GPM Core Observatory will be launched on February 27th 2014 (UTC).
KuPR: 13.6GHz radar (phased array)
KaPR: 35.5GHz radar (phased array)
GMI (Microwave Imager)
Core
Observatory by NASA-JAXA
Constellation
Satellites by international partners
GPM Core Observatory
Global Precipitation Measurement (GPM)
Notes: Global Precipitation Measurement (GPM) is the follow up mission to TRMM. GPM is not the name of a single satellite, but the name of the mission consisting of GPM core observatory and constellation satellites for high accurate and frequent global precipitation observation. The GPM core observatory has been developed under an equal partnership between NASA and JAXA. As constellation satellites, we will utilize the international partners’ satellites with precipitation measurement capability. GPM is equipped with the most sophisticated spaceborne radar, the Dual-frequency Precipitation Radar (DPR) developed by JAXA and the National Institute of Information and Communications Technology (NICT), to observe 3-dimensional structure of rainfall. While TRMM/PR only uses a Ku-band radar (at approximately 13 GHz), GPM/DPR will add Ka-band radar (at approximately 36 GHz) to increase its sensitivity to weak rainfall and solid precipitation like snow. NASA provides the GPM microwave imager (GMI), which is a passive microwave radiometer, to obtain wide-area distribution of rainfall. GPM core observatory will be launched on February 27, 2014 (UTC).

## Slide 5
Typhoon MORAKOT (09W): Aug. 5 – 10, 2009 (Big impact in Chinese Taipei)
Rapidly changing precipitation phenomena need frequent observations.
Global rainfall map merging TRMM, polar orbiting microwave radiometer/sounders, and geostationary infrared radiometers.
http://sharaku.eorc.jaxa.jp/GSMaP/
GSMaP
5

## Slide 6
14 year-mean (from Jan. 1998 to Dec. 2011) surface rain observed by TRMM/PR
6
Rainfall Climatology by TRMM/PR
Notes: This is an example of TRMM results, showing the rainfall climatology over the tropics during a 14 year TRMM/PR observing period. This is really a breakthrough result, since there have been virtually no accurate precipitation observations over oceans. Considering the original design life of TRMM, which was just 3 years, we needed a follow up mission to continue this important observation from space.

## Slide 7
Ocean
Land
Variation of precipitation by TRMM/PR (Jan. 1998 – Jun. 2012)
Rainfall Climatology by TRMM/PR
To be extended by GPM to longer time period and mid/high latitudes

## Slide 8
2 types of medium-sized satellites and 3 generations: 10-15 years observation
GCOM 1st Generation Satellites
Instrument | Advanced Microwave Scanning Radiometer-2
Orbit | Sun Synchronous orbit Altitude：699.6km (on Equator) Inclination: 98.2 degrees Local sun time: 13:30+/-15 min
Size | 5.1m (X) * 17.5m (Y) * 3.4m (Z) (on-orbit)
Mass | 1991kg
Power gen. | More than 3880W (EOL)
Launch | May 18, 2012
Design Life | 5-years
GCOM-W1 (Water)
Instrument | Second-generation Global Imager
Orbit | Sun Synchronous orbit Altitude：798km (on Equator) Inclination: 98.6 deg. Local sun time: 10:30+/- 15min
Size | 4.6m (X) * 16.3m (Y) * 2.8m (Z) (on orbit)
Mass | 2093kg
Power gen. | More than 4000W (EOL)
Launch | JFY 2016
Design Life | 5-years
GCOM-C1 (Climate)
“SHIZUKU”
8

## Slide 9: Overview of GCOM Products
cloud
liquid
water
soil mois-
ture
snow
ice
distribu-
tion
sea ice
concen-
tration.
ocean
color
water
vapor
cloud
proper-
ties
snow
depth
snow
surface
temp.
land
cover
land
surface
tempera-
ture
sea
surface
temp.
sea
surface
wind
speed
precipi-
tation
aerosol
proper-
ties
snow
surface
proper-
ties
above-
ground
bio-
mass
primary
produc-
tion
PAR
Land
Ocean
Cryosphere
Atmosphere
C
Radiation
Budget
C
Carbon
Cycle
W
Water &
Energy
Cycle
9

## Slide 10
Depression of SST by Typhoon passage
10

## Slide 12
May 1-15, 2012
May 16-31, 2012
June 1-15, 2012
June 16-31, 2012
July 1-15, 2012
July 16-31, 2012
August 1-15, 2012
August 16-31, 2012
September 1-15, 2012
September 16-30, 2012
October 1-15, 2012
October 16-31, 2012
AMSR2
WindSat
300
200
150
120
100
90
70
30
0
[%]
Wet
Dry
Dry Snow
Wet Snow
Snow Area by MODIS
Soil Moisture Anomaly Ratio by Microwave
12
Soil Moisture Anomaly over
North America

## Slide 13
Atlantic
Patific
Northern Hemisphere：-153km2/day
Bering Sea：+0.5km2/day
Barents Sea：-30km2/day
http://kuroshio.eorc.jaxa.jp/JASMES/climate/index.html
Long-Term Dataset of Arctic Sea Ice
Combining histrical dataset and AMSR-E/AMSR2
13

## Slide 14
Land | 
Surface reflectance | Precise geometric correction
 | Atmospheric corrected reflectance
Vegetation and carbon cycle | Vegetation index
 | Above-ground biomass
 | Vegetation roughness index
 | Shadow index
 | Fraction of Absorbed Photosynthetically available radiation
 | Leaf area index
Temp. | Surface temperature
Application | Land net primary production
 | Water stress trend
 | Fire detection index
 | Land cover type
 | Land surface albedo
Atmosphere | 
Cloud | Cloud flag/Classification
 | Classified cloud fraction
 | Cloud top temp/height
 | Water cloud optical thickness /effective radius
 | Ice cloud optical thickness
 | Water cloud geometrical thickness
Aerosol | Aerosol over the ocean
 | Land aerosol by near ultra violet
 | Aerosol by Polarization
Radiation budget | Long-wave radiation flux
 | Short-wave radiation flux
Cryosphere | 
Area/ distribution | Snow and Ice covered area
 | Okhotsk sea-ice distribution
 | Snow and ice classification
 | Snow covered area in forest and mountain
Surface properties | Snow and ice surface Temperature
 | Snow grain size of shallow layer
 | Snow grain size of subsurface layer
 | Snow grain size of top layer
 | Snow and ice albedo
 | Snow impurity
 | Ice sheet surface roughness
Boundary | Ice sheet boundary monitoring
Common | 
Radiance | TOA radiance (including system geometric correction)
Ocean | 
Ocean color | Normalized water leaving radiance
 | Atmospheric correction parameter
 | Photosynthetically available radiation
 | Euphotic zone depth
In-water | Chlorophyll-a conc.
 | Suspended solid conc.
 | Colored dissolved organic matter
In-water | Inherent optical properties
Temp. | Sea surface temp.
Application | Ocean net primary productivity
 | Phytoplankton functional type
 | Redtide
 | multi sensor merged ocean color
 | multi sensor merged SST
Blue: standard products
Red: research products
Radiation budget by the atmosphere-surface system
Carbon cycle in the Land and Ocean
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
ECV
Future GCOM-C Products
14

## Slide 15
Global aerosol optical thickness in June 2003 using the GLI Near-UV (380nm) channel (NIR is used for the ocean area)
Global aerosol optical thickness in June 2003 using POLDER-2 polarization reflectance (provided by T. Sano, Kinki Univ.)
JAXA/EORC
Near-UV aerosol
Polarization aerosol
Not only over the ocean, SGLI will estimate land-area aerosols using near-UV (380nm) and polarization channels which are more sensitive to atmosphere scattering rather than land surface reflection
Combination of aerosol absorption by Near-UV and fine-mode aerosol properties by polarization
They will improve the atmospheric correction
Future GCOM-C Products
- Land Aerosol by NUV and Polarization -
15

## Slide 16
Photosynthetically Available Radiation
Snow Cover Extent
Plant Water Stress Trend
Hot Spots of Wild Fire
Cloud Cover Rate
Activity of Vegetation (NDVI)
Chlorophyll-a
Aerosol Optical thickness
Ocean and Land Surface Temperature
http://kuroshio.eorc.jaxa.jp/JASMES/index.html
16

## Slide 17
TANSO = Thermal And Near infrared Sensor for carbon Observation
TANSO-FTS (Fourier Transform Spectrometer)
TANSO-CAI
(Cloud and Aerosol Imager)
Greenhouse Gases Observing SATellite (GOSAT)
  Monitoring global distribution of Greenhouse Gases (CO2, CH4) from space.
  Joint project by JAXA, NIES, and MOE.
  Launch: 23 January 2009 by H2A launch vehicle
17
Notes: 1

## Slide 18: Five-year CO2 ,CH4, and the flux estimate data from GOSAT
Monthly Global Map of the CO2 column-averaged volume mixing ratios in 2.5 deg by 2.5 deg mesh in August 2013 (Ver.02.21)
http://www.gosat.nies.go.jp/index_e.html

## Slide 19: Earth Cloud, Aerosol and Radiation Explorer (EarthCARE)
To reduce the uncertainties in global warming prediction by measuring the three dimensional structure of clouds and aerosols, which are most uncertain parameter in the numerical climate models.
  Joint Mission by Europe and Japan
  Launch in 2016
  3 years lifetime
  400 km altitude
  Sun-synchronous orbit (Local time: 14:00)
Instrument
  CPR (Cloud Profile Radar)
  ATLID (Atmospheric LIDAR)
  MSI (Multi-Spectral Imager)
  BBR (Broad Band Radiometer)
19

## Slide 20
ALOS
(Optical & SAR)
(2006～2011)
ALOS-2 (SAR) (Launch: 2014)
Next Gene. (Optical)
Wide-swath and high-resolution data of ALOS series to contribute to disaster monitoring, land management, and solution of global environment issues, etc.
To promote public-private partnership
Panchromatic imager with wide-swath (50km) and high-resolution (0.8m)
obtain global 3D geospatial information
Wide-swath (Max 490km), High-resolution (1-3m)
L-band SAR (PALSAR-2)
ALOS
(Optical & SAR)
ALOS-2 (SAR)
2006
2011
2014
Next Gene. (Optical )
Concept of ALOS F/O Mission
Notes: ・ JAXA is planning new satellites as a post-ALOS mission.
・ ALOS-2 and ALOS-3.
・ ALOS-2 will carry L-band SAR, and ALOS-3 will carry optical imagers.
・ Tomorrow morning, Suzuki-san from JAXA will introduce about ALOS-2.
・ ALOS-3 will take over the global land observation by PRISM and AVNIR-2 on board ALOS, as well as ・・・