## Slide 1: ESA EO Data Preservation System: CBA Infrastructure and its future
LTDP+ Team

## Slide 2: Data Preservation System

## Slide 3: Preservation Element Front End (PE-FE)
Data flow between live missions and Data Preservation System via a common Front-end
Master Archive
Preservation Element Front-End
Cryosat-2
SMOS
TPM
Ingestion report
Cold Back-up Archive
Ingestion report
AEOLUS
Data Information System
Data Reprocessing

## Slide 4: Master Archive - Data Archive Service (DAS)
Implements the ESA Master Archive through a dedicated service awarded to industry through an open ITT:
Contract Kicked-off in August 2016
4.5 TB of EO consolidated Data
Two copies of the data held > 200 Km apart
Connection to the ESA EO WAN
Checks of the data at all stages from ingestion to delivery
Scalability required for growth of contents
Management of the data information (MetaData) in fully redundant Databases

## Slide 5: DAS Consortium
The industrial consortium is made of ACRI-ST (FR), adwäisEO (LU) and KSAT (NO), with the following distribution of roles:
ACRI-ST: Data Archiving (and delivery) Service provider – Prime contractor
adwäisEO: data archiving (and delivery) operation provider with its leading edge IT and connected secured infrastructure in Luxembourg
KSAT: data knowledge provider and overall ingestion validation

## Slide 6: DAS Infrastructure
Data ingestion
Data evolution
Data alignment
Data Management System
Tape transfer to Backup Archive
Data retrieval

## Slide 7: DAS Data flow

## Slide 8: Cold Back-up Archive (CBA)
Implemented in May 2014
Unique data & Unconsolidated data
PAC and Station Phase-out project data
Inter-directorate disaster recovery archive
Second copy of the Master Inventory
Live mission support to PDGS’s
  Odin
  Proba-1
  SCISAT
Two copies of the data held at ESA premises in Frascati
ESA Internal LAN
Main Tape Library capable of storing 24 Petabytes
Live Mission support
  Swarm (started in mid 2014)
  Cryosat-2 (started in March 2015)
  SMOS (started in May 2016)
  AEOLUS (supported at day zero)
EO-SIP, SAFE and Native Format archiver

## Slide 9: CBA Figures
Amount of Data (JAN 2019) 7.95 Petabyte | Number of Files (JAN 2019) 129,500,000 | 
Chart: 
| EO-SIP | Native
 | 20 | 80
Mission | Uncons. | Cons. | Native | EO-SIP | LIVE
ERS-1/2 | X | X | X | X | 
Envisat | X | X | X | X | 
Cryosat-2 | X | X | X | X | X
SMOS | X | X | X |  | X
SWARM | X |  | X |  | X
AEOLUS |  |  |  |  | X
Goce | X |  | X |  | 
Adeos | X |  | X |  | 
ALOS | X | X | X | X | X
GOSAT | X |  | X |  | X
Ikonos-2 | X |  | X | X | 
IRS-P3 | X |  | X |  | 
JERS-1 | X | X | X | X | 
Kompsat-1 | X |  | X |  | 
Landsat-1,8 | X | X | X | X | X
MOS-1,1b | X |  | X |  | 
Nimbus | X |  | X |  | 
NOAA-7,19 | X |  | X |  | 
Oceansat-2 | X |  | X |  | X
ODIN | X |  | X |  | X
PROBA-1 | X |  | X |  | X
QuickSCAT | X |  | X |  | 
Rapideye | X |  | X |  | 
Scisat | X |  | X |  | X
Seasat | X | X | X | X | 
SeaStar | X |  | X |  | 
SPOT1-2 | X |  | X |  | 
TerraSAR | X |  | X |  | 
WorldView-1,3 | X |  | X | X | 
Windsat | X |  | X |  | 
Average write a day: 13TB
Peak read a day: 10TB

## Slide 10: CBA Main Tape Library
STK SL8500
3000 slots
8 T1000D Drives (252 MB/s)
8 Robotic Arms
Fully redundant
16 GB Fibre Connection
SSD Disk based cache
ORACLE HSM driven

## Slide 11: CBA Ingestion tool
Bulk Ingestion from local or remote locations
Automated Ingestion from inbox baskets
EO-SIP and SAFE Validation
Metadata extraction
Reporting
Ingestion Confirmation Reports
Data Information System population

## Slide 12: Preservation Element Web Portal
Cold Backup Figures
Link to DAS datasets
Knowledge
Media Archive
Documentation
Ingestion status reports
Extraction status and Reports

## Slide 13: CBA Hardware

## Slide 14: LTDP Working Group #37 – DLR Presentation

## Slide 15: Cold Back-up Archive HW enhancements
Migrated technology and data from T10KB to T10KD
Increased number of drives to 8
Implemented 10GB Network
Upgraded FC environment from 8gbp/s to 16gbp/s
Upgraded 1rst tier from mechanical HDD to SSD Disks
Optimized 1st tier – dedicated LUN for iNodes
Implemented Disaster Recovery
Implementation of Business Continuity (1h)
Introduction of 2nd tier (sort of)
Migration to LTO-9
Introduction of object storage node (replace DR library ?)
2014
2017
2018
2019
2015
2016
2020
2021

## Slide 16: Dedicated LUN for iNodes
RAID
LUN1
LUN2
LUN3
LUNn
SAM-FS Master Configuration File
RAID-1
RAID
LUN
LUN1
LUN2
LUNn
SAM-FS Master Configuration File
iNodes
HSM File-System

## Slide 17: Business Continuity

## Slide 18: Business Continuity (2)

## Slide 19: Business Continuity (3)
Disaster Recovery Library seen as second copy by samfs-remote
Full iNodes dump performed daily
Incremental iNodes dump performed every hour
INBOX
LTA
samfs remote sync
Inbox
inodes
dump
Full
inodes
dump
Live Data
Disaster Recovery
HSM
Disaster Recovery
Tapes

## Slide 20: Business Continuity (4)
IP switch
Fully working CBA Environment
Maximum of 59 minutes of data loss

## Slide 21: Re-Introduction of 2nd Tier

## Slide 22: Large Tape User Group outcome
Technology progress per se is good, but obstacles ahead (NAND, HDD)
Key computing markets in the hand of very few companies
Price/performance advances are slowing down
HDD are a key storage for the foreseeable future, SSDs not cost effective for capacity
Have to closely watch the tape development
There will be NO relevant new storage technologies in the market in the coming few years (e.g. DNA storage)
Holistic view needed for the storage architecture, careful combination of SDD, HDD and Tape to optimize pure storage needs and high throughput I/O