## Slide 1
Hiroaki OKONOGI
Japan International Cooperation Agency (JICA)
15, Mar. 2018
Bogota, Columbia
GFOI Plenary 2018
Notes: Introduction about JJ-FAST

## Slide 2: Satellite sensor (L-band SAR)
Optical imager
SAR uses microwave, so it can observe both day and night regardless of cloud cover.
Synthetic Aperture Radar (SAR)
Landsat-5/TM 1992.04.23.
JERS-1/SAR 1992.04.23.
[RSSJ, 2011]
JAXA

## Slide 3: Deforestation detection
Forest area:
Strong radar reflection
Deforestation area:
Weak radar reflection
High image contrast between “forest” and “deforestation” areas.
JAXA

## Slide 4
Country | Cloud cover ratio
Ecuador | 97%
Gabon | 88%
Equatorial Guinea | 75%
Colombia | 65%
Bhutan | 63%
Indonesia | 60%
Vietnam | 56%
DRC | 54%
… | …
Global cloud-cover map
MODIS satellite data
Ecuador
Gabon
Ratio of period with more than 50% cloud-cover (in 2015.01-2017.09).
Vast rainforests are covered by cloud!
JAXA

## Slide 5: Example: Democratic Republic of Congo
Jul. 24, 2015
Jul. 27, 2015
42 days
Sep. 4, 2015
Aug. 28, 2015
PALSAR-2
LANDSAT-8
Oct. 16, 2015
Oct. 15, 2015
42 days
Jan. 3, 2016
Jan. 8, 2016
42 days
JAXA

## Slide 6: System Development
Satellite
  ALOS-2
  L-band PALSAR-2
  50m resolution
JJ-FAST
  From Nov. 2016
  For 77 countries
  Every 1.5 month
  More than 5 ha
  Low speed internet

## Slide 7: Web-Site of JJ-FAST
http://www.eorc.jaxa.jp/jjfast/

## Slide 8: Verification Survey & Feedback
By JAXA team
Verification at
  Brazil
  Botswana
  Gabon
  Indonesia
  Peru
By JICA Technical Cooperation Project
Feedback system
Countries
/Project

## Slide 9: Collaboration with optical satellite
Early Warning System
Control and Surveillance System
 | Optical | Radar
Resolution | ○ | ✗
Cloud | ✗ | ○

## Slide 10: The algorithm is being improved
Forest map (Mask data) improvement
2 times analysis -> time series analysis
Detection larger than 5 ha -> 2-3 ha
Data collaboration between optical and radar data

## Slide 11: TV program “Forest can change the World”
Scheduled to be broadcast on 27th Apr. 2018
*You can also watch through the internet from the next day.
Check detail at “https://www3.nhk.or.jp/nhkworld/”
UTC -5 | UTC (GMT) | UTC +9 (JST)
18:30-(26th Apr.) | 23:30- (26th Apr.) | 8:30-
00:30- | 5:30- | 14:30-
7:30- | 12:30- | 21:30-
12:30- | 17:30- | 26:30-

## Slide 12
fb.me/jica.jj.fast
@JICA_JJFAST
http://www.eorc.jaxa.jp/jjfast/

## Slide 14: Background
Tokyo Denki University
129 million hectares
(1990 to 2015: FRA2015 )

## Slide 15: JAXA’s L-band SAR satellites
1992.02.11. - 1998.10.12.
Resolution = 18m
JERS-1/SAR
ALOS-2/PALSAR-2
ALOS/PALSAR
2006.01.24. - 2011.04.22.
Resolution = 10m
2014.05.24. –
Resolution = 3m
JAXA

## Slide 16: Brazil’s case from 2009-2011
Project for Utilization of ALOS Images to Support the Protection of the Brazilian Amazon Forest and Combat Against Illegal Deforestation
Brazilian Government
Year | Detection of Deforestation | Illegal Logging
2010 | 1,007 | 140
2011 (stopped in April) | 176 | 11
Landsat 5 Image on 2011/09/07
Forest Density Difference by ALOS
Between 2009 and 2011
Notes: Brazilian government has been tackling illegal deforestation using optical satellite images (Landsat) since 2004.
Challenge was deforestation detection in the rainy season. Almost a half period of a year, the Amazon Forest is covered with clouds.
The ALOS SAR sensor can detect deforestation even in the rainy season or night time.

## Slide 17: Forest Governance Initiative