## Slide 1
JAXA missions and datasets
Status update
A. Rosenqvist, O. Ochiai, T. Tadono (JAXA)
SDCG-15 Session 2 Item#5

## Slide 2
ALOS-2 - 2018
  PALSAR-2 instrument status nominal
  Major revision of Basic Observation Scenario (BOS) implemented from Jan 2018
    10m dual-pol Fine Beam mode
      Observation windows increased (4  6)
      Boreal observations in May-Sept period to reduce seasonal impact on backscatter
      Increased obs frequency in the tropics
    50m ScanSAR
      Staggered observations to improve acq. success rate
      Every 42-day repeat maintained
    6m Quad-pol
      Global observations discontinued  focus on Super Sites
    3m Ultra-Fine
      Global observation plan completed

## Slide 3
ALOS-2 - 2019
  PALSAR-2 instrument status nominal
  Completing 5 years in orbit. PALSAR-2 entering “post-operational” phase from May 2019
  Reduction of duty cycle from 50% to 30%
  Impact on Basic Observation Scenario (BOS)
    10m dual-pol Fine Beam mode
      Observations reduced to single global cover age per year at top priority
      Additional observations planned at low priority
    50m ScanSAR
      No change.
      Every 42-day repeat maintained

## Slide 4: Schedule of ALOS/ALOS-2 Data Processing and Open Free Access
 |  | 2018 |  |  |  | 2019 |  |  | 
 |  | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec
ALOS | AVNIR-2 (10 m) |  |  |  |  |  |  |  | 
 | PALSAR (10 m) |  |  |  |  |  |  |  | 
ALOS-2 | ScanSAR (100 m) |  |  |  |  |  |  |  | 
 | Fine Mode (10 m) |  |  |  |  |  |  |  | 
As of February 2019
on Supercomputer
±60
Degree Area
Global
Japan Area
Data Processing
JICA-JAXA JJ-FAST intermediate products (ARD) processing
Data Processing
±60
Degree Area
Global
Japan Area
Data Processing
Under negotiation with commercial data provider

## Slide 5: GFOI Core Data Set – 25 m L-band SAR mosaics and Forest/Non-Forest maps
Annual global mosaics and Forest/Non-Forest (FNF) map
JERS-1 (1996) ~ ALOS (2007-2010) ~ ALOS-2 (2014-2017)  Over 20 years changes
1996 JERS-1
(only HH-pol.)
2007-2010 ALOS
2015-2017
ALOS-2
• HH backscatter (gamma-0) 16 bits
• HV backscatter (gamma-0) 16 bits
• Mask image (no-data, water, layover, shadowing.) 8 bits
• Local incidence angle image, 8 bits BYTE
• Observation date image (DN = days after mission launch) 16 bits
• Forest/Non-forest map

## Slide 6: GFOI Core Data Set – 25 m L-band SAR mosaics and Forest/Non-Forest maps
Global coverage
PALSAR-2 2018 (release
Q3 2019)
PALSAR-2 2017
PALSAR-2 2016
PALSAR-2 2015
PALSAR 2007 – 2010
JERS-1 ~1996
Free download at:
http://www.eorc.jaxa.jp/ALOS/en/palsar_fnf/fnf_index.htm

## Slide 7
Regional (pan-tropical) coverage (25m)
JERS-1: 1996 – 1998
Global low resolution (100m) coverage
JERS-1: 1996 – 1998
Free download at:
http://www.eorc.jaxa.jp/ALOS/en/palsar_fnf/fnf_index.htm
GFOI Core Data Set –
25 m L-band SAR mosaics and Forest/Non-Forest maps

## Slide 8: SAR Global Mosaic Status
Issue: Discontinuity of mosaic image in 2017
Solutions:
1. To use only summer season data from 2014 to 2018 as “MASTER”.
2. To widen the width of Path Ortho data.
2017 mosaic

## Slide 9: SAR Global Mosaic Status
Solution 1: To generate MASTER mosaic from only summer season data
For making Master mosaic, JAXA/EORC set the rule.
In the “2017 mosaic”, the rule of path selection was as following.
2017 Summer (from May to Aug)
 2017-Winter (the other month)
 2016 Summer  2016 Winter  2015 Summer  2015 Winter
The rule of “Master mosaic” is as following.
Monthly priority; Jul  Aug  Sep  Jun  May  Oct
Yearly priority; 2018  2017  2016  2015 2014

## Slide 10: SAR Global Mosaic Status
Solution 1: To generate MASTER mosaic from only summer season data
N65E105 (MASTER mosaic)
N65E105 (2017 mosaic)
2017 mosaic appeared the seasonal efficient because it is used the Jan-Feb data.
MASTER mosaic uses only summer season data.
 Backscatter is smoothly.
date
date
RGB
RGB
Jan-Feb
#Light Color in the date image indicates the early phase of the year.

## Slide 11: SAR Global Mosaic Status
Solution 2: To widen the width of Path Ortho data
N65E130(New mosaic)
N65E130(2017)
N65E130
①
②
③
④
⑤
⑥
⑦
⑧
The width of the image paths are extended in order to reduce striping effects.
①Jun-17, 2017, ② Sep-05, 2017
③Sep-05, 2017, ④ Jul-24, 2017
⑤Sep-19, 2017, ⑥Sep-01, 2017
⑦Sep-29, 2017, ⑧Sep-15, 2017

## Slide 12: SAR Global Mosaic Status
2017 Global mosaic

## Slide 13: SAR Global Mosaic Status
MASTER Global mosaic

## Slide 14: SAR Global Mosaic Status
Ex. Alaska
2017 RGB
MASTER RGB
MASTER date
2017 date
2017 N65W150
MASTER N65W150
Specially, Alaska mosaic has changed smoothly.
#Light Color indicates
the early phase of the year.

## Slide 15
Global Mangrove Watch
An international collaborative project established as part of JAXA’s Kyoto & Carbon (K&C) Initiative
  Mapping of extent and changes in global mangrove area
  Thematic Datasets
  Global mangrove baseline extent maps for 2010 (PALSAR + Landsat)
  Global maps of annual changes in the global mangrove extent – public release 2018/Q4
    1996 (JERS-1)
    2007 – 2009 (ALOS PALSAR)
    2015, 2016 & 2017 (ALOS-2 PALSAR-2)

## Slide 16
2010 global mangrove baseline
Niger river delta, Nigeria
Sundarbans, India & Bangladesh
Guayaquil, Ecuador

## Slide 17: Changes over time (7 epochs)
Kahan river delta, North Kalimantan, Indonesia.
(Left) Multi-temporal SAR composite (1996 JERS-1 SAR and 2016 ALOS-2 PALSAR-2)
(Right) Mangrove extent and changes, Red – mangroves lost 1996-2007, Orange – loss 2007-2016, Green – mangrove cover in 2016.

## Slide 18
Global 2010 baseline (v2.0) online at www.gfw.org
and for public download at data.unep-wcmc.org/datasets/45