## Slide 1: GEOS and GEOGLAM Activities Landsat 7/8 Phase 1 acquisitions and data distribution
Gene Fosnight

## Slide 2: Mission Landsat Launch and commissioning
Landsat 7
  Operational: since 15 April 1999
  Expected life time:; anticipate decommissioning in 2017
Landsat 8
  First OLI image 18 March on WRS since 11 April 2013
  Design Life: 5 years OLI and 3 years TIRS
  Fuel: 12+ years
Data policy: Free and open access
8 day repeat cycle using both satellites; 30 meter pixel; 185 km swath

## Slide 3: Mission Landsat-7 and -8 Acquisition Strategy
Construct an objective Global Environmental Record using a long-term acquisition plan
We propose to focus the use of Landsat 7 on continental land masses
  Reduce the use of Landsat 7 for acquisitions of island, night, ocean, and Antarctica scenes
  Landsat 8’s larger daily acquisition limit and sensor characteristics provide opportunities for increased extreme latitude, island, ocean and night acquisitions to complement a Landsat 7 LTAP focused on continental land masses

## Slide 4: Long-Term Acquisition Plan Summary
Landsat 7
  Images 350 – 450 images per day out of 540 - 630 sun-lit land opportunities
  ETM+ has strict duty cycle constraints
  Power cycling incurs warm up and data overhead penalties for short intervals equivalent to 4 scenes
  Storage capacity constraints
  Since the Scan Line Corrector failure, the LTAP pursues image pairs
  Acquires oceanic islands at reduced priority and frequency
  Acquires Arctic once per season
Landsat 8
  Currently acquiring 550 images per day
  Acquires using a formal LTAP
  Specified to acquire and distribute 400 images per day
  Deep Blue Band for ocean monitoring
  Better cloud detection with Cirrus Band
  Improved dynamic range
Landsat 7
  Increased imaging of continental land masses improved coverage of persistently cloudy areas and better gap filling
  Eliminate routine imaging of islands, water and Antarctica
  Increase imaging from 369 images/day (69%) to approximately 438 images/day (91%)
  Reduce ETM+ duty cycle from 15.1% to 14.4% and power cycles from 28.6 to 17.5 per day
Landsat 8
  Constrained by download costs/opportunities
  Higher island priority
  More frequent imaging for islands and Arctic
  Lower sun elevation constraint from 15% to 5%
  Increase Antarctica acquisitions
  Support selected night campaigns (such as urban heat islands, fires, sea ice, and volcanoes)
  Include selected near shore and interior water scenes
  Support large water campaigns
  Increase ascending node day acquisitions
Prior
Current

## Slide 5: Landsat 7 Continental versus Ops Model
Modeled one-year global coverage
Ops one-year global coverage

## Slide 6: Mission Landsat Data processing
Processing levels:
  Systematic-Corrected (L1G): Landsat 1-7
  Systematic- and Terrain- Corrected (L1Gt): Landsat 7-8
  Precision- and Terrain-Corrected (L1T): Landsat 1-8
  If precision control is available, we attempt to create an L1T. If, for example due to cloud cover, enough control cannot be found, we fall back to a systematic product.
Data formats:
  GeoTIFF
Means for data distribution
  Download only

## Slide 7: Total GEOGLAM Landsat 7 and 8 Images in 2013
Landsat 7 & 8 acquired up to 41 images for each scene
Landsat 8 only imaged during the last three quarters
The “worst” best cloud cover was 18%

## Slide 8: Landsat 7 & 8 2013 - Africa

## Slide 18: Total GFOI Landsat ETM+ and OLI Images in 2013
40% of the scenes had cloud free images
80% of the scenes had images with better than 1% cloud cover
90% of the scenes had images with better than 2% cloud cover

## Slide 19: Landsat 7 & 8 2013 Best Cloud Cover by Season
With Landsat 7 only the best cloud cover for 90% of the scenes is 15.62%.
With Landsat 8 only the best cloud cover for 90% of the scenes is 16.83%.
However using both Landsat 7 & 8 the best cloud cover for 90% of the scenes drops to 9.79%.
Landsat 8 statistics are worse than Landsat 7, presumably due to the lack of 1st quarter data.
Landsat 7 end of life will be no later than early 2018!

## Slide 20: Landsat 7 & 8 2014 and beyond
Acquisitions will continue at the current 550 images per day or greater
We currently acquire driving by cloud avoidance, so there are diminishing returns on additional acquisitions.
To do better requires more frequent coverage: Sentinel-2, CBERS-4
Radar and Airborne platforms provide the best opportunities for cloud avoidance…

## Slide 21: Looking forward to 2014
600
possible
550
current
750 unlikely
600 - 550
750 - 550

## Slide 22: Hopes and expectations
Good chance we’ll increase to 600 images/day at least for the northern hemisphere summer
Download costs and shutter use are limiting constraints
Will add selected “interior” water bodies
Will create a smooth priority ramp at poles to shift additional resources to vegetated regions
Will not be able to add more night imaging
Data distribution continues to be a challenge

## Slide 23
Thank You!
Questions?