## Slide 1: Update on KMA Space Program
Geun-Hyeok Ryu
Korea Meteorological Administration
CEOS Plenary 2018
Agenda Item 4.3
Brussels, Belgium
17 – 18 October 2018
Committee on Earth Observation Satellites

## Slide 2
Launch of GK-2A
AMI (Resolution) |  | ABI | AHI
1 blue | 0.47 (1km) | 0.47 | 0.46
2 green | 0.511 (1km) |  | 0.51
3 red | 0.64 (0.5km) | 0.64 | 0.64
4 | 0.856 (1km) | 0.865 | 0.86
5 | 1.38 (2km) | 1.378 | 
6 | 1.61 (2km) | 1.61 | 1.6
 |  | 2.25 | 2.3
7 | 3.830 (2km) | 3.90 | 3.9
8 | 6.241 (2km) | 6.185 | 6.2
9 | 6.952 (2km) | 6.95 | 7.0
10 | 7.344 (2km) | 7.34 | 7.3
11 | 8.592 (2km) | 8.50 | 8.6
12 | 9.625 (2km) | 9.61 | 9.6
13 | 10.403 (2lkm) | 10.35 | 10.4
14 | 11.212 (2km) | 11.2 | 11.2
15 | 12.364 (2km) | 12.3 | 12.3
16 | 13.31 (2km) | 13.3 | 13.3
2017
2019
2018
2013
2014
2015
2016
System Integration
Module integration
Bus design and review
Launch/IOT/OPS
Kick-off
Launch
CDR
TRR
Test
AMI PSR
SRR
PDR
System
Req. analyss
Preliminary
Design
Critical
Design
payload
test
AIT
Prep. Launch
IOT, Ops
GK2A is scheduled to be launched in 5th December 2018

## Slide 3
Observation Area and Schedule
  Full Disk (FD)
  Extended Local Area (ELA) : 3800 X 2400 km (EW X NS)
  Local Area (LA) 1000 X 1000 km
1 FD + 5 ELA + 5 LA : 10 min

## Slide 4
GK-2A 10-minute Timeline
KMA will operate 3 different observation areas with 10-min schedule
  FD : Full Disk
  ELA : Extended Local Area centered Korean Peninsular
  LA : Target Area which can observe any area by user request
The official request of target area observations by global users
over the Asian Pacific region (RA II and RA V) will be available
  The first priority is the disasters monitoring over Korean Peninsular,
  such as typhoon, wild fire etc
  Global users submit official request form defining specific measurement area via designated web page (or email)
  Decision will be made before disseminating images via designated web page

## Slide 5
GK-2A/AMI Geophysical Products
Secondary Products
Vertical
Temperature
Profile
Vertical
Moisture
Profile
Instability Index
Cloud Detection
Primary Products
Fire Detection
Vegetation Index
Vegetation Green Fraction
Surface Emissivity
Surface Albedo
Cloud Effective Radius
Cloud Liquid Water Path
Cloud Ice Water Path
Cloud Layer/Height
Probability of Rainfall
Fog
Sea Surface
Temperature
Land Surface
Temperature
Snow Cover
Sea Ice Cover
Aerosol
Detection
Asian
Dust
Detection
Asian
Dust
Optical
Depth
Aerosol
Optical
Depth
Volcanic
Ash
Detection,
Height &
Mass
Radiance
Atmospheric
Motion
Vector
Total Ozone
Cloud Top
Temperature
Cloud Top
Pressure
Cloud Top Height
Rainfall Rate
Convective Initiation
Cloud Phase
Snow Depth
Ocean Current
Cloud Type
Cloud Amount
Cloud Optical Depth
Rainfall Potential
Aerosol Particle Size
Visibility
Absorbed SW Radiation (SFC)
Downward SW Radiation (SFC)
Reflected SW Radiation (TOA)
Downward LW Radiation (SFC)
Upward LW Radiation (SFC)
Upward LW Radiation (TOA)
Aircraft Icing
Overshooting Top Detection
SO2 Detection
Total Precipitable Water
Clear Sky Turbulence

## Slide 6
Non Meteorological Application
  Focus on NMA products such as dust and ocean/land surface parameters
  With coming era of GK-2A, significantly expand to NMA by preparing the various additional products for monitoring forecast fire and flood
NMA products | Current (COMS) | Future (GK-2A)
Dust | Aerosol Index AOD | Aerosol Detection(Aerosol Type) AOD, Aerosol Peak Height Surface-level Aerosol Concentration
Ocean environment monitoring | SST Sea Ice | SST, Sea Surface Current, Sea Ice SST Anomaly, Ocean Front, Ocean Eddy Upwelling Age, Vessel Icing
Land surface properties and Hydrology | evapotranspiration LST | Soil Moisture, Evapotranspiration Surface Albedo, Surface Emissivity LST, NDVI, Drought Index
Forest fire |  | Fire Detection Fire Potential Fire Radiative Power Fire Fraction of Burned Area
Flood |  | Flood RGB image

## Slide 7
Application: Dust height & dust at surface
=
AODcombine Process
MODIS <10km>20070109
SeaWiFs <10km>20070109
O4 VCD
SZA
VZA
RAA
Reflectance
AOD
LUT Matching
O4 AMF from OMI
Retrieved Dust peak Height
Estimated PM10
PM10 & AOD matching
AOD(Cloud Screening), PBLH, f(RH), Surface wind
MLR model
  Aerosol Concentration at surface
  AOD Fusion
  Aerosol Peak Height

## Slide 8
Application: Ocean
Ocean environment monitoring parameters; sea surface temperature and SST anomaly, sea surface current, ocean front, upwelling age, oceanic eddy, and vessel icing together with sea surface temperature and sea surface current.
SST
Sea Surface Current

## Slide 9
Application: Surface property/Soil moisture
Soil moisture
LST = a+b NDVI
(an empirical formula: a, b is determined from observation data)
Relationship between TVDI and SM
TVDI : 0 (saturated soil) ~ 1(dry soil )
* TVDI: Temperature-Vegetation Dryness Index
LSTmax= a1 + b1 (NDVI)
LSTmin = a2 + b2 (NDVI)
TVDI-based Soil Moisture (%)

## Slide 10
Application: Drought and Flood monitoring
Drought / Flood
Drought monitoring: VHI (Vegetation Health Index)
Improvement of sensitive variable in order to explain vegetation stress by VHI
Considering seasonal and individual vegetation difference with respect to change weight of VHI and TCI (Temperature Condition Index)
Flood monitoring
high resolution RGB composite image
(0.5 km spatial resolution downscaling)
2km-2km-2km
2km-1km-500m
500m-500m-500m

## Slide 11
Application: Forest fire monitoring
Wildfire potential
Development of four meteorology-based indices and two surface dryness indices
  - FFDI(Forest Fire Danger Index), FFMC(Fine Fuel Moisture Code), HI(Haines Index), MNI(Modified Nesterov Index)
  - NDDI (Normalized Difference Drought Index), TVDI (Temperature Vegetation Dryness Index)
Fire Radiative Power
Fire Burned Area
  using Sentinal-2 data

## Slide 12
Global network of Space Weather monitoring
GK-2A: 128º E
EDRS-C : 31º E
GOES-East : 75º W
GOES-West: 135º W
Compression (dayside)
Field Stretching (night side)
Solar Wind Variation
(Bz, V, n)
GOES-East
GOES-West
GK-2A
EDRS-C
Data Receiving
and
Pre-processing
LV1
Data Processing
system
Data Analysis
system
Public
service
FTP, Web
LV2
LV1 : Reconstructed, Processed instrument data at full resolution, time-referenced anotated with ancillary
information including calibration coefficients and georeferencing parameters applied
LV2 : Product retrieved using additional algorithm or model with LV1 data
  KSEM of GK2A could cover eastern local times for the space weather monitoring at geostationary orbits
  Space Weather Data Processing Subsystem for L1 and L2 retrieval

## Slide 13
Data Service Plan : Geo-KOMPSAT-2A
Via GK-2A broadcast (< 3 minutes data latency)
  Broadcast all 16 channels data (UHRIT, full resolution) of meteorological observations
  Maintain L/HRIT broadcast corresponding to COMS five channels
Via Landline
  Real-time cloud service similar to HimawariCloud will be implemented (< 5 min data latency)
  GK-2A data also will be available in DCPC-NMSC (http://dcpc.nmsc.kma.go.kr)
L1 Data Format
  netCDF4(for each channels), with GSICS information
L2 Data Format
  netCDF4(for each products)
L1 Data Header Structure
General Information
Output Information
Pixel File Information
Projection Information
Star Measurement Information
INR Characteristics Information
Image Geometry Quality Information using Star Measurements
Registered Image Information
Quality Area Image Information

## Slide 14
Data Service Plan : LDUS System Development(Under detail design)
A
K
3.7m
E
5.5m
C
N
6.5m
3.5m
F
N
P
4.5m
M
N
A
K
Rain Loss Margin(99.99%) : ITU-R 837-5
E
A
Area1(-1dB, EL=55°)
Area2(-2dB, EL=37°)
Area3(-3dB, EL=10°)
[UHRIT Service Area and Rain rate Map by ITU-R]
SDUS
LRIT service is redesigned for using on a ship mounting with an 2 axis tracking antenna.
Minimized SDR(Software Defined Radio) Receiver
Contents will be satellite images, weather fax, etc.
MDUS
Downscaled 5ch data(TBC) will be serviced by COMS compatible HRIT telemetry.
Compact SDR(Software Defined Radio) Receiver built in Receiving Server
LDUS
AMI 16ch data will be serviced by CCSDS formatted UHRIT Telemetry on DVB-S2 Broadcasting Standard
Service Area is same as COMS (El > 10°) but required antenna diameter depends on the rain degradation margin.
Mini PC
ADC
SDR
Receiver
SDUS System

## Slide 15: Thank you!