## Slide 1
CEOS Plenary 2025
Implementation of the Common Practices for Quantifying Methane Emissions
from Plumes Detected by
Remote Sensing
Paul Green, NPL / UKSA
with JPL, NIST & LLBL
& wider GHG TT
Agenda Item #4.5
39th CEOS Plenary
Bath, United Kingdom
4th - 6th November, 2025

## Slide 2
Motivation
The Global Methane Pledge (now signed by 155 countries) seeks to reduce methane emissions by 30% between 2020 and 2030
Fugitive emissions / high emitters (emissions t> 100 kg/hr) represent a substantial fraction of fossil and waste emissions. Estimated between 30% and 75% of O&G emissions in some US production basins.
Public and New Space observations of CO2 and CH4 are increasingly being used to identify high emitters to improve production efficiency of drilling, support regulation, and are likely needed for a functioning reporting obligations and carbon market. Despite the current geopolitics, the need for data is increasing, not reducing.
Currently there are 3 missions dedicated to facility scale emissions monitoring, with another 10 expected in few years – in addition to the products generated from public data.
We need a set of “common” practices for reporting VVUQ and QA for facility scale emissions so that producers of these data know what is expected by the community and (new) users know how the data should be generated and reported so that it can be trusted

## Slide 3
Growing constellation of GHG concentrations observations from the global to the facility scale
These are now being used to derive carbon dioxide and methane emission (flux) estimates on a range of spatial and temporal scales

## Slide 4: New rules on Energy sector
https://www.epa.gov/controlling-air-pollution-oil-and-natural-gas-operations/epas-final-rule-oil-and-natural-gas
https://oeil.secure.europarl.europa.eu/oeil/popups/ficheprocedure.do?reference=2021/0423(COD)&l=en

## Slide 5: Corporate emissions and climate risk reporting
TCFD
Compulsory emissions & climate risk reporting for listed companies in US and UK, together with voluntary schemes to maintain market competitiveness aligned with customer climate expectations

## Slide 6: Common practise structure & contributors
Common practices intended users are
  producers of these data (to know what is expected by the community)
  users of these data (to understand how it should be generated and know how to use)
Overall structure
  Motivation, remit and timeliness
  Common practise for L0 to L4
  Validation current art
  Quality assessment framework
Integrates efforts across multiple agencies

## Slide 7: Workflow Common Practice
At a high level, all practitioners use the same sequence of steps in their workflows
The details of implementation vary, increasingly later in the process (from concentration/enhancement to emissions estimates)
Later plume detection, delineation and emission quantification steps require a human in the loop
Credit (L-R):
GHGSat
MethaneSat
CarbonMapper

## Slide 8: State of Practice for Validation – controlled release
Independent testing of space-based methane detection needed, including several new satellite programs launched last year
Cooperative and single-blind controlled release tests, building on 5+ years of satellite, airplane and ground sensor tests
Expanded participation to 12+ methane satellite platforms and 15 analysis teams
2024-2025
150 release (10-1500 kg/h) cooperative stage being analysed
First single-blind stage “Phase 1” is ongoing in Q1 2025, data to be unblinded on May 1
Subsequent phases to follow with alternate testing configurations
?
Metering and
release point
Gas trailers and
pressure reg
Work station
10 m ultrasonic winds
and meteorological station
Credit: A Brandt Stanford tinyurl.com/stanford-methane
*Participants know location but not [on/off] or volume flow rate. Coriolis flow metering for leaks between 3 kg/h and 1500 kg/h

## Slide 9: Quality Assessment framework
Column Enhancement
Emissions
Quality Assessment framework aligned with that developed within EDAP / CSDA for consistency across GHGs and other ECVs

## Slide 10: Best practice as an enabler
Build on previous CEOS work on best practises in the public and new space domains and want to partner with key parallel programmes and stakeholders to add value as an underpinning framework to enable reporting in the public and commercial sectors
UNFCCC
CEOS roadmap
UNEP IMEO
WMO G3W
US GHG Centre

## Slide 11: Progress and timeline
2024 – outline development & peer review
2025 – detailed completion, peer review & v1 finalization for Summer 2025
  v1.0 endorsed by CEOS & CGMS in August 2025
  Available at https://ceos.org/publications-key-documents/ and directly at https://zenodo.org/records/17047789

## Slide 12
Implementation
Facility scale / Plume Detected emissions
    Implementation plan to develop first adopters –two commercial producers engaged (GHGSat and CarbonMapper) with assessment against common practices underway (followed by others)
Continued engagement with UNEP IMEO in their adoption within the MARS program and beyond
‘The common practices defined by CEOS for satellite-derived plume emission estimates provide a solid foundation for achieving aligned methods and data descriptors that enable efficient and comprehensive emissions data sharing and intercomparison as well as provide a route to understand the sources and effects of variation in approach. The document specifies clear data descriptors and methods transparency requirements that IMEO will require of satellite data providers aiming to contribute to our system’
UN Climate & Clean Air Coalition (short-lived climate pollutants initiative) Global Methane Pledge
WMO G3W and IG3IS 2026 best practices initiatives
Represented at COP-30 via SBSTA statement, UNEP IMEO, ESA and GMP Ministerial engagement
Highlighted in UK Govt Carbon Budget and Growth Delivery Plan Methane Action Plan
Discussion: Future work on implementation, promotion, and encouraging uptake.

## Slide 13
Next steps (in GHG TT roadmap)
Facility scale / Plume Detected emissions
Co-ordination of controlled release validation alongside academic partners
Studies to follow up v1.0 recommendations (and identified gaps)
L2 & L4 intercomparison exercises recommendations
Towards v2.0 (in a few years) to maintain relevance in evolving ecosystem and incorporate on-going studies to more from ‘common practice’ to ‘good practice’- activity progressed by AC-VC and GHG task team.
Area flux mappers
    Motivated to provide more useful and accessible routes to use in GST2 (2027), the focus is on a unified offering on country-scale emission estimates.
    Draws on existing initiatives OCO-MIP, RECCAP2 etc.
    Aim is to quantify, consolidate and (where possible) reduce uncertainties in estimates
    Existing finance sector interest alongside academic.
    CO2/CH4 may require different approaches – as at different levels of agreement and maturity.
    In time this effort is handed off to an appropriate ”operational” focused organization after agreement between vested parties