## Slide 1: An Effort for Improving Reliability of GHG Monitoring from Space – JAXA-NASA Joint Collaboration for 10 years -
Akihiko KUZE
Earth Observation Research Center
Japan Aerospace Exploration Agency
UNFCCC/IPCC Engagement Side Meeting
SIT Tech Workshop 2017 ESA/ESRIN, Frascati, Italy
12th September 2017
Committee on Earth Observation Satellites

## Slide 2
GHG measurements from space
2
SCIAMACHY (2002 - 2012) | GOSAT (2009 - ) | OCO-2 (2014-)OCO-3 (2018) |  | GHGsat (2016-)
TanSat (2016-) | TROPOMI (2017) | GOSAT-2 (2018-) | MERLIN (2020) | GeoCARB
MicroCarb (2020) | ASCENDS (2021) | CarbonSat (2022) |  | 

## Slide 3
Intercomparison between Instruments
Steps Towards contribution to GHG Anthropogenic Emission Inventory
3
Radiance Spectra
Challenges
Pre-launch
Radiometric Standard
GHG Column Density
Global and Regional Flux
High spectral resolution data with different type of spectrometers
Selection spatio-temporal sampling Pattern from limited number of data and spatial resolution
Topography, Observation geometry, aerosol scattering,
instrument degradation

## Slide 4
GOSAT Operation and Research Progress
since its Launch
Frequent and global CO2 distribution
2011 Butz et al.
the accuracy of 2 ppm or 0.5% for CO2 and 13 ppb or 0.7% for CH4
Global flux inversion (b)
2011 Joiner et al. and Frankenberg et al.
Solar induced Chlorophyll Fluorescence (c)
Long term CO2 and CH4 (d)
2015 Turner et al. (e)
North American CH4 emissions using prior information on source locations <aggregation, emission source classification>
Flux Emission from CH4 point sources
Goal
City level CO2 flux estimation with source classification
Launch 2017
Instrument Data Processing
Level 1 V201 (2015)
Long-term uniform quality data set
V210 (2017)
Feb. 2009
The first very-high spectral resolution spectrometer to measure column-averaged dry air mole fractions of CO2 and CH4 globally
Jul. 2014
OCO-2 launch
Pointing mechanism switched to the secondary
(Jan. 2015)
2-axis agile pointing system effectively collects science data over regions and areas of special interest.
(d) NIES/JAXA/MOE
(b) Houweling et al.
(e) Turner et al.
(a) Hammerling et al.
Non-linearity corrections
(C) Frankenberg et al.
4

## Slide 5
Japanese GOSAT and US OCO-2 have different observation strategies.
TANSO-FTS onboard GOSAT has wide spectral coverage from SWIR to TIR and an agile pointing system at the expense of spatial context, while OCO-2 targets CO2 with higher spatial resolution using imaging grating spectrometers.
Since the early phase of the two projects, both teams have worked to demonstrate the effectiveness of satellite greenhouse gases observation.
International Effort to Demonstrate the Reliability
of Satellite GHGs observations.
5

## Slide 6: International Collaboration to Demonstrate the Reliability of the GHG Monitoring from Space Inter-Comparison between GOSAT and OCO-2
2008 2009 2010 2011 2012 2013 2014 2015 2016 2017
Radiometric calibration
Prelaunch
X-CAL
CO2 & CH4 profile
XCO2 XCH4 XCO
Coincident Target
Annual Vicarious Calibration at the desert playa in Nevada
In situ CO2 and CH4 on NASA AMES AJAX
Column with a compact FTS
Calibrated GOSAT and OCO-2 radiance spectra agrees within 5% for all bands (386 match up data).Katoka et al., (submitted)
6
2014/09～2016/05
XCO2 Level2 matchup
Agreement:
(ACOS-GOSAT B73.3
OCO-2 B7.3)
<0.18 ppm over Ocean
<0.57 ppm over Land, high gain
< 0.19 ppm over Land (desert)

## Slide 7
Annual Joint Campaign
Every June near summer solstice (9th in 2017) in Nevada Desert site
Almost all the geophysical parameters in radiative transfer have been measured
Surface Spectral Reflectance
UV-SWIR
BRDF
Path 37
from West
Path 36
from East
19.9deg
19deg
33.0deg
25deg
Surface and Profile
of Pressure, Temperature, Humidity
Surface Thermal radiation
Variability
Aerosol Optical Depth
TOA Spectral radiance
High altitude
Vertical
CO2 CH4 O3
Horizontal
CO2 CH4
Surface
CO2 CH4 CO O 3 Wind speed
7
Notes: 1

## Slide 8
Long Term and Global Intercomparison
Kataoka et al. (submitted)
The time series of XCO2 from Sep. 2014
8

## Slide 9: GOSAT Data Products and Distribution
Level 4 Processing
- estimate the global net flux
NIES
Level 1 Data
Measurement
Receive and Record
Interferogram
JAXA
H2O
CO2
CH4
Data distribution
Level 2 and 3Processing
- to produce the global distribution map for CO2 and CH4
- validation
Level 1 processing
- processing to spectra
- calibration
Data distribution
Public
Regional Flux
9
Notes: 9

## Slide 10: Beyond Data Products Analytical Results Availability
http://www.eorc.jaxa.jp/GOSAT/CO2_monitor/index.html
July 2010
https://mirador.gsfc.nasa.gov/
Coal
Livestock
Oil /Gas
Total
Fire
Rice
Waste
Wetland
Other
CH4 emission (Gg/year）
NASA GES DISC (N America CH4 Emission) CMS (Carbon Monitoring System) Methane (CH4) Flux for North America 0.5 deg x 0.667 The CMS Methane (CH4) Flux for North America data set contains estimates in North America based on an inversion of the GEOS-Chem chemical transport model constrained by GOSAT.
Contents: Long term
CO2, CH4, SIF, AOD measured by GOSAT
Solar-induced chlorophyll fluorescence
Aerosol optical depth
10
Ratio of successful retrieval by GOSAT

## Slide 11
Conclusion
Almost all the geophysical parameters in radiative transfer have been measured during annual joint campaigns. Accuracy and precision of GHG satellite remote sensing have been well characterized.
The cross-comparison of spectral radiances and CO2 estimates from long term and global GOSAT and OCO-2 observations demonstrated the reliability of CO2 remote sensing from space.
These exercises will facilitate the interpretation of the data from the near-future satellites with unique instrument designs from different space agencies.
Both top-down satellite data and bottom-up emission inventories will be crucial to climate policy.
11