## Slide 1: Carbon Strategy: GHGs and AC-VC
David Crisp, Jet Propulsion Laboratory, California Institute of Technology, NASA
CEOS 2018 SIT Technical Workshop
Climate and Carbon Observations, 2.5
EUMETSAT, Darmstadt, Germany
13 – 14 September 2018
Committee on Earth Observation Satellites

## Slide 2
Background
Action T71 from GCOS IP 2016 GCOS-200
“Specifically CEOS and CGMS will undertake, over the next few years, dedicated preparatory work in a coordinated international context…:
The definition of an architecture of space component elements to address the requirements of a CO2 and GHG monitoring system , … This will provide a global holistic perspective both from the point of view of existing and planned space segment assets as well and that for an optimum global constellation.
The documentation of best practices on the relationships between individual space agencies and their counterparts working on the modelling aspects, the inventories and in-situ data provision, …
The further consolidation of partnerships and collaborations between the relevant international entities including: the relationship between CEOS and CGMS on the space component aspects, the partnership with the WMO and GEO on the broader framework, … and finally the relationships with GCOS itself, UNFCCC and IPCC TFI process in better defining the role for space-based observation in the inventory guideline process.”
Mark Dowell, 6/2018

## Slide 3
Approach:
The CEOS Chair Initiative on GHGs
Specific Chair Initiative : Laying the foundation for an international CO2 and GHG monitoring system
Three specific activities are foreseen for advancing this effort in 2017-2018:
Facilitate the completion and follow-on activities of the AC-VC whitepaper on defining an optimum constellation for CO2 and GHG monitoring, including the joint competences of CEOS and CGMS, and in the general framework of the continued implementation of the CEOS Carbon Strategy
Advance the relationship with CGMS for an operationally implemented and sustained observation capability. Consider establishing a formal working relationship between CEOS and CGMS as with the successful ongoing relationship on Systematic Observations of ECVs in support of UNFCCC.
Place the space segment in the broader context of a fully sustained system for CO2 monitoring. Individual CEOS Agencies have counterparts in their individual countries/regions who have responsibility for Inventories, the required modelling, in-situ infrastructure and the ground segment elements.
Mark Dowell, 6/2018

## Slide 4
The CEOS Chair commissioned the Atmospheric Composition Virtual Constellation (AC-VC) to define the key characteristics of a global architecture for monitoring atmospheric CO2 and CH4 concentrations and their natural and anthropogenic fluxes from instruments on space-based platforms to:
reduce uncertainty of national emission inventory reporting, identify additional emission reduction opportunities and provide nations with timely and quantified guidance on progress towards their emission reduction strategies and pledges (NDCs); and
track changes in the natural carbon cycle caused by human activities (deforestation, degradation of ecosystems, fire) and climate change (drought, temperature stress, melting permafrost and changes in ocean thermal structure and dynamics).
Objectives of the AC-VC White Paper

## Slide 5
Incorporates contributions from
  2017 and 2018 CEOS SIT, AC-VC and CEOS Chair Priority meeting and 2017 and 2018 CGMS meetings
  83 authors from 45 organizations
White Paper Structure, content, and intended audiences
  Executive Summary (2 pages)
    Overview of objectives and approach
    Intended for policy makers and CEOS/CGMS Agency leads
  Body of report (75 pages)
    Documents science background and requirements, current and near-term mission heritage, and system implementation approach
    Intended for program scientists and project managers
  Technical Appendices (42 pages)
    “Textbook” summarizing state-of-the-art in observation capabilities and analysis methods to justify system-level requirements
    Intended for scientists, engineers, and inventory community
AC-VC White Paper Approach

## Slide 6
Executive Summary
Chapter 1: Introduction
Chapter 2: Retrieving Fluxes from Atmospheric CO2 and CH4 Measurements
Chapter 3: Space-based CO2 and CH4 Measurement Capabilities and Near-term Plans
Chapter 4: The Transition from Science to Operations
Chapter 5: Designing an Operational LEO Constellation for Measuring Anthropogenic CO2 Emissions – The Sentinel CO2 Initiative
Chapter 6: Integrating CO2 and CH4 Satellites into Operational Constellations
Chapter 7: Conclusions and Way Forward
Appendices
A1: Remote sensing retrieval methods for estimating XCO2 and XCH4 from observations of reflected sunlight
A2: Methods for quantifying surface fluxes of CO2 and CH4 from space-based XCO2 and XCH4 estimates
A3: Observation system simulation experiments (OSSEs)
A4: Lessons learned from SCIAMACHY, GOSAT and OCO-2
A5: Greenhouse gas monitoring satellites from commercial organizations & non-governmental organizations
A6: Advantages of LEO, GEO and HEO vantage points
A7: CEOS Agencies implementing CO2 and CH4 missions
A8: Acronym List
References Cited
White Paper Contents

## Slide 7
A System-Level Approach for Integrating Atmospheric Data
Observations
Integration & Attribution
Outputs
Models
Transport, land & ocean carbon cycle, fossil fuel emissions.
Estimation system
Data assimilation and uncertainty estimation
CO2 and CH4 emissions & removal Hot-spots with uncertainties
Country/region CO2 and CH4 emissions & removals with uncertainties
Satellite Measurements of CO2 and CH4
Ground and Airborne Measurements of CO2 and CH4
Meteorology
Satellite & in-situ
Auxiliary Data
Satellite observations of CO, NO2, clouds, aerosols …
Prior Information
Fluxes, model parameters, emission reports, economic statistics.
Other Carbon Cycle Products

## Slide 8
GHG Mission Timeline

## Slide 9
To transition from a series of scientific experiments to an operational constellation designed to provide end users with products and services, CEOS should work with CGMS and other partners to:
Define the overall system requirements
Establish data delivery latency requirements (Timeliness)
Incorporate reliability and robustness in the end-to-end system
Provide traceability in a configuration-controlled environment
Incorporate reprocessing, preservation, and archiving systems
Implement rigorous quality assurance
Continuously monitor and report calibration and validation
Provide user support and capacity building
Establish international coordination and long-term planning
Transition from Science to Operations

## Slide 10
To define requirements for space-based atmospheric products that can support GHG inventories, CEOS and should work with
  stakeholders in the GHG inventory and policy communities (in particular the UNFCCC), to refine the atmospheric product types and requirements that must be met to inform inventories
  GCOS, WMO IG3IS, and the ground-based GHG measurement community to define the relative roles of ground-, aircraft-, and space-based measurements in an atmospheric GHG monitoring system
CEOS should work with CGMS and other partners to define requirements and implementation strategies that will provide
  A Prototype system that delivers harmonized observations (calibrated, geolocated spectral radiances) and XCO2 and XCH4 estimates from the existing fleet of CO2 and CH4 satellites
  A prototype atmospheric CO2 and CH4 flux product that can provide a baseline atmospheric CO2 and CH4 inventory for use in the 2023 stocktake
Step 1: Defining Requirements

## Slide 11
By 2021, CEOS Member Agencies will have launched 10 space-based CO2 and/or CH4 monitoring satellites
CEOS should integrate the products from these space-based systems into to create a harmonized, global, space-based record of atmospheric CO2 and CH4 spanning the period from 2009 - 2021.
CEOS should exploit the capabilities of its member agencies and its partners in WMO IG3IS to combine the space-record with ground-based and aircraft-based atmospheric CO2 and CH4 measurements to produce a prototype end-to-end atmospheric GHG system and use this prototype system to create a baseline atmospheric CO2 and CH4 flux inventory.
If this prototype atmospheric inventory can be completed by 2021, CEOS should work with its partners in the inventory community to assess its utility for informing the bottom-up inventories being prepared for the 2023 stocktake
Step 2: Integrating Existing Systems to Develop a Prototype Product

## Slide 12
The coverage, resolution, and precision requirements could be achieved with a constellation that incorporates
A constellation of 3 (or more) satellites in LEO with
  A broad (> 200) km swath with a mean footprint size < 4 km2
  A single sounding random error near 0.5 ppm, and vanishing small regional scale bias (< 0.1 ppm) over > 80% of the sunlit hemisphere
  One (or more) satellites carrying ancillary sensors to identify plumes (CO, NO2) or to detect and mitigate biases (CO2 and/or CH4 Lidar)
A constellation with 3 (or more) GEO satellites
  Monitor diurnally varying processes (e.g. rush hours, diurnal variations in the biosphere)
  Stationed over Europe/Africa, North/South America, and East Asia
This constellation could be augmented with one or more HEO satellites to monitor carbon cycle changes in the high arctic
A Candidate Operational CO2/CH4 Constellation Architecture

## Slide 13
Space based sensors for CO2 and CH4 must be
  calibrated to unprecedented levels of accuracy to detect and quantify the small XCO2 and XCH4 changes associated with surface fluxes
  cross-calibrated against internationally-accepted standards prior to launch and in orbit so that their measurements can be integrated into a harmonized data product that meets the accuracy, precision, resolution, and coverage requirements for CO2 and CH4
Efforts by the ACOS and GHG-CCI teams have demonstrated the feasibility of this approach for SCIAMACHY, GOSAT, and OCO-2
  Rigorous pre-launch and in-orbit calibration methods demonstrated
Substantial improvements will be needed to meet the much more demanding requirements of anthropogenic emissions monitoring
  Cross-calibrating a more diverse range of spacecraft sensors
  Reducing calibration-related biases across multiple spacecraft
Other Needs: Calibration Advances

## Slide 14
XCO2 and XCH4 estimates across the constellation must be cross validated against internationally-recognized standards to yield a harmonized integrated product that meets the demanding precision, accuracy, resolution, and coverage requirements
The Total Carbon Column Observing Network (TCCON) currently serves a critical transfer standard between the space based measurements and the in situ standard maintained by WMO GAW
TCCON must be maintained and expanded meet the much greater demands of anthropogenic emissions monitoring on national scales
  Biases must be reduced by a factor of 5-10 from 0.25% on regional scales to < 0.025 to 0.05% to improve inventories
Additional validation methods must be developed to support validation emissions estimates on scales ranging from that of individual large power plants to that of a large urban area.
Other Needs: Validation Advances

## Slide 15
Two types of analysis tools are needed to estimate CO2 and CH4 fluxes (sources and sinks) from space-based observations:
  Remote sensing retrieval algorithms are used to estimate the XCO2 and XCH4 from space based observations
  Flux inversion models are used to estimate the surface fluxes needed to maintain the observe XCO2 and XCH4 distributions in the presence of the prevailing winds field
Substantial advances has been made in both retrieval algorithms and flux inversion methods over the past decade
  These methods are now being successfully used to study emission hot spots and regional-scale natural CO2 sources and sinks
A substantial amount of additional development is needed to support applications as demanding and diverse as
  supporting urban- to national-scale GHG emission inventories
  monitoring the natural carbon cycle response to climate change
CEOS should work with its partners to meet these needs
Other Needs: Science advances needed to support GHG monitoring

## Slide 16
Create linkages with the ground-based GHG measurement community and stakeholders in the inventory and policy communities (in particular the UNFCCC), to refine the requirements and implementation approach;
Exploit the capabilities of the CEOS member agencies, Coordination Group on Meteorological Satellites (CGMS) and the WMO Integrated Global Greenhouse Gas Information System (IG3IS) to integrate available and planned space-based sensors into a constellation that can provide prototype space-based CO2 and CH4 product in time to inform the bottom-up inventories for the 2023 global stocktake; and
Use the lessons learned from the development of this prototype product to refine the requirements for a future, purpose-built, operational, space-based constellation that more completely addresses the objectives cited above in time to support the 2028 global stocktake.
Proposed CEOS Actions

## Slide 17
The AC-VC GHG White Paper is complete and ready for review by the CEOS SIT Technical Workshop
  This should close Action CARB-12 - White paper on a carbon observation constellation
If the paper and its recommendations are accepted, the next step would be to submit the proposed actions to the Plenary for disposition
If the proposed actions are approved, AC-VC supports the proposal to transfer the implementation responsibility to a (new) CO2/CH4 subgroup within WGClimate
  Already joint working group with CEOS and CGMS
  Side Meeting planned on 12 September to plan details of transition
  AC-VC will continue to support synergistic GHG and atmospheric composition observations and modeling efforts
White Paper Status and Plans

## Slide 18
Options
Continue adhoc collaboration in context of CEOS Carbon Strategy Actions e.g. as-in joint efforts on AC-VC Whitepaper
Establish a sub-group (with dedicated resources) in context of existing standing WG i.e. Joint WG on Climate
Extend the current CEOS Atmospheric Composition Virtual Constellation to be a Joint CEOS-CGMS Virtual Constellation
Establish a dedicated Joint WG specifically on Carbon /GHG observations
Assess/discuss these different options both within CEOS and CGMS - propose a preferred option
CEOS CGMS Coordination on GHG monitoring

## Slide 19
Establish a sub-group with WGClimate

## Slide 20
Extend the current CEOS AC-VC to be a joint CEOS/CGMS VC

## Slide 21
Pros and Cons of Options 3 & 4