## Slide 1
5.01 GHG Summary

## Slide 2: Summary of Topics
The primary focus of the first session greenhouse gas (GHG) day was the status of the pilot CO2 and CH4 inventories being developed to support the first global stocktake
  D. Crisp provided a high level overview of the objectives and deliverables
  B. Byrne summarized the approach and status of the CO2 inventory development effort
  J. Worden and R. Engelen summarized the approach, status, and plans for the CH4 inventory development effort and the long-term plan for an operational GHG flux estimates
The second session was devoted to status reports from operating and planned missions
  Operating missions: GOSAT, GOSAT-2, OCO-2/3, TROPOMI
  Missions in development: MethaneSat, AIM, GOSAT-GW, Carbon Mapper, MicroCarb, CO2M
  Discussion: How do we coordinate the implementation and operations of the public and private GHG satellites to provide the most useful products
    Cross-calibration, Coordinated observations, cross validation, integrated products

## Slide 3: Overall comments on the GST effort
We have made a lot of progress over the past year
  Last year, we had a CO2 product but had not identified a CH4 product. Now, we have two groups collaborating on CH4 products
  We now have a specific plan and schedule for delivering products to the COP-26
A huge amount of progress has been made in quantifying regional to local emissions using combinations of data from different satellites or satellite + aircraft data, where the emissions and their uncertainties are “quite large”
  This is where we have most confidence (or greatest information content) in our results
  Several satellites under development have observation strategies optimized for this
Large discrepancies remain in top-down versus bottom up for global budgets
  For CO2, satellites are providing a 1 Pg / 3 Pg land / ocean CO2 net flux partitioning versus 2/2 for bottom up; resolving this is critical for understanding of Carbon/Climate feedbacks.
  For the methane budget, the wetlands bottom up versus top down estimates have similar disagreements. In addition, bottom up estimates suggests fossil methane emissions are ~100 Tg / yr but isotope data suggest 120 to 140 Tg/yr.

## Slide 4: Overall comments on the GST effort
The products under development have also identified limitations in the current capabilities
  While resolution and coverage are the primary assets of space based products, we still need improvements in those areas
    GOSAT-GW, GeoCarb, CO2M and other future missions will address these needs in many areas
  Space based systems provide poor coverage over persistently cloudy regions and regions at high latitudes that receive little sunlight during winter.
    This emphasizes the need for an enhanced ground-based network in these regions
  Available space-based GHG products also reinforce the need for more accurate retrieval algorithms and inverse modeling systems
    Accuracies in the CO2 and CH4 retrievals needs to be improved as variable biases in the data could potentially explain these top-down/bottom up discrepancies.
    Structural and/or parametric error in global chemistry transport models, or incorrect up-scaling of bottom-up emissions / fluxes could also explain the discrepancies so these high level budget questions are still a science challenge.
We still need to define the best practices for developing and using top-down atmospheric inverse models for informing and validating bottom-up national inventories

## Slide 5: Discussion – Coordination of Public/Private Observations
How can we coordinate measurements of the national/agency and commercial satellites (GHGSat, Carbon Mapper, MethaneSAT)? Is CEOS the best organization for that effort?
  Tight coordination is challenging, OCO-3 uses an automated prioritization tool
  It would be interesting to have some testbed to optimize viewing across multiple assets.
  The GHGSat/TROPOMI collaboration was a grassroots effort that illustrates one model
  Perhaps coordination could benefit from a "tip and queue" working group to devise more optimal strategies (ideally, a coordinated anomaly detection and notification framework).
  It will likely require significant investment in time and resources to make this more operational across diverse systems - but definitely doable.
  Could IMEO help to coordinate the CEOS efforts with commercial efforts for CH4?
  IG3IS might be a more appropriate interface between the national and commercial efforts, but we have not yet explored that option.
  We should encourage support and empowerment of already established programs like IG3IS. Don't have time to reinvent the wheel - or wrangle all the governments again!

## Slide 6: Discussion – Cross Calibration and Cross Validation
Cross-validation of radiances and cross validation of retrieved concentration data from the public and private systems needs attention. Is CEOS the best group for that?
  CEOS WGCV has been primarily on radiance calibration, but has also started to explore the use GHG measurements from commercial aircraft to validate both concentrations and fluxes
  GSICS works with the CEOS WGCV. As mentioned, we have a GSICS Research Working Subgroup focusing on establishing in-orbit calibration for UV, Vis, and NIR spectrometers. http://gsics.atmos.umd.edu/bin/view/Development/WebHome
  Validation is critical. When assimilating different XCO2 retrievals from different instruments, it will be a major challenge to understand how potential differences in biases could impact the inversions.
  AC-VC is also encouraging CEOS Agency members to form a closer relationship with the TCCON, COCCON and AirCore networks to facilitate the cross-validation of XCO2 and XCH4 products
    TCCON works with GAW (as a contributing network) to ensure the traceability to WMO scales