## Slide 1
ALTIUS
status and expected performance
E. Dekemper, and BIRA-IASB’s ALTIUS team
USASK’s ALTIUS team
ESA’s ALTIUS team

## Slide 2
Mission objectives
Mesosphere
Stratosphere
Troposphere
O3
NO2
H2O
aero
OClO
BrO
NO3
T°
limb scattering
stellar/planetary occultations
solar/lunar occultations
still to be evaluated

## Slide 3
Mission concept
On the capability of the ALTIUS data to constrain modelled stratospheric O3
 Errera et al., AMT 14, 2021
Limb-scattering
Solar/Lunar occultations
Stellar/Planetary occultations

## Slide 4
VIS channel |  |  | 
 | bright limb | solar/lunar occultations | stellar/planetary occultations
Field of view | 2° x 2° |  | 
Vertical sampling | 200 m |  | 
Spectral filter technology | acousto-optical tunable filter (AOTF) |  | 
Spectral domain | 440-675 nm |  | 
Spectral resolution | 2-10 nm |  | 
Target species | O3, NO2, aerosols | O3, NO2, aerosols, NO3, | O3, aerosols
UV channel |  |  | 
 | bright limb | solar/lunar occultations | stellar/planetary occultations
Field of view | 2° x 2° | 2° x 2° | 0.2° x 0.2°
Vertical sampling | 600 m | 600 m | 60 m
Spectral filter technology | stack of 4 Fabry-Pérot interferometers |  | 
Spectral domain | 250-355 nm |  | 
Spectral resolution | 2-3 nm |  | 
Target species | O3, T° | O3, BrO, OClO, T° | O3
NIR channel |  |  | 
 | bright limb | solar/lunar occultations | stellar/planetary occultations
Field of view | 2° x 2° |  | 
Vertical sampling | 400 m |  | 
Spectral filter technology | acousto-optical tunable filter (AOTF) |  | 
Spectral domain | 600-1020 nm |  | 
Spectral resolution | 2-10 nm |  | 
Target species | aerosols | aerosols, H2O | aerosols
Mission concept

## Slide 5
Mission status
Space segment CDR closed in June 2024

## Slide 6
Mission status
Platform at Redwire in May 2025.

## Slide 7
Mission status
CCUs (mechanics)
FM manufacturing ongoing
Star trackers
FM ready
NIR & VIS Bench
ready
UV Bench
ready
Baffles
FM under manufacturing
External Harness FM under manufacturing
Radiator
FM procurment to start
MLI
FM available
VIS/NIR cover Use of STM
UV cover Use of STM
Many subsystems are delivered.

## Slide 8
Mission status – UV channel
Mechanism FM Ready
STO M1
To be re-coated
BEO structure
Ready for mirror assembly
FPA
Under manufacturing
Periscope Mirror
Under performance assessment
STO M2
Ready for integration with mount
STO M3
Ready for integration with mount
STO M4
Under re-manufacturing
Folding mirror
StO M5: ready for mount integration BL Fold: Under performance assessment
FPI FM
TRB completed
BEO M1, M2, M3
Under manufacturing
UV Harness
FM available
UV band pass filter
Ready for integration with mount

## Slide 9
Mission status – VIS/NIR channel
VIS/NIR BEO Structure
Ready for assembly
VIS/NIR Mechanism FM
ready
VIS/NIR AOTF Assembly
Delivered
VIS/NIR Periscope Mirror under manufacturing
VIS/NIR BEO Mirrors: NIR mirrors ready
VIS mirrors under manufacturing
FPA
Under manufacturing
VIS/NIR Folding Mirror
Ready for mount integration
NIR FEO structure ready
VIS FEO structure
Under repair
VIS/NIR FEO Mirrors
NIR: integrated VIS: under manufacturing
VIS/NIR Harness
Ready

## Slide 10
Mission status
Fabry-Pérot Interferometer (UV channel) manufactured and characterized by VTT in Finland.

## Slide 11
Mission status
VIS and NIR AOTFs produced by Gooch & Housego in UK.

## Slide 12
Mission status
Space segment CDR closed in June 2024
Payload subsystems integration is starting at OIP (Belgium)
Calibration and characterization will start in 2026 at CSL (Belgium)
Ground segment CDR in progress
Shared launch with ESA’s FLEX is becoming highly hypothetical. Ride share in 2027 being negotiated with AVIO.

## Slide 13
Mission performance verification approaches
System Performance Simulator (SPS)
Based on synthetic data
RTM-generated scenes
L0
(raw images)
Instrument + Satellite Model
L1a
(radiometric corrections)
L1b
(geo-referencing)
L1c
(straylight removal)
L2
Synthetic L1 generator
(spectral convolutions, radiometric noise, images formation)

## Slide 14
System Performance Simulator (SPS)
Based on synthetic data
Based on existing satellite data
RTM-generated scenes
L0
(raw images)
Instrument + Satellite Model
L1a
(radiometric corrections)
L1b
(geo-referencing)
L1c
(straylight removal)
L2
Synthetic L1 generator
(spectral convolutions, radiometric noise, images formation)
Satellite L1 data
Mission performance verification approaches

## Slide 15
Bright limb
OMPS-LP
Solar occultations
SAGE-III
Stellar occultations
GOMOS
Mission performance verification approaches

## Slide 16
Mission performance verification approaches
Satellite instrument L1 file
OMPS-LP: -limb radiance spectra
-solar angles
-satellite position/velocity
GOMOS: -atmospheric transmittance spectra
-1kHz scintillation term
-star ID and TOA spectrum
SAGE-III: -atmospheric transmittance spectra
“Altiusification”
-Creation of a pseudo stimuli
-Replacement of atmospheric parameters (T°, P, O3, etc)
-Update the light source settings (solar angles or star ID)
-Interpolation/extrapolation of the (ir)radiance spectra on the ALTIUS altitude and wavelength grid
ALTIUS SPS
-Simulation of the spectral images at the requested wavelengths (according to an acquisition plan)
-Estimation of measurement errors
-Georeferencing
ISM -> L0 -> L1a -> L1b -> L1c
Satellite instrument L2 file
-O3 profile
-Aerosol extinction coef. profiles
-Temperature
-Pressure
-Albedo
Satellite instrument L2 validation report
-Latitude and altitude-dependent O3 profile random and systematic differences
Source: Ozone CCI+ PVIR v4.0
Performance Evaluation Module (PEM)
-Comparison of the 2 retrieved O3 profiles
-Assessment of significance with respect to the satellite product validation report
Intercomparison report
L2
Processor
O3 profile retrieval

## Slide 17
Limb scattering mode – O3
End-to-end simulations show that the mission (space + ground segment) is currently meeting the primary scientific requirements.

## Slide 18
Limb scattering mode – O3
This is based on L1  L2 sensitivity analyses…
Random errors Systematic errors

## Slide 19
Limb scattering mode – O3
… and on L2 sensitivity analyses (modeling errors, auxiliary data uncertainties, etc).
ALTIUS is not different than other limb scattering instruments, and the driver of the error budget is the uncertainty on the aerosol particles in the atmosphere.

## Slide 20
Limb scattering mode – O3
E2E simulations using OMPS-LP L1 radiances is a complex exercise, as there are many differences between the two instruments:
  Polarisation sensitivity
  Different spectral resolutions
  Imaging vs non-imaging system (and different vertical resolution)
The raw data of ALTIUS take the form of spectral images.

## Slide 21
Limb scattering mode – O3
Still solving issues with O3 cross sections and aerosol model, but results obtained with the OMPS-LP L1 radiances are encouraging.

## Slide 22
Solar occultation mode – O3, kaer , NO2
E2E simulations of solar occultation show no particular difficulty for O3, aerosol extinction, and NO2 retrievals.
Typical performance of an O3 retrieval in solar occultation.

## Slide 23
Solar occultation mode – O3, kaer , NO2
E2E simulations of solar occultation show no particular difficulty for O3, aerosol extinction, and NO2 retrievals.
Typical performance of an aerosol extinction coefficient retrieval in solar occultation.

## Slide 24
Solar occultation mode – O3, kaer , NO2
E2E simulations of solar occultation show no particular difficulty for O3, aerosol extinction, and NO2 retrievals.
Typical performance of an NO2 retrieval in solar occultation.

## Slide 25
Solar occultation mode – O3, kaer , NO2
E2E simulations based on the SAGE-III/ISS L1 transmittances are also performed for testing the solar (and soo the lunar) occultation mode.

## Slide 26
Solar occultation mode – O3, kaer , NO2
Full end-to-end processing of a few SAGE-III occultations
! The SPS takes ages to fabricate the hundreds of spectral images acquired by ALTIUS during the occultation !
O3 retrievals are always in excellent agreement with SAGE-III solution.

## Slide 27
Solar occultation mode – O3, kaer , NO2
Full end-to-end processing of a few SAGE-III occultations
! The SPS takes ages to fabricate the hundreds of spectral images acquired by ALTIUS during the occultation !
O3 retrievals are always in excellent agreement with SAGE-III solution.
Aerosol extinction coefficient at 750nm are also good (now considering to use v6.0 for easier conversions over wavelengths).

## Slide 28
Solar occultation mode – O3, kaer , NO2
Full end-to-end processing of a few SAGE-III occultations
! The SPS takes ages to fabricate the hundreds of spectral images acquired by ALTIUS during the occultation !
O3 retrievals are always in excellent agreement with SAGE-III solution.
Aerosol extinction coefficient at 750nm are also good (now considering to use v6.0 for easier conversions over wavelengths).
NO2 retrievals are not yet ok due to:
Spectral resolution of ALTIUS is at the limit
Spectral gaps in SAGE L1s are filled arbitrarily

## Slide 29
Solar occultation mode – O3, kaer , NO2
Full end-to-end processing of a few SAGE-III occultations
! The SPS takes ages to fabricate the hundreds of spectral images acquired by ALTIUS during the occultation !
O3 retrievals are always in excellent agreement with SAGE-III solution.
Aerosol extinction coefficient at 750nm are also good (now considering to use v6.0 for easier conversions over wavelengths).
NO2 retrievals are not yet ok due to:
Spectral resolution of ALTIUS is at the limit
Spectral gaps in SAGE L1s are filled arbitrarily
Sunrise Sunset

## Slide 30
Stellar occultation mode – O3, kaer , NO2
The stellar occultation mode is struggling with a low SNR.
Star scintillation is more difficult to manage in absence of fast photometers like in GOMOS.
 E2E simulations confirm feasibility with 10 stars + 5 planets.

## Slide 31
Stellar occultation mode – O3, kaer , NO2
The stellar occultation mode is struggling with a low SNR.
Star scintillation is more difficult to manage in absence of fast photometers like in GOMOS.
 E2E simulations confirm feasibility with 10 stars + 5 planets.
Typical synthetic retrieval performance for O3 retrieval.

## Slide 32
Stellar occultation mode – O3, kaer , NO2
E2E simulations based on GOMOS L1 star irradiance spectra are confirming that ALTIUS can will be able to deliver nighttime O3 profiles, and aerosol extinction profiles in case of event.
ALTIUS
GOMOS

## Slide 33
Stellar occultation mode – O3, kaer , NO2
Full end-to-end processing of GOMOS data were achieved with the SPS, and the baseline L2P.
The 10 brightest stars + 5 planets seem feasible.
Achernar
Rigil

## Slide 34
Stellar occultation mode – O3, kaer , NO2
Full end-to-end processing of GOMOS data (O3) were achieved with the SPS (very slow), and the baseline L2P.
Hundreds of occultations of year 2004 were processed. Good agreement is observed down to 20km for O3.

## Slide 35
Stellar occultation mode – O3, kaer , NO2
For aerosol extinction coefficient at 750nm, ALTIUS will be able to contribute when the aerosol loading is moderate: km-1.
Full end-to-end simulation with the SPS, for Sirius.

## Slide 36
Stellar occultation mode – O3, kaer , NO2
For NO2, there is not enough SNR in the stars signal.
Planetary occultations still need to be tested with the SPS.

## Slide 37
Conclusions
ALTIUS space segment is making progresses  calibration in 2026  launch in 2027
The L1 and L2 products performance are assessed with the SPS (instrument perf. simul.)
“Altiusification” of L1s from other limb sounders is helping checking our perf. and algos.
 | O3 | k750 | NO2 | H2O
Limb-scatter | Simul: Real: OMPS-LP | Simul: see USASK Real: see USASK | To be started | In progress
Solar/Lunar occultation | Simul: Real: SAGE-III | Simul: Real: SAGE-III | Simul: Real: SAGE-III | In progress
Stellar occultation | Simul: Real: GOMOS | Simul: >4.10-4km-1 Real: GOMOS | Simul: x Real: x | x
Planetary occultation | Simul: Real: TBD | Simul: Real: TBD | Simul: TBD Real: TBD | ?

## Slide 38
The O3 retrieval game
visit  altius.aeronomie.be/altius-video-game