## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO Mission Status
Xiong Liu1, K. Chance1, C.R. Nowlan1, G. Gonzalez Abad1, R. Suleiman1, J. Houck1, J. Davis1, H. Wang1, H. Chong1, W. Hou1, J. Park1, J. Bak1, L. Carpenter1,
C. Chan Miller1, J. Fitzmaurice1, A. Oppenheimer1, E. O’Sullivan1,
K. Daugherty2, D.E. Flittner2, C. Fenn2, D. Rosenbaum2, C. Brown2, N. Mishra2,
R.T. Neece2 , E. Roback2, J. Strickland2, L. Judd2, P. Rawat2, K. Travis2, J. Carr3,
J. Szykman4, B. Henderson4, L. Valin4, J. Joiner5, Z. Fasnacht5, S. Frith5,
D. Haffner5, E. Knowland5, N. Kramarova5, N. Krotkov5, C. Li5, W. Qin5,
G. Jaross5, C. Seftor5, A. Vasilkov5, E.-S. Yang5, J. Ziemke5, M. Newchurch6,
Naeger6, R. Cohen7, J. Geddes8, J. Herman9, B. Pierce10, R. Spurr11,
S. Kondragunta12, J. Wang13, O. Torres5, H. Zhang12, P. Ciren12,
X. Zhao14, and the TEMPO Team
1Smithsonian Astrophysical Observatory (SAO), CfA
2NASA LaRc 3Carr Astro. 4EPA 5NASA GSFC 6UAH 7UCB
8BU 9UMBC 10UWM 11RT Sol. Inc 12NOAA 13UI 14ECCC
CEOS AC-VC-21
Takamatsu, Japan
June 11, 2025

## Slide 2: Tropospheric Emissions: Monitoring of Pollution
NASA’s first Earth Venture Instrument (EVI-1), selected in 2012
Led by Smithsonian Astrophysical Observatory (SAO) in partnership with NASA LaRC, with instrument built by Ball Aerospace (now part of BAE Systems)
NASA’s first host payload, launched on board Intelsat-40e in April 2023 on to the GEO at 91 ∘ W
Hourly daytime air pollution over North America at neighborhood scale (2x4.75 km2 at the center of the field of regard)
Global Geostationary Air Quality Constellation along with GEMS (2020) and Sentinel-4 (2025)
Credit: NASA’s Scientific Visualization Studio
TEMPO first light RGB and examples of spectra
Credit: Heesung Chong
293-494 nm
538-741 nm

## Slide 3: TEMPO Commissioning and Nominal Operation
Launch
TEMPO
Power On
First Light
TEMPO Commissioning
S/C Activity (TEMPO Off)
Activation
Outgassing
Instrument Characterization and Analysis
PLAR
Nominal Operations
L+61 days (6/7/23)
L+115 days (7/31-8/2/23)
L+194 days
(10/19/23)
L+0 (4/7/23)
TEMPO commissioning: SAO + LaRC + Intelsat + Maxar + Ball + Carr Astronautics
Nominal operation on 10/19/2023: 20 months Baseline mission Phase E until 6/18/2025
NASA approved TEMPO mission extension through 9/2026: further extension via NASA senior review
Successful TEMPO commissioning and nominal operation, instrument performing very well
Trending solar irradiance: 2024/8/1 vs. 2023/8/2
Credit: Heesung Chong

## Slide 4: TEMPO Scanning
Nominal scans: hourly, 2.4M pixels
  2035 North/South pixels
  1181 East/West steps per hour
  2 x 4.75 km2 at center of field of regard
Optimized scans
  Higher temporal resolution scans in early AM and late PM over coasts (40 mins)
Twilights scans
  Performed during darkness (~Aug. 15-Apr. 15)
  City lights, moonlights, Aurora, airglow, gas flaring, lightning, fires
Special observations: can be requested with strong science justification
  High-time scans (5-10 mins) over selected longitudes (several hours, alternate hourly scan/1 hour high-time scans)
  Lunar collect
  RRV 2024/2025 (side slither)
Request special observations at TEMPO Early Adopter Website
Credit: NASA’s Scientific Visualization Studio
Radiance derivation  Post-processing (de-speckling, de-streaking, etc.)  Composite
Clearest-Sky City lights Composite 1–12 February 2024
Credit: Jim Carr

## Slide 5: TEMPO Data Products Public Release NASA’s Atmospheric Science Data Center (ASDC)
Public Release | Date | Details
V01 | Feb. 2024 | Limited 3 weeks released
V02 | Feb. 2024 | Level 1 (spectra) released
V03 | May 2024 | L1 updated, Level 2/3 cloud, NO2, HCHO, total O3 V3 O3 profile (ASDC June 9, 2025, not for the public)
V04 | Aug. 2025 | Release ozone profile, update L1 + other L2/L3
TEMPO data now publicly available at NASA’s ASDC (~6 hours latency).
Multiple tools:
  Earthdata Search, OPeNDAP
  NASA Worldview: all data products (L2+L3)
  ArcGIS services: currently L3 NO2 + HCHO new
  RSIG (EPA)
  TEMPO-Lite (CfA): currently L3 NO2
  NASA SPoRT Viewer
For more information check out:
  User Guides (known issues)
  Daily operation & commissioning logs
  Validation reports (coming soon)
  Algorithm Theoretical Basis Documents (drafts available upon request, L2 ATBDs released)
2 Petabyte of TEMPO V3 data downloaded from Earthdata within 1 year!
ASDC TEMPO

## Slide 6: Baseline TEMPO Data Products
*Beta: “minimally validated”, publication “not recommended and highly discouraged”
*Provisional: “performance demonstrated”, "suitable for scientific publication”
The data products are upgraded to provisional status after the validation team approval in Dec. 2024!
Level | Product | Validation Status
L1 | Irradiance | Provisional
 | Radiance | Provisional
 | Radiance (twilight – city lights) | Provisional
L2 | Clouds | Provisional
 | NO2 | Provisional
 | HCHO | Provisional
 | O3 (total) | Provisional
 | O3 (profile) | Beta June 9, 2025
L3 | L2 gridded to 0.02° × 0.02° | Provisional

## Slide 7: Baseline TEMPO Data Products + SNWG TEMPO NRT + TEMPO Enhanced
Level | Product | Developer
L1 | Irradiance | SAO
 | Radiance NRT | SAO
 | Radiance (twilight – city lights) | SAO
L2 | Clouds NRT | SAO/GSFC
 | NO2 NRT | SAO
 | HCHO NRT | SAO
 | O3 (total) | SAO/GSFC
 | O3 (profile) | SAO
 | TEMPO/GOES-R synergy aerosol product NRT | NOAA
 | C2H2O2 | SAO
 | H2O | SAO
 | BrO | SAO
 | SO2 NRT | NASA GSFC
 | UVAOD | NASA GSFC
 | Aerosol layer height | U. Iowa
 | UVB | NASA GSFC
Baseline Products
Satellite Needs Working Group (SNWG)
Cycle 3 NRT Products (~2-3 hours)
Public release (~Sep. 2025)
SNWG Cycle 4
TEMPO Enhanced Products
To be funded ~Q3 2025
Research Products
  Ocean color
  Vegetation
  Solar induced fluorescence
  City lights/lighting types
  HNO2
  Surface albedo
  Surface concentrations
  Free tropospheric NO2
  Emissions
  IO
  NO3

## Slide 8
Algorithm Updates for V4 (~8/2025)
L1b
  Improve absolute calibration (~10% overestimation in normalized radiance)
  Improve straylight correction
  Improve wavelength calibration (wrt cal. coeff.)
  Improve INR (geolocation)
GEOS-CF (met/a priori): V1  V2
Trace gases and clouds
  NO2 / O2-O2 de-striping
  HCHO reference & background correction
  Improve GLER-based surface albedo
  Fix surface pressure anomaly
Total O3
  Reduce latitude-dependent bias from improved L1b
Profile O3
  Soft calibration & optimization
  Preliminary Validation
wavelength [nm]
Cloud-free
20% cloud cover
 High residuals

## Slide 9
TEMPO AGU Special Collection &
Joint TEMPO/ACX STM 2025
Call for Papers
TEMPO Data Products, Science, and Applications
Submission Deadline: December 31, 2025
Joint TEMPO/ACX STM
SAO, Cambridge, MA
August 19-22, 2025

## Slide 10: Summary and Outlook
TEMPO operations are nominal, and instrument is performing very well.
L1b (including twilights), cloud, NO2, HCHO, total O3 are publicly available and upgraded to provisional status. O3 profile product is operationally produced.
Next version including ozone profile and NRT products expected ~August 2025
Mission extended to September 2026, further extension via Senior Review
Many more TEMPO products to come!
AGU Special Collection “TEMPO data products, science and applications” are open until 12/31/2025.
Thank you!
Acknowledgements: Funding from NASA (TEMPO, NNL13AA09C; SNWG TEMPO NRT, 80MSFC24CA004)