## Slide 1
Zhao-Cheng Zeng (zczeng@pku.edu.cn)
School of Earth and Space Sciences, Peking University, Beijing, China
Mengya Sheng, Shangyi Liu, Jiancong Hua, Yingjun Zheng, Shan Han, Runyi Zhou, Sirui Wu (Peking University)
Lu Lee, Chengli Qi, Feng Lu, Xiuqing Hu (National Satellite Meteorological Center)
Wei Wang (Chinese Academy of Sciences)
Cathy Clerbaux (LATMOS)
CO
NH3
HCOOH
Geostationary Interferometric Infrared Sounder
Atmospheric composition (CO, NH3, and HCOOH) from the Geostationary Interferometric Infrared Sounder (GIIRS)
21st meeting of the CEOS Atmospheric Composition Virtual Constellation (AC-VC)

## Slide 2
The Geostationary Interferometric Infrared Sounder (GIIRS)
FY-4A/GIIRS (launched in Dec 2016), spectra data need re-calibration improvement for AC retrieval;
FY-4B/GIIRS was launched in June 2021 (data available from June 2022)
It was located at 105°E before March 2024, and now at 133°E.
GIIRS scans the Earth in a “step-stare” mode: Each field of view collects16×8 interferograms
One coverage takes about 2.0 hours. 12 maps in a day covers day and night.
Footprint size at Nadir: about 12 by 12 km.
Retrievals of CO, NH3, HCOOH from June 2022 to May 2024 (more is coming). This talk will focus on validation and comparison with exiting datasets.
27 FORs
12 Scans
Detector layout
(16×8 interferograms)
By courtesy of Dr. Lee Lu (NSMC)

## Slide 3
Ammonia (NH3)
Retrievals are avaialble from June 2022 to May 2024, and more is coming
Two major source regions (North China Plain and Northern India)
We see the difference betwee morning and afternoon (filtered by DOFS and TC)
Zeng et al., 2023a, AMT

## Slide 4
Comparison with ground-based FTIR and IASI
GIIRS vs FTIR
GIIRS vs IASI
Hefei
(31.8°N, 117.2°E)
FTIR in Hefei retrieves NH3 column from 2017 to 2023.
Consistent seasonality with high values during summer
GIIRS data have good agreement with FTIR and IASI

## Slide 5
Diel cycle of wildfire CO columns from Southeast Asia
Strong CO emissions transported toward the South China Sea and the Pacific;
The diel cycle represents typical fire emissions caused by changes in temperature/humidity/agricultural activities
Observation sensitivity changes (indicated from AK matrix)
2-hour averages over the SE Asia land
LT: 13 pm
Maps of CO columns every 2-hour in Apr 2023
Zeng et al., 2023b, AMT

## Slide 6
Comparison with TCCON CO
Data collocation: Lat ±0.5° and Lon ±0.5°; Time ± 1 hour;
Convolved with averaging kernel
Good correlation between all TCCON sites;
A systematic difference over the Burgo site, showing GIIRS is overestimating over the region.
TCCON @ Heifei
TCCON @ Xianghe
TCCON @ Burgos
TCCON @ Saga

## Slide 7
Formic Acid (HCOOH)
Zeng et al., 2024, JGR-Atmosphere
HCOOH is an important VOC;
Large enhancement can be seen from wildfires from southeast Asia (Mar and Apr) and Siberia (June);
No ground-based observations are available; Comparison with IASI show good agreement.

## Slide 8
SO2 observations from FY-4B/GIIRS
Covered by GIIRS (<1130 cm-1)
Figures from Carboni et al. (2012)
SO2 absorption feature
GIIRS spectra only cover part of the ν1 weak absorption band
SO2 ν1 (weak absorption band)
SO2 ν3 (strong absorption band)

## Slide 9
SO2 observations from FY-4B/GIIRS (Kanlaon volcano)
Kanlaon (10.4°N, 123.1°E)
12h
14h
16h
18h
20h
22h
0h
02h
04h

## Slide 10
Low Earth Orbit constellation
FY-3D/HIRAS: afternoon orbit (2am/pm)
FY-3E/HIRAS-II: dawn-dusk orbit (5:30am/pm): world’s first for civil use.
FY-3F/HIRAS-II: mid-morning orbit (10am/pm)
Hyperspectral Infrared Atmospheric Sounder (HIRAS)
Dawn-dusk orbit is not optimal for trace gas retrieval (TC can be low)
Hua et al., 2025, RSE
Wildfire emissions during dawn-dusk from FengYun-3E/HIRAS

## Slide 11
Conclusions
FY-4B/GIIRS provide measurements of CO, NH3, HCOOH over East Asia;
Comparison with ground-based observations or IASI (when available) shows good agreement in general;
GIIRS in IR is complementary to GEMS in UV/VIS, a synergy of the two allows the study of (NH3+NO2).
FY-4C/GIIRS, planned to launch in late 2025. The combination of FY-4B and FY-4C will provide better coverage and higher frequency observations.
Data availability:
The GIIRS L1 spectra are publicly available from the National Satellite Meteorological Center: http://satellite.nsmc.org.cn/portalsite/.
Early portion of CO, NH3, HCOOH, and Ozone are publicly available online, links are provided in the related papers; Full 2-year datasets are available (zczeng@pku.edu.cn). The recent data are in processing.
Thank you for your attention!
Acknowledgement:
National Science Foundation of China;
IASI data (https://iasi.aeris-data.fr/);
ECMWF ERA5 (https://cds.climate.copernicus.eu/);
TCCON (https://tccondata.org/);