## Slide 1: High Resolution AI/ML Trace Gas Products from PACE OCI
Zachary Fasnacht1,2, Joanna Joiner2, Eric Bucsela1,2, Matthew Bandel1,2
Sergey Marchenko1,2, Lok Lamsal3, Can Li2, Nickolay Krotkov2
1SSAI, 2NASA GSFC, 3Dept of Interior - BOEM,
***Paper accepted by ERL

## Slide 2: Motivation
NO2 sources are both natural (wildfires, soil, lightning) and anthropogenic (burning of fossil fuels, biomass burning)
NO2 has adverse health effects and contributes to the formation of aerosols and tropospheric ozone
NO2 impacts ocean color algorithms. Errors under high loading (1x1016 mol cm-2) of 10-20% in water leaving radiance (Ahmad et al., 2007).
2021 annual averaged TROPOMI troposphere NO2 column (courtesy Lok Lamsal)
Can we retrieve NO2 accurately with PACE OCI and if so, can it provide value-added data for the atmospheric chemistry community (for downscaling emissions, etc)?

## Slide 3: Heritage Trace Gas (NO2) Instruments
 | Spatial Res. at nadir | Spectral Res. | Spectral Range | Orbit
OMI | 13x24km2 | 0.42-0.63nm | 264-504nm | Polar
TROPOMI | 3.5x5.5km2 | 0.25-0.55nm | 267-499nm 661-786nm 2.3-2.389um | Polar
TEMPO | 2x4.7km2 ** | 0.6nm | 290-490nm 540-740nm | Geo
PACE OCI | 1km2 | 5nm | 315-895nm | Polar
Traditional trace gas satellite instruments (OMI, TROPOMI, TEMPO) have lower spatial resolution (~10x coarser) than PACE OCI, but higher spectral resolution
Previous ocean color multi-spectral instruments such as MODIS and VIIRS have spectral resolution of 20nm+, too coarse for NO2 retrievals
**Spatial resolution at center of field of regard

## Slide 4: Basic approach
Approach is purely data driven with trained model only using PACE OCI measurements as input
Model trained using ~10% of TROPOMI data from random 10 days per month
Current model trained globally for land scenes, NO2 model over water is still in development

## Slide 5: Comparison with Pandora NO2
Provided by Eric Buscela
Comparisons with Pandoras from U.S. sites (stars on TROPOMI NO2 map to left) shows similar results as the TROPOMI comparison (ML model will only do as well as the data it’s trained on)
TROPOMI May 2024

## Slide 6: Weekend vs Weekday NO2 in LA Metro
Air quality in LA region is heavily dominated by vehicular traffic leading to a significant weekend/weekday effect as seen in NO2 retrievals on right
Unlike TROPOMI and TEMPO, with PACE OCI spatial resolution we can begin to see individual highways, particularly in heavy vehicular traffic such as Monday April 29

## Slide 7: NO2 in Eastern Saudi Arabia
NO2 in eastern Saudia Arabia is elevated due to many power plants and manufacturing plants in the region
  P: Power Plant
  C: Cement Factory
  D: Desalination Plant
  S: Steel Factory
PACE OCI shows better defined NO2 plumes such as to the north where there are two power plants and a cement factory (dashed circle)

## Slide 8: Downscaled Monthly NO2 in France September 2024
PACE OCI 0.5km Resolution
TROPOMI 1km Resolution
Monthly NO2 from PACE OCI provides much finer detail of smaller cities, highways, and terrain
Pyrenees Mountains
Toulouse
Bordeaux
Nantes
Lyon
Paris
Caen
Rennes
Alps
Massif Central
Pyrenees Mountains
Toulouse
Bordeaux
Nantes
Lyon
Paris
Caen
Rennes
Alps
Massif Central

## Slide 9: Downscaled Monthly NO2 in Canada May 2024
PACE OCI 1km Resolution
TROPOMI 5km Resolution

## Slide 10
Applying Approach to Retrieve Ozone from PACE
May 21, 2024
Similar PCA+NN approach applied to retrieve ozone from PACE OCI, utilizing ozone retrievals from TROPOMI as truth
OCI also provides the opportunity to retrieve ozone with coverage down to 315nm
Calibration of OCI below 340nm is more uncertain, but ozone results suggest there is useful information in these shorter OCI wavelengths
Potential for improved tropospheric ozone at 1-2km resolution?

## Slide 11: Potential Applications and Future Work
Applications
Improved spatially resolved emissions estimates
Better resolved exposure estimates
Improved ocean color retrievals
Improved chemistry-transport modeling
Spatial downscaling of TEMPO hourly measurements (complementary)
Future Work
Expanding approach to include water scenes
More validation with aircraft as well as ground-based
Develop approach for tropospheric NO2