## Slide 1: Atmospheric Mission Performance Cluster (ATM-MPC) Sentinel-5 Precursor TROPOMI Validation Update
  J.-C. Lambert, S. Compernolle, Arno Keppens, B. Langerock, T. Verhoelst (BIRA-IASB),
  D. Stein-Zweers (KNMI), A.Dehn (ESA),
  D. Hubert, Y. Geunes, J. Granville, O. Rasson, I. De Smedt, T. Ooms, G. Pinardi, M.K. Sha, N. Theys, C. Vigouroux (BIRA-IASB),
  A.M. Fjæraa (NILU), S. Niemeijer (s[&]t), A. Argyrouli, M. Coldewey-Egbers, K.-P. Heue, P. Hedelt, G. Lichtenberg, R. Lutz, F. Romahn (DLR),
  D. Balis, K. Garane, ML. Koukouli, K. Michailidis, A. Pseftogkas (AUTH), S. Beirle, T. Wagner (MPI-C),
  J. Claes, M. de Graaf, H. Eskes, E. Loots, E. van der Plas, J. van Geffen (KNMI), K.-U. Eichmann (IUP-UB), M. Alparone, C. Zehner (ESA)

## Slide 3: Fiducial Reference Measurements and Other Validation Data
S5P data Product | Mission requirements Systematic Random |  | Fiducial Reference Measurements and other ground-based data sources | Satellite data sources
L1B radiance & irradiance | band dependent |  | PICS based monitoring | OMPS-NP, OMPS-NM
O3 total column | 5% | 2.5% | Brewer, Dobson, ZSL-DOAS, PGN | OMI, GOME-2
O3 vertical profile | 30% | 10% | ozonesonde, DIAL (strato+tropo) | OMI, GOME-2
O3 tropospheric column | 25% | 25% | ozonesonde | OMI, GOME-2
NO2 stratospheric column | 10% | 0.5 e15 | NDACC ZSL-DOAS | OMI, GOME-2
NO2 tropospheric column | 50% | 0.7 e15 | NDACC MAX-DOAS | OMI, GOME-2
NO2 total column | - | - | PGN | OMI, GOME-2
SO2 total column SO2 layer height | 30% - | 30% - | MAX-DOAS, PGN - | OMI, OMPS-NP IASI-B, IASI-C, CALIPSO
HCHO total column | 80% | 1.2 e16 | MAX-DOAS, NDACC FTIR, PGN | OMI, GOME-2
CO total column | 15% | 10% | NDACC FTIR, TCCON, COCCON | GOSAT-2, OCO-2
CH4 total column | 1.5% | 1% | NDACC FTIR, TCCON, COCCON | GOSAT-2, OCO-2
Cloud Fraction | 20% | 0.05 | FRM not available | VIIRS, OMI, GOME-2
Cloud Height (pressure) | 20% | 0.5 km | CLOUDNET lidar/radar | VIIRS, OMI, GOME-2
Cloud Optical Thickness | 20% | 0.05 | FRM not available | VIIRS, OMI, GOME-2
Aerosol Absorbing Index | 1 AAI | 0.1 AAI | FRM not available | OMI, OMPS-NP
Aerosol Layer Height | 100 hPa | 50 hPa | EARLINET lidar | CALIPSO, VIIRS, GOME-2
Colour code: automated production of S5P QIs by the VDAF-AVS manual data collection and/or validation
FRM not available, quality evaluation mainly via diagnostics and satellite data intercomparisons
Monitoring Networks
ESA FRM Programme

## Slide 4: VDAF-AVS: Automated comparison to ground-based networks and permanent reporting of S5P TROPOMI L2(+) data Quality Indicators
https://mpc-vdaf-server.tropomi.eu
Total SO2 column

## Slide 5: L1B Radiance, Irradiance and Reflectance Stability Coordinator: Emiel van der Plas (KNMI) Contributors: Melanie Coldewey-Egbers (DLR), Erwin Loots (KNMI)
  Example: Analysis of long-term stability of L1B V02.01.00 cloud-free reflectance over ~20 CEOS Pseudo-Invariant Calibration Sites (Saharan Desert and Arabian Peninsula) in band 3 and band 4
  Results: L1B v02.01.00. reflectance over PICS stable for both band 3 and band 4. Long-term drift <0.5% over the current lifetime of TROPOMI
Reflectance BAND 4
Reflectance BAND 3

## Slide 6: Validation of S5P Cloud Products as Major Influence Quantities for Other S5P Data Products
S5P ALH
S5P O3 trop VCD
S5P O3 OFFL total VCD
S5P HCHO trop VCD
S5P NO2 trop & strat & total VCD
S5P CLOUD
S5P FRESCO
Radiometric cloud fraction
Cloud pressure/height
S5P OCRA/ROCINN_CAL
Radiometric cloud fraction
Cloud top pressure/height
Cloud optical thickness
S5P OCRA/ROCINN_CRB
Radiometric cloud fraction
Cloud pressure/height
Cloud albedo
S5P SO2 VCD
S5P O3 NRTI total VCD
S5P O3 profile
S5P CH4
Back-up cloud mask
Cloud products are used by other S5P products
to mask pixels that are too cloudy for use
to account for cloud (radiative) effects in trace gas and aerosol data retrievals
O3
NO2
SO2
HCHO
aerosol
CHOCHO
BrO
CH4
CO

## Slide 7
L2_CLOUD Lidar/radar
V2.6.1
Vs. ACTRIS-Cloudnet networks of cloud lidars & radars
Cloud parameters scrutinized
Top and mean heights, fractional cover, optical thickness
Processors: OCRA/ROCINN CAL & CRB, FRESCO
Validation particulars
Low/middle cloud fraction with focus on AQ and O3 retrievals
Vs. OPERATIONAL network ACTRIS-Cloudnet
Vs. satellites: OMI, VIIRS
Effects of S5P OCRA cloud fraction version changes
Cloud Properties Validation Coordinator: Steven Compernolle (BIRA-IASB). Contributors: Ronny Lutz, Athina Argyrouli, Victor Molina Garcia (DLR),
Maarten Sneep (KNMI)

## Slide 8
Cloud Properties Validation Coordinator: Steven Compernolle (BIRA-IASB). Contributors: Ronny Lutz, Athina Argyrouli, Victor Molina Garcia (DLR),
Maarten Sneep (KNMI)
FRESCO v1.3
v1.4
v2.2-2.3
Comparison using low clouds: most relevant for trace gas data retrieval
S5P FRESCO upgrade v1.4:
cloud height increase from Cloudnet ~cloud base height to in-between mean height and top height
S5P NO2 vs PGN Pandora
lower bias in S5P NO2

## Slide 9: O3 Column Validation Coordinator: Tijl Verhoelst (BIRA-IASB) Contributors: Katerina Garane (AUTH), Klaus-Peter Heue (DLR)
S5P vs. Brewer Network
S5P OFFL vs. S5P NRTI

## Slide 10
Tropospheric O3 Column Validation Coordinator: Daan Hubert (BIRA-IASB) Contributor: Klaus-Peter Heue (DLR)

## Slide 11: Ozone Profile Validation Coordinator: A. Keppens. Contributors: D. Hubert, J.-C. Lambert
Key validation results
  5-6 DFS with dependence on SZA and slant column
  7-15 km effective vertical resolution
  Altitude: ~10 km offset towards surface and upper stratosphere
  Bias: 5-15 %, oscillations in stratosphere
  Dispersion: 20-30 % below TP, 5-10 % above
  Uncertainty underestimated by factor ~2 below tropopause
  Lat.-dependent drift, highest in mid-latitude troposphere, negative in stratosphere, negligible integrated drift
  Integrated profile consistent with ozone column (~5 % diff.)
  Slight striping along orbit
  Poorer retrieval quality around Antarctic
OFFL, DDS sampling
DDS v2.8
2018/05-2024/12

## Slide 12: NO2 (Partial) Columns Validation Validation coordinator: K.-U. Eichmann (IUPB) Contributors: S. Compernolle, G. Pinardi, and T. Verhoelst (BIRA-IASB), H. Eskes, J. van Geffen (KNMI)
total
S5P vs. MAXDOAS  tropospheric NO2
S5P vs. NDACC ZSL-DOAS  stratospheric NO2
S5P vs. PGN  total NO2

## Slide 13: Open issue in L2_NO2  Need for mission reprocessing
MAR/APR/MAY 2019-2024
RES: 0.05°
COL =
FRESCO version change
NO2 trop VCD
Cloud pressure

## Slide 14: HCHO Column Validation Validation coordinator: K.-U. Eichmann (IUPB). Contributors: S. Compernolle, I. De Smedt, G. Pinardi, C. Vigouroux (BIRA-IASB)
Processor version 02.07.00 OFFL + 02.04.01 RPRO
S5P vs. NDACC MAX-DOAS
S5P vs. NDACC FTIR
Bias, (Dispersion):
  FTIR [clean <2.5 Pmolec/cm2] 30%, (9 Pmolec/cm2)
  [polluted >8 Pmolec/cm2] -30%, (25 Pmolec/cm2)
  MAX-DOAS -37%, (<10 Pmolec/cm2)
  PGN -31%, (9.6 Pmolec/cm2)
  OMI [polluted >5 Pmolec/cm2] (3%, <7 Pmolec/cm2)
S5P vs. PGN

## Slide 15
SO2 Column Validation
Validation coordinator: T. Wagner (MPI-C) Contributors: N. Theys, S. Compernolle (BIRA-IASB)
Switch to COBRA retrieval algorithm
Validation example using routine PGN measurements
Results from the Sentinel-5P MPC Validation Server
The standard deviation of the SO2 is largely reduced after the switch to COBRA
(results for measurements close to the equator)
The switch to COBRA gets smaller (and less negative values) of the TROPOMI SO2 VCds.
There are still several cases where TROPOMI VCDs are higher than the pandora values.

## Slide 16
SO2 Layer Height Validation Validation coordinator: T. Wagner (MPI-C) Contributors: A. Pseftogkas, M. Koukouli, K. Michailidis (AUTH)
Daily mean TROPOMI (y-axis) and IASI/MetopB&C SO2 LH during volcanic eruptions of the September-November 2024 period.
Relatively good agreement between TROPOMI and IASI, but IASI results are systematically higher (~3km for all eruptions; ~1.5 km for strong eruptions)
Often trajectory results agree better with TROPOMI than with IASI (0.5 – 0.7 km)

## Slide 17: CO and CH4 Columns Validation Validation coordinators B. Langerock and M. K. Sha (BIRA-IASB)
NDACC
TCCON
TCCON

## Slide 18
Aerosol Index Validation Validation coordinator: T. Wagner (MPI-C) Contributors: D. Stein Zweers (KNMI), O. Torres, C. Ahn (NASA)
Within requirements
Slight downward trend (2021-July to present) appears to be partly aerosol-physically-driven, and partly instrument-related. Investigations with the L1 team are ongoing
354/388 nm
340/380 nm

## Slide 19
For the version (02.06 OFFL) especially over land the results are much improved:
Mean Bias over Ocean: 1.46 ± 1.69 km
Mean Bias over Land: -0.49 ± 1.33 km
The scatter is increased compared to earlier versions
For the latest updated version (02.07, 02.08 OFFL) over land the results are:
Mean Bias over Land: -0.57 ± 0.63 km
(Results for EARLINET stations - ongoing)
Aerosol Layer Height Validation
Validation coordinator: T. Wagner (MPI-C)
Validation contributors: M. de Graaf (KNMI), K. Michailidis , M-E. Koukouli (AUTH)
Validation against ground-based EARLINET lidars
Top: TROPOMI ALH (v02.06) against EARLINET data for May 2018 to August 2024. Colour-scale indicates TROPOMI retrieved UVAI (388/354nm), vertical error bars indicate the standard deviation of the spatial average of the TROPOMI ALH pixels. Bottom: Histogram of absolute difference between TROPOMI and EARLINET ALHs.

## Slide 20: S5P TROPOMI Routine Validation Service Portal
Up-to-date quality information on TROPOMI L1B and L2(+) data
Routine Operations Validation Platform https://mpc-vdaf.tropomi.eu
Search engine to browse
results by processor
versions, networks etc.
To the Automated
Validation Server
Results and resources by product
Direct access to quarterly report