## Slide 1: PEGASOS & GEO-RING: Consistency TEMPO-GEMS-S5p
Ronny Lutz1, Arno Keppens2 and the PEGASOS and Geo-Ring teams
1German Aerospace Center (DLR), 2Royal Belgian Institute for Space Aeronomy (BIRA-IASB)
AC-VC #21, Takamatsu (Japan) & online, 9-13 June 2025

## Slide 2: PROJECT overview

## Slide 3: Validation initiatives for GEO observations
PEGASOS Phase 1 (2023-2024)
GEMS
PEGASOS Phase 2 (2025-2026) & Geo-Ring Phase 1 (2025)
GEMS
TEMPO
Future
Sentinel-4

## Slide 4: PEGASOS consortium Product Evaluation of GEMS L2 via Assessment with S5P and Other Sensors
DLR
  German Aerospace Center
  Remote Sensing Technology Institute
AUTH
  Aristotle University of Thessaloniki
  Laboratory of Atmospheric Physics
BIRA-IASB
  Royal Belgian Institute for Space Aeronomy
IUP-UB
  University of Bremen
  Institute for Environmental Physics
ESA - ESRIN

## Slide 5: Geo-Ring consortium Validation of Environmental Satellites and Air pollution Studies in the Northern Hemisphere through the Geo-Ring International Collaborative Research
Yonsei University
  Dept. of Atmospheric Sciences
  Atmospheric Radiation Laboratory
SAO
  Smithsonian Center for Astrophysics
  Atomic and Molecular Physics
BIRA-IASB
  Royal Belgian Institute for Space Aeronomy
DLR
  German Aerospace Center
  Remote Sensing Technology Institute
NIER

## Slide 6: L2 products evaluated by PEGASOS & Geo-Ring
PEGASOS Phase 1: all of the above
SO2 and BRF no longer in PEGASOS Phase 2 + Geo-Ring
Additional in Geo-Ring: HONO + HCHO retrieval improvement
Ozone
total
tropospheric
profile
Sulfur
dioxide
total
Nitrogendioxide
total
Clouds
fraction
height
Aerosols
index
layer height
Formaldehyde
total
Surface properties
BRF

## Slide 7: Main objective
Evaluation of and L2 data products using
LEO | GB FRM
TROPOMI / S5P | Brewer
OMI / Aura | Dobson
GOME-2 / MetOp | Ozonesondes
IASI / MetOp | FTIR
VIIRS / S-NPP | MAX-DOAS
CALIOP / CALIPSO | PGN
AMI / GK-2A | NDACC

## Slide 8: selected highlights

## Slide 9: Total Ozone Team: K. Garane, T. Verhoelst, K.-P. Heue, S. Compernolle
Results:
3.5 years of GEMS O3T v2.0 data showed:
Mean relative bias w.r.t. ground-based stations and other satellite missions: -1.8 %
Pearson correlation coefficient ≥ 0.85 (0.97 – 0.99 for the PGN co-locations), showing a very good agreement between GEMS and the reference measurements
North – South gradient with an annual cycle:
Very good agreement during spring, summer and autumn months (± 1%).
During winter months and for higher latitudes GEMS underestimates total ozone by up to -4%
The mean percentage difference between the O3T observations from GEMS and other satellite missions (left → OMI, middle→ S5P, right →GOME2C), over the GEMS FOV.
Left: Hemispherical time-series of the mean relative bias (%) of GEMS O3T observations w.r.t. ground-based reference measurements from Brewer stations within the GEMS FOV.
Right: the same, for the Tsukuba station, Japan, also showing O3T v2.1

## Slide 10: NO2 Team: K.-U. Eichmann, G. Pinardi, S. Compernolle, T. Verhoelst, S. Seo
Results:
MAX-DOAS (11 stations) tropospheric NO2 (V2): median bias 2.3 Pmolec/cm² (23.3%) and network dispersion 3.9 Pmolec/cm² (34%). V3 shows an absolute reduction in bias (~30%) and dispersion.
PGN (10 stations) total NO2 (V3): median bias ~0.04 Pmolec/cm² and network dispersion 5.6 Pmolec/cm². This is a clear improvement over V2
TROPOMI vs GEMS NO2 V3: negative GEMS bias over Ocean removed and high bias over polluted scenes reduced wrt V2.
Comparison of GEMS V3 - TROPOMI total/tropospheric NO2 differences for 2023.
Total
Troposphere

## Slide 11: Clouds Team: R. Lutz, V. Molina García
Results:
comparisons based on: TROPOMI, CALIOP
good agreement for cloud fraction: corr: 0.87, mean diff: 0.04
ok agreement for cloud pressure: corr: 0.65, mean diff: -50 hPa
deviations appear over bright surfaces, for low cloud coverages and extreme viewing zenith angles
Comparison with TROPOMI/S5P cloud fraction (left) and cloud pressure (right) for June and December 2021.
Comparison with CALIOP on 10 June 2023.

## Slide 12
Results:
Overestimation of the GEMS AAI
The inter-comparisons appear to have high dependency on the event and the sensors (e.g. the wavelength pair)
Better agreement between S5P/TROPOMI and GEMS
Inter-comparisons of the GEMS L3 AAI (0.5x0.5 grid) between the respective S5P-TROPOMI (left) and GOME-2C (right) datasets, for specific dust events
Aerosol Index Team: P. Fountoukidis, M.-L. Koukouli, K. Michailidis, D. Balis

## Slide 13
Pixel-to-pixel comparisons (Quality flags applied)
L2 and L3 gridded data are used – S5P: [0.2° x 0.2°] / GOME2: [0.5° x 0.5°]
GEMS vs TROPOMI
GEMS vs MetOp
Dust Event
Results:
GEMS ALH vs TROPOMI ALH | L2
GEMS ALH vs GOME2/MetOp [B+C] AAH | L2
Aerosol Layer Height Team: K. Michailidis, P. Fountoukidis, M.-L. Koukouli, D. Balis

## Slide 14: HCHO Team: K.-U. Eichmann, I. de Smedt, C. Vigouroux, G. Pinardi, S. Compernolle, T. Verhoelst
Results:
TROPOMI: V2 GEMS HCHO has a low bias with a more negative bias towards the West. Overall bias < -60 %, dispersion 2.4 Pmolec/cm².
FTIR (4 stations): V2 GEMS median bias < -67%, dispersion < 5.6 Pmolec/cm²
MAX-DOAS (10 stations): V2 GEMS median bias -25%, dispersion 2.7 Pmolec/cm²
Monthly mean HCHO differences of GEMS V2 and TROPOMI (June 2024).
GEMS mean HCHO (V2) bias for the 4 FTIR sites.
Box-whisker plots of GEMS V3 median HCHO [%] at MAX-DOAS sites and the effect of smoothing.

## Slide 15: Ozone (tropospheric) Team: K.-P. Heue, D. Hubert
Results:
Based on version 2.0
Bias 30-40% relative to S5P and GOME_2
  Within the tropics (up to 20°S)
  Confirmed by sondes in Hong Kong and Kuala Lumpur
Lower bias over Korea relative to sondes

## Slide 16: Ozone (profile) Team: A. Keppens, D. Hubert, J.-C. Lambert
Results:
GEMS O3P v3 information content:
Mostly off-diagonal sensitivity
DFS ~1.5 from lower stratosphere (15-30 km)
5-10 km effective vertical resolution (FWHM)
GEMS O3P v3 uncertainty:
Order of 5-10 % negative bias and 10 % dispersion in lower stratosphere
10-20 % positive tropospheric bias & dispersion (increase in UTLS)
AK smoothing systematically reduces tropospheric uncertainties
Clear effect of clouds and SZA / VZA
Bak et al. “GEMS ozone profile retrieval: impact and validation of version 3.0 improvements” under review for AMT.
GEMS L2 v3 ozone profile data in comparison with vertically smoothed ozonesonde data from four stations (2021/03 – 2023/12)

## Slide 17: GEMS HONO & HCHO retrieval improvement Team: N. Theys, I. de Smedt
Aim:
Support development of GEMS HONO retrieval, based on previous collaboration between BIRA-IASB and NIER
Strengthening collaboration on HCHO
Work:
Assessing and evaluating products for HONO, propose improvements and support implementation of algorithms by performing tests and comparison against TROPOMI and possible other datasets
Similar assessment for HCHO with focus on how to improve the spectral fitting and background correction
Southeast Asia 2021 burning season (March-April)
Theys et al., JGR-A, 2025

## Slide 18: Credits to the GEMS and TEMPO teams!
We appreciate the good collaboration with the GEMS L2 product developers in Phase 1
We look forward to a good collaboration with the TEMPO L2 product developers in Phase 2

## Slide 19
Comments or questions? ronny.lutz@dlr.de / arno.keppens@aeronomie.be
Thank you for your attention!