## Slide 1: Validation and support of space-based measurements with the Pandonia Global Network of ground-based spectrometers Thomas Hanisco1, Alexander Cede1,3,5, Nader Abuhassan1,2,3, Stefano Casadio4, Limseok Chang6, Angelika Dehn4, Emma Knowland7, Elena Lind1,Apoorva Pandey1,2, Bryan Place1,3, Alberto Redondas8, James Szykman9, Martin Tiefengraber5, Luke Valin9, Michel van Roozendael10, and Jonas von Bismarck4 1NASA Goddard Space Flight Center, Greenbelt, Maryland, USA 2University of Maryland Baltimore County, Maryland, USA 3SciGlob, Columbia, MD, USA 4Earth Observation Ground Segment Department, ESA / ESRIN, Frascati, Italy 5LuftBlick, Innsbruck, Austria 6National Institute of Environmental Research, Incheon, Korea 7NASA Headquarters, Washington, DC, USA 8AEMET- Meteorological State Agency, Spain 9EPA Research Triangle Park, Charllotte, NC, USA 10BIRA-IASB, Brussels, Belgium
11-June, 2025
CEOS AC-VC meeting

## Slide 2: Pandonia Global Network
Calibration and Quality Assurance:
  Laboratory and Field calibration of instruments
Network operation
  Remote monitoring and repair of instruments
Retrievals
  Production of O3, SO2, NO2 and HCHO Columns/Profiles
The PGN operates 185+ Pandora instruments
https://www.pandonia-global-network.org/
Thomas.Hanisco@nasa.gov, alexander.cede@luftblick.at

## Slide 3: Pandora measurements
Direct sun: mostly BEER’s Law.
Total absorption used to derive the column abundance between the instrument and the top of atmosphere
MAX-DOAS: multiple angle BEER’s Law
Differential measurements used to derive the abundance at multiple elevations

## Slide 4
Pandonia Global Network
            185+ Official instruments
            Unofficial
            Adding 30/year
TEMPO
SENTINEL-4
GEMS
Notes: Buenos Aires and Rivadiva, Antarctica Trollhausen, Ann Marie Fjaera NILU

## Slide 5
Notes: Added Actris not up to date

## Slide 6
6
6
6
PGN Real Time Data: BlickV http://blickv.pandonia-global-network.org/
All products are available for download on BlickV.
Quality assured total column NO2 and O3 are archived at the EVDC.
“Out of the Box” MAX-DOAS products provided without a field calibration.
Stan State - 248

## Slide 7: PGN NO2 total columns (DS) and profiles (MAX)
4 minutes in Innsbruck, Austria
High precision allows high frequency measurements to reveal small scale variability
Pandora 106, 234, PI: Martin Tiefengraber
Extended AMF validity due to effective temperature and height estimation from stratospheric climatology
Pandora 65
PI: Michel Grutter
1 day at Altzomoni (~4000 m.asl), Mexico City

## Slide 8: PGN O3 total column (DS)
Upcoming version retrieves effective O3 temperature instead of using a climatology
O3 temperature
O3 column
(clim. O3 temp.)
(retr. O3.temp.)
Pandora 142
PI: Michel Grutter
Increasing O3 temperature over the day points to tropospheric O3 accumulation

## Slide 9: PGN SO2 total column (DS)
High precision data allows to monitor
background signals and volcanic emissions
Correlation with NO2 suggests anthropogenic SO2
SO2
NO2
Pandora 101 PI: Alberto Redondas
Pandora 159, PI: Refilwe Kai
Cumbre Vieja eruption as seen at Izana, Tenerife
Coal power plant emissions in Wakkerstroom, South Africa

## Slide 10: PGN HCHO total columns (DS) and profiles (MAX)
PGN still underrepresented in biomass-burning areas.
Apoorva Pandey, NASA
Slope=1.14
Intercept=1.7e15
R2=0.79
MAX-DOAS HCHO column [molec/cm2]
DS HCHO column [molec/cm2]
A portion of the free tropospheric column is potentially not seen by MAX-DOAS

## Slide 11: PGN H2O total columns (DS) and profiles (MAX)
H2O - a dynamic tracer
Extreme dryness at Antarctica (Troll station)
O3
vortex intrusion of NO2 rich air?
NO2
H2O
(hole)
H2O
O3
NO2
Dry air advection with O3 increase and NO2 decrease in Athens, Greece
Pandora 242, PI: Ann Mari Fjaeraa
Pandora 119, PI: Stelios Kazadzis

## Slide 12: Expansion programs
EPA 25+ instruments
United Nations UNESCAP/KOICA/NIER: 23 instruments in southeast ASIA.
    Completed all installations in 2024
NASA IPMSI – 13 instruments
  Completed in 2024
NASA Satellite needs Working Group (SNWG)
  10 US department of Agriculture rural sites – 4/10 installed
  20 US State Department embassy locations 2/20 installed
    10 selected and in progress
    10 additional in 2026-2027
Guatemala City, Guatemala | Kigali, Rwanda
Beijing, China | Willemstad, Curacao
Cairo, Egypt | Ashgabat, Turkmenistan
Skopje, Macedonia | Addis Ababa, Ethiopia
Antananarivo, Madagascar | Nairobi, Kenya
Notes: Shobha Kondragunta at NOAA Bojan Bokov at Eumetsat

## Slide 13: SNWG: Produce localized NO2 forecasts by combining PANDORA observations with GEOS model output
Pandora observations
GEOS-CF model output + machine learning
Adapt ML method developed for surface observations (Christoph Keller et al., ACP 2021)
Method is limited to locations with at least 1 year of historical data
PGN +
GEOS_CF trop columns -> Surface concentration
PI Emma Knowland, NASA HQ

## Slide 14: “Standard” Model Forecasting of Surface Ozone
Emma Knowland and Carl Malings

## Slide 15: Measurement-ML Model Forecasting of Surface Ozone

## Slide 16: Next steps
Technology development
  Low stray-light spectrometer
Validation studies
  CINDI-3 ground-based
  SARP airborne in situ
  Balloon and drone in situ
New retrievals
  V1.9 with stratospheric temperature
SNWG-2026
  Forest fire locations (up to 20)
Notes: Shobha Kondragunta at NOAA Bojan Bokov at Eumetsat