## Slide 1: Uptake of satellite data in the CAMS system
Antje Inness (ECMWF)
With thanks to the ECMWF CAMS team
AC-VC#21 meeting - 11 June 2025

## Slide 2: Copernicus Atmosphere Monitoring Service (CAMS)
Within the 6 Copernicus Services, the CAMS mandate is to deliver consistent and quality-controlled information related to the chemical composition of the atmosphere, its drivers (air pollutants and GHG) and its impact on air quality and health, solar energy, climate forcing, in Europe and everywhere in the world.
Air quality
Policy tools
Solar energy
Ozone layer and UV radiation
Emissions and surface Fluxes
Climate forcing
Air quality

## Slide 3: CAMS integrated framework
Data assimilation
Satellite Observations
(AOD, O3, CO, NO2, SO2,CH4,CO2)
ECMWF
IFS
global,
40x40 km
11 regional CTMs over Europe,
10x10 km
Boundary Conditions
Surface AQ observations
Data assimilation
European CAMS
Emissions
Global
CAMS Emissions
GFAS
wildfire emissions

## Slide 4: AC observations used in global NRT CAMS system
Species | Instruments
CAMS NRT | 
O3 | S5P, GOME-2, OMI, OMPS-NP, MLS, OMPS-LP, GEMS, TEMPO
CO | S5P, IASI, MOPITT
NO2 | S5P, GOME-2, GEMS, TEMPO
Aerosol | MODIS, VIIRS, PMAp, S3
CO2 | GOSAT, IASI, OCO-2
CH4 | GOSAT, IASI, S5P
SO2 (volcanic) | S5P, GOME-2, IASI
SO2 (anthropogenic) | S5P
HCHO | S5P, GEMS, TEMPO
GFAS fire emissions | MODIS, VIIRS, GOES, S3
---- Used
---- Undergoing testing
---- Retired since Feb 2025
CAMS uses Earth Observation data from many satellites for atmospheric composition and weather.

## Slide 5: AC observations used in global NRT CAMS system
Species | Instruments
CAMS NRT | 
O3 | S5P, GOME-2, OMI, OMPS-NP, MLS, OMPS-LP, GEMS, TEMPO
CO | S5P, IASI, MOPITT
NO2 | S5P, GOME-2, GEMS, TEMPO
Aerosol | MODIS, VIIRS, PMAp, S3
CO2 | GOSAT, IASI, OCO-2
CH4 | GOSAT, IASI, S5P
SO2 (volcanic) | S5P, GOME-2, IASI
SO2 (anthropogenic) | S5P
HCHO | S5P, GEMS, TEMPO
GFAS fire emissions | MODIS, VIIRS, GOES, S3
---- Used
---- Undergoing testing
---- Retired since Feb 2025
CAMS uses Earth Observation data from many satellites for atmospheric composition and weather.

## Slide 6: Geostationary AC data
The HE CAMEO project is helping prepare CAMS for the assimilation of geostationary AC data

## Slide 7: Animation of hourly NO2 retrievals 20241203
GEMS
Hourly during daytime
TEMPO
Hourly during daytime
S5p & GOME-2BC
polar orbits

## Slide 8: TEMPO NO2 animation: 2-15 Dec 2024
NO2 observations
NO2 analysis departures (obs-an)
Positive departures over pollution sources in Eastern US (morning)

## Slide 9: TEMPO NO2: Hourly timeseries
Larger negative departures in the afternoon

## Slide 10: TEMPO NO2 assimilation test
Small reduction in departures when assimilating TEMPO NO2

## Slide 11: OZONE DIFFERENCES (NO2 ASSIM - CTRL)
MNMB (ASSIM – CTRL)
RMSE (ASSIM – CTRL)
Comparison with Airnow surface O3 observations
Small reduction in O3 MNMB and RMSE when assimilating TEMPO NO2, especially in central and eastern US

## Slide 12: Average hourly NO2 data
Reduced bias in GEMS V3
But GEMS V3 still has larger NO2 bias wrt CAMS than TEMPO
GEMS
V2 -> V3
2-17 Dec 2024
20 Dec 2024 – 5 Jan 2025
GEMS
GEMS
TEMPO
TEMPO

## Slide 13: A new CAMS reanalysis (EAC5)
Global reanalysis (EAC5), preparations have started, start prod. in 2025
higher resolution (~ 40 km, 137L), tropospheric & stratospheric chemistry
Global reanalysis (EAC4)
~80 km, 60 levels, tropospheric chemisty, lin O3 stratosphere
```
2003
1979
2021
2007
2014
CAMS
CAMS 2.0
Final preparations for EAC5 ongoing
Improvements to chemistry (IFScompo-BASCOE, including stratospheric chemistry)
Newer/ improved IFS version (better meteorology): CY49R2 – same as ERA6
Increased resolution (137 vertical levels; TL511 horizontal, ~ 40 km)
New reprocessed observation, new emissions including online biogenic emissions
Status
Acquisition and processing of observations finished
Testing of model and DA configuration in final stages
Improved QC for assimilated data before starting production
No emission inversion yet in EAC5
Production to start in
2025

## Slide 14: New model version (CY49R2) in EAC5
Model simulation without AC data assimilation (control runs) to test the impact of emissions and model upgrades
EAC5 CR show better results for many species, e.g. PM2.5
OBS EAC4 EAC5_1 CR (ECSAM4Clim=off) EAC5_2 CR (ECSAM4Clim=on)
Credit: Johannes Flemming

## Slide 15: Data acquisition and preparation
Data acquisition complete
This was a big task taking several years
150 TB of data (more than 2 million compressed files) in different formats ranging from pure binary to netCDF/HDF/BUFR and coming from different providers
Credit: Chris Kelly

## Slide 16: Quality check of TCO3 data
SCIA CCI
OMI CCI
GOME-2A AC-SAF
GOME-2B AC-SAF
GOME-2C AC-SAF
TROPOMI ESA
Good agreement between the TCO3 datasets
varBC will handle remaining differences

## Slide 17: CAMS satellite monitoring page
Monitoring plots are
routinely displayed on the CAMS website
They give us and the data producers timely information about any changes in the data
https://atmosphere.copernicus.eu/charts/packages/cams_monitoring/

## Slide 18: The Atmosphere Data Store (ADS)
All CAMS data are freely available: https://ads.atmosphere.copernicus.eu/
Documentation of atmospheric composition in IFS:
https://www.ecmwf.int/en/elibrary/81374-ifs-documentation-cy48r1-part-viii-atmospheric-composition
Validation reports and validation servers:
https://atmosphere.copernicus.eu/quality-assurance
Copernicus EU
www.copernicus.eu
atmosphere.copernicus.eu
@copernicusecmwf
Copernicus ECMWF
@copernicusecmwf.bsky.social

## Slide 19: Thank you
© European Union 2023
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com