## Slide 1
TEMPO Case Study: Tracking Canadian Wildfires Smoke and its Impact on Air Quality
Amy Huff1 Hai Zhang1, Pubu Ciren1, Zigang Wei1, and Shobha Kondragunta2
Aerosols and Atmospheric Composition Science Team 1STC at NOAA/NESDIS/STAR
2NOAA/NESDIS/STAR
CEOS AC-VC-21
Air Quality Aerosol Session
June 12, 2025

## Slide 2
Central/Western Canada’s 2025 fire season is well above average to date
Driven by abnormally dry conditions
“Out of control” wildfires releasing thick, brown-colored smoke
  Degrading surface air quality
  Reducing visibility
Prompted state of emergency & evacuations of thousands in Manitoba
Northerly winds blew smoke into the continental US starting May 29-30
Manitoba
Ontario
Saskatchewan

## Slide 3: Smoke Contains PM2.5
Images credit: US EPA
PM2.5 (fine particulate matter): very small aerosols, diameter ≤2.5mm
PM2.5 is harmful to human health
  Sensitive Groups are at greatest risk: children, seniors, people with existing respiratory or cardiovascular diseases
US EPA’s Air Quality Index (AQI) communicates PM2.5 concentrations
  Code Orange or higher: take action to limit exposure!

## Slide 4: May 30: Smoke Pushes Southward into the US
Smoke flowed into the Upper Midwest on May 30
Most of the smoke remained above the surface, so initial impacts on PM2.5 air quality were limited
Thick brown-colored smoke caused hazy skies & vivid sunsets!
Notes: TEMPO true color, scan 05 (13:15-14:08 UTC)

## Slide 5: May 31: Poor Air Quality in North & South Dakota
Thick smoke impacted surface air quality in the Upper Midwest
  Very Unhealthy (Code Purple) & Unhealthy (Code Red) daily 24-hour average PM2.5
Surface PM2.5 estimated from TEMPO & ABI synergy fills gaps in the PM2.5 regulatory monitor network
Smoke reached the eastern US but was aloft, so it had a limited effect on air quality
  Moderate (Code Yellow) conditions

## Slide 6: New! Height of Smoke in the Atmosphere from TEMPO
High particle concentrations
Aerosols near the surface, poor AQ
Smoke aloft, not impacting surface AQ
Aerosol Layer Height enhances Aerosol Optical Depth measurements with a 3-D view of smoke
High PM2.5 at the surface
Low PM2.5 at the surface

## Slide 7: June 2: Smoke Swirls over the Eastern US
Satellite Aerosol Detection highlights smoke (lavender)
Useful for end users because it quickly draws the eye to areas of smoke or dust
ABI missed a lot of the wildfire smoke!
  ABI’s spectral range is Visible-IR
Absorbing aerosols, like smoke & dust, are more sensitive to shorter wavelengths, e.g., UV
GOES-East ABI
Aerosol Detection
Animation from the AerosolWatch website

## Slide 8: TEMPO-ABI Synergy Enhances Smoke Detection
TEMPO’s UV-Deep Blue spectral range is more sensitive to absorbing aerosols
Hybrid TEMPO-ABI Aerosol Detection algorithm takes advantage of the synergy between the two sensors
Much greater coverage of the wildfire smoke than using ABI alone!
  Also provides info on the relative intensity of smoke/dust (thick vs thin)

## Slide 9: Ceilometer Profile Confirms TEMPO Smoke Layer Height on June 2
PAMS ceilometer in Cleveland, Ohio shows smoke mixed down to the boundary layer by ~18:30 UTC; correlates with aerosol layer height from TEMPO Scan 10
Smoke plume
Ceilometer plot courtesy of Jim Szykman (US EPA)

## Slide 10: Summary
NOAA aerosol satellite imagery provides vital observations during smoke transport events
  Helps operational air quality forecasters issue accurate alerts to public
  Allows people to take action to minimize exposure to harmful conditions
Hourly surface PM2.5 estimated from TEMPO-ABI synergy fills gaps in the US regulatory monitor network & gives end users critical info on current air quality conditions
TEMPO-ABI products have enhanced coverage & potentially higher accuracy compared to ABI alone
  Plus new products from TEMPO, e.g. Aerosol Layer Height
Near real-time TEMPO aerosol imagery is coming to our group’s AerosolWatch website in the next 1-2 months!
Enter “NOAA AerosolWatch” in your favorite search engine!