## Slide 1
JPSS and Near Earth Orbit Network Mission Update
NOAA
Satya Kalluri
Senior Scientist
Office of Low Earth Orbit (LEO) Observations
Satya.kalluri@noaa.gov
CEOS AC-VC21 2025
Contributors: Brian McDonald, Own Cooper (NOAA/OAR), Kai Yang (UMD/CISESS), Shobha Kondragunta (NOAA/NESDIS)

## Slide 2: Outline
Current status of JPSS mission
JPSS sensors and capabilities for measuring atmospheric composition
Recent examples of atmospheric composition application from JPSS data
NOAA intense flight campaigns for measuring atmospheric composition
Status of atmospheric composition data assimilation and modeling in NOAA’s Unified Forecast Modeling system
Plans for CrIS IR sounder follow on sensor under NOAA Near Earth Orbit Network (NEON).

## Slide 3: SNPP, NOAA20, NOAA21

## Slide 4: NOAA LEO Satellite Programs
4

## Slide 5: JPSS Sensors for Atmospheric Composition
Cross-track Infrared Sounder (CrIS)
Visible Infrared Imaging Radiometer Suite (VIIRS)
Ozone Mapping and Profiler Suite (OMPS)
CO, CO2, O3, CH4
Aerosols, Smoke, Dust
O3, SO2, NO2, Aerosol Index

## Slide 6: NOAA 21 VIIRS August 29, 2023
Idalia
Franklin

## Slide 7: Canadian Fires Monitored by VIIRS
NOAA21 VIIRS
June 26, 2023
PORTUGAL
SPAIN
Ravan Ahmadov
NASA GEOS-FP

## Slide 8: Carbon Monoxide From Canadian Fires Observed by CrIS June 26, 2023
VIIRS Active Fires
CrIS CO

## Slide 9: VIIRS PM2.5 Retrievals
SNPP VIIRS PM2.5 data shows that there is an increasing trend in smoke related exceedances of EPA National Ambient Air Quality Standard in the United States

## Slide 10: Texas Dust Storm, March 14, 2024
© 2024 AFP
NOAA21 OMPS
March 14, 2024
Photo: Lubbock Fire Rescue

## Slide 11
OMPS Data Vital For Monitoring Ozone
Arctic March 2024
Arctic March 2020
NASA Earth Observatory/NASA ozone watch
2024 Antarctic Ozone Hole
Arctic Ozone Record High
Antarctic
Arctic Concentration

## Slide 12: Intense Canadian Wildfires in the Summer of 2023
NOAA-20/CrIS - Carbon Monoxide
wildfire emissions & transport
NOAA-20/VIIRS – Wildfires detected (May – Jun 2023)
NOAA-20/CrIS – Peroxyacetyl Nitrate
wildfire oxidant & pollutant
highlighted
by

## Slide 13: OMPS NO2 Measurements
OMPS tropospheric column NO2, 2020-2024
2020-2024 NO2 Anomalies with reference to 2012-2019

## Slide 14: Large Multi-Agency Airborne Field Campaigns in Summer of 2023
https://csl.noaa.gov/projects/ages/

## Slide 15: NOAA Developing Unified Forecasting System with Chemistry (UFS-Chem) Model
Multiple NOAA OAR laboratories developing Research-to-Operations modeling capability for global / regional atmospheric composition forecasting and reanalysis, capable of assimilating JPSS satellite products for air quality and smoke & dust forecasting.
https://csl.noaa.gov/groups/csl4/modeldata/ufs-chem/

## Slide 16: Strong Agreement of UFS-Chem with SNPP/OMPS NO2 over Global Megacities

## Slide 17: Strong Agreement of UFS-Chem with SNPP/OMPS HCHO over Biogenic Regions

## Slide 18: CrIS Follow-on IR Sounder Notional Requirements for NEON
Sounding for IR Based Applications (SIRBA)
Chart: Infrared Sounder Instrument Wavebands
| SIRBA (channels TBS) | IASI-NG (16,921 channels) | IASI (8,461 channels) | CrIS (2,211 channels)
 | 1.5
SW-ext | 1
 | 1.12 | 3.62 | 3.62 | 3.92
SW | 1.38 | 1.38 | 1.38 | 0.72
 | 0 | 0 | 0 | 1.07
MW | 3.26 | 3.26 | 3.26 | 2.55
 | 0 | 0 | 0 | 0.88
LW | 7.24 | 7.24 | 6.84 | 6.24
Priorities | Performance Factor | Aspirational Target
 | Channels for direct Temperature Sounding and spectral resolution | All bands below: LW Band around 15 µm MW Band around 5.55 µm SW Band around 4.3 µm 0.25 cm-1 unapodized, 10 ppm spectral uncertainty No gaps
 | Channels for direct Moisture sounding and spectral resolution | MW Band around 6.3 µm 0.25 cm-1 unapodized, 10 ppm spectral uncertainty
 | Channels for atmospheric composition monitoring | Add extended Shortwave at 1.5-2.5 µm
 | Spatial coverage (daily global coverage) | 95% Global Coverage
 | Noise Level NEDT for Temperature sounding channels | CrIS-type NEDT levels (CrIS_NEDT) or better
 | Noise level NEDT for Moisture sounding channels | CrIS-type NEDT levels (CrIS_NEDT) or better
 | Spatial resolution | ~ 2km resolution or better (@nadir)
 | Geolocation/ Cloud-clearing Capability | ~1km or better resolution
 | CrIS Channels Continuity | Yes, for similar channels
 | Spatial sampling | Contiguous Footprints
Wave | Spectral Range | Spectral Range | Primary Use
Longwave | 650-790 cm-1 | 12.65-15.38 µm | Atmospheric temperature and cloudy-sky retrieval on the sensitivity to cold objects and CTH, CO2
Longwave | 790-1180 cm-1 | 8.47-12.65 µm | Surface/cloud properties and O3
Midwave | 1210-1650 cm-1 | 5.56 - 8.60 µm | Atmospheric water vapor and temperature, N2O, CH4, SO2
Shortwave | 2100-2150 cm-1 | 4.65 - 4.76 µm | Total column CO
Shortwave | 2150-2250 cm-1 | 4.44 - 4.65 µm | Atmospheric temperature and total column N2O
Shortwave | 2350-2420 cm-1 | 4.13 – 4.25 µm | Atmospheric temperature, CO2
Shortwave | 2420-2700 cm-1 | 3.7 – 4.13 µm | Surface/cloud properties
Shortwave | 4200-5210 cm-1 | 2.38 – 1.92 µm | Total column carbon dioxide, moisture and carbon monoxide
Shortwave | 5920-6410 cm-1 | 1.69 – 1.56 µm | Total column carbon dioxide and methane
Infrared Spectral Band Guidance
Notes: Updated slide after the Feb 28’s meeting

## Slide 19: Summary
VIIRS, CrIS, and VIIRS (3 out of 4 JPSS sensors) operationally measure atmospheric composition.
With 3 JPSS satellites in operations and 2 more yet to be launched, the mission is expected to provide atmospheric composition measurements well in to the next decade.
These JPSS observations are routinely used for air quality measurements and will be assimilated into global chemical models in NOAA’s next generation Unified Forecast System.
Several, large airborne field campaigns by NOAA and its partners are providing valuable in-situ validation measurements.
Next generation IR sounders by NOAA are expected to have enhanced atmospheric chemistry capabilities under the NEON program.