## Slide 1
David J. Diner1, Sina Hasheminassab1, Larry Di Girolamo2, Yang Liu3, Jun Wang4, Feng Xu5, and Huanxin-Jessie Zhang4
1Jet Propulsion Laboratory, California Institute of Technology
2University of Illinois at Urbana-Champaign
3Emory University
4University of Iowa
5University of Oklahoma
CEOS Atmospheric Composition – Virtual Constellation
12 June 2025
© 2025 California Institute of Technology.
Government sponsorship acknowledged.
Update on the
Multi-Angle Imager for Aerosols (MAIA) Mission
Reviewed and determined not to contain export-controlled CUI

## Slide 2
1
Satellite instrument data Multiangle UV/VNIR/SWIR and polarization imagery | Surface monitor measurements Conversion of retrieved aerosol properties to surface PM concentrations |  |  |  | WRF-Chem outputs Meteorological data; PM gap-filling | Health records Birth, death, hospitalization
Elements of the MAIA Earth Venture Instrument investigation
Daily-averaged total PM10, total PM2.5, and speciated PM2.5 in selected target areas on a 1-km grid
Epidemiological study results
Publicly available data
Privacy protected data
MAIA will explore linkages between exposure to different types of ambient particulate matter (PM) – mixtures of particles with different sizes, shapes, and compositions – and human health.

## Slide 3
The MAIA instrument was delivered (in place at JPL) in October 2022; delivery to ASI is planned for Fall 2025
2
  Within the the MAIA instrument is a 14-band spectropolarimetric camera that is pointable in two axes
Band (nm) | Aerosol bands
364 | absorbing particles
388 | 
414 | 
440* | fine particles
551 | 
646* | 
749 | 
865 | 
1044* | coarse particles
1608 | 
 | Specialty bands
762.5 | O2 absorption
943 | water vapor
1882 | cirrus screening
2124 | land surface
Scan (along-track) axis enables multiangle imaging of targets up to 70º view zenith angle
Pan (cross-track) axis provides ±48º field of regard, enabling frequent target observations (multiple times/week)
*polarimetric

## Slide 4
3
PTAs (12)
STAs (26)
Calibration/Validation Target Areas (4)
Primary Target Areas (PTAs): Surface monitor data collections, epidemiological studies (3-4 satellite observations/week)
Secondary Target Areas (STAs): Air quality and climate studies (1-4 satellite observations/week)
Calibration/Validation Target Areas (CVTAs) (~monthly for instrument/algorithm performance maintenance)
PTA/STA dimensions: 360 km x 480 km
Current map of MAIA target areas
3

## Slide 5: Spacecraft, launch, and orbit update
NASA’s mission partner, the Italian Space Agency (ASI), is planning for MAIA launch on a Vega-C launch vehicle in mid-2026 aboard ASI’s PLATiNO-2 spacecraft.
The launch manifest shows PLATiNO-2/MAIA as a shared ride with ESA’s Sentinel-3C spacecraft.
The launch plan has resulted in a change in the orbit from ascending to descending node.
Due to the targeting nature of the MAIA instrument, the reoriented ground tracks required a re-optimization of MAIA target coordinates.
Nominal equator-crossing time is moved up from 10:30 am to 10:00 am.
ascending flight direction
descending flight direction

## Slide 6
Surface monitors are essential for calibrating the transformation of satellite-derived aerosol information to near-surface PM concentrations.
The MAIA surface monitor air pollution network is
currently in operation
5

## Slide 7
Mean PM2.5 concentrations and
chemical compositions in the MAIA PTAs (2022-2023)
6
Spain
10 mg m-3
Rome
14 mg m-3
Israel
17 mg m-3
Boston
8 mg m-3
S. Africa
25 mg m-3
India
93 mg m-3
S. Korea
19 mg m-3
Taiwan
15 mg m-3
Ethiopia
33 mg m-3
Atlanta
10 mg m-3
Los Angeles
9 mg m-3
Chile
30 mg m-3
Not yet available
+ +
Calibrated PurpleAir PM2.5 data in Ethiopia, using BAMs at US Embassy facilities as reference sensors

## Slide 8
Geophysical retrieval algorithm overview
Retrieval | Algorithm approach
Cloud mask | 5 tests against predetermined thresholds (1) brightness; (2) normalized difference vegetation index or normalized difference snow index; (3) spectral whiteness; (4) cirrus test; (5) spatial variability
Aerosol | Optimal estimation (OE) preceded by initial step that constrains AOD using the MISR algorithm Employs a coupled atmosphere-surface vector Markov Chain/adding-doubling radiative transfer (RT) code A neural-network (NN)-based RT approach boosts computational efficiency Surface BRF climatology from MODIS MAIAC provides retrieval constraints
Satellite-based PM | Geostatistical Regression Models (GRMs) to map PM, trained using surface monitor measurements Offsets and satellite AOD coefficients are modeled as random effects; land use, meteorology, and other aerosol parameters are modeled as fixed effects Simplified pre-launch GRMs in the PTAs have been trained using AERONET AOD and WRF-Chem meteorology
Gap-filled PM | Similar GRM formulation but with WRF-Chem PM outputs as the primary predictor Training using surface monitors and addition of other predictors are employed to correct the CTM outputs for biases The corrected WRF-Chem estimates are merged with the satellite-based results using ensemble averaging
7

## Slide 9
MAIA data products for the PTAs
(NetCDF format)
Data Product | Contents | Spatial Grid | Temporal Info
L1 Georectified Imagery | Map-projected radiance and polarization data, view and illumination geometry, latitude/longitude coordinates | 250 m | Time/days of target overpass
L2 Cloud Mask | Cloud or Clear designation and confidence indicator Incorporates NOAA snow and ice mask (GMASI) | 1 km | Time/days of target overpass
L2 Aerosol Product | AOD, fractional AOD by size/shape/absorption, size distribution, refractive index | 1 km | Time/days of target overpass
L2 PM Product | PM10, PM2.5, speciated PM2.5 (sulfate, nitrate, OC, EC, dust) | 1 km | 24-hr averaged/days of target overpass
L4 Gap-filled PM Product | PM10, PM2.5, speciated PM2.5 (sulfate, nitrate, OC, EC, dust), spatially and temporally gap-filled | 1 km | 24-hr averaged/daily
Ancillary Geographic Product (AGP) | Land use information | 125 m - 1 km | Static
Surface Monitor Product | Measured and quality-controlled surface-based PM data | Point locations | Days when surface monitor data are collected
Current plans are to process STAs through L2 Aerosol and to provide AGPs, with other processing on a best-efforts, resource availability basis.
8

## Slide 10
The MAIA Geographic Information Visualization Tool (GIVT) is a web-based interactive GIS tool publicly available on the MAIA website.
GIVT enables exploration of MAIA target area locations and access to dynamic surface-based total and speciated PM data collected in the MAIA PTAs.
Surface Monitor Data Products in NetCDF format are also available from NASA Earthdata.
MAIA surface monitor data are publicly available
Example surface monitor data visualization in the Johannesburg PTA
9
GIVT: https://maia.jpl.nasa.gov/mmgis/
Earthdata: https://search.earthdata.nasa.gov/search
Search on “MAIA PM Surface Monitor”

## Slide 11
Concluding remarks
10
https://maia.jpl.nasa.gov
Generation of MAIA data products will integrate satellite, surface monitor, and CTM data.
  Data products will include daily maps of total PM2.5, total PM10, and speciated PM2.5 (sulfate, nitrate, EC, OC, dust) at 1-km spatial resolution in 12 PTAs.
Surface-based total and speciated PM data collection is now underway in all PTAs.
  The data can be explored using the GIVT tool on the MAIA website and NetCDF products available from NASA Earthdata.
The MAIA satellite instrument will be launched in 2026 (flight mission duration: 3 years).
After launch, epidemiologists on the MAIA Science Team will investigate linkages between PM type and human health.
Exposure timescale Health outcomes
Acute (days to weeks) Emergency room visits, premature deaths
Subchronic (months) Adverse birth outcomes, pregnancy complications
Chronic (years) Cardiovascular and respiratory diseases
Planned epidemiological studies in the MAIA PTAs