## Slide 1: Multi-Angle Polarimeter observations supporting the Copernicus Anthropogenic CO2 Monitoring (CO2M) Mission
Dr. Yasjka Meijer (ESA)
Dr. Rüdiger Lang (EUMETSAT)
AC-VC 21, Takamatsu, Japan

## Slide 2: CO2 Monitoring (CO2M) Mission
Detection of emitting hot spots
Monitoring the hot spot emissions
Assessing emission changes against local reduction targets
Assessing the national emissions and changes CO2 required precision: 0.16% CO2 required bias: <0.12%
747-773 nm
1590-1675 nm
1990-2095 nm

## Slide 3: Change of light path
A change in light path (in lowest 1 km) of 13 meter can cause an error of 0.5 ppm (0.12%) in XCO2 [SRON]
(760nm)=0.3 and (1600nm) =0.07
Notes: Ignoring the light path change can induce XCO2 errors of ppm. (see also non-scattering error Butz et al., App. Opt. 2009).
Just a back-of-the envelope calculation how relevant the light path is!
Ignoring the light path change can induce XCO2 errors of ±5 ppm. (see also non-scattering error Butz et al., App. Opt. 2009).
Just a back-of-the envelope calculation how relevant the light path is!

## Slide 4: Aerosol for GHG monitoring
XCO2 bias (ppm)
Aerosol amount (AOD)
With MAP
Without MAP
Aerosol & cloud scattering:
Heritage missions without MAP require bias correction and strict quality filtering for AOD<0.3.
For CO2M, Light path correction by measuring effective aerosol & clouds:
Higher accuracy CO2 data (less posterior bias correction)
More data and also at higher aerosol loading; up to 0.5 AOD
Cloud cover of CO2 pixel 1 – 5%
MRD
0.0 0.5 1.0
Aerosol amount (AOD)
Credits: SRON, Utrecht

## Slide 5: XCO2 bias: dependence on AOT
Joint CO2I+MAP retrieval
CO2I only retrieval
std dev. =1.86 ppm
median bias = 0.95 ppm
std dev. =0.57 ppm
median bias = -0.088 ppm
Credits: SRON, Utrecht

## Slide 6: XCO2 bias: dependence on AOT
Joint CO2I+MAP retrieval
CO2I only retrieval
std dev. =1.86 ppm
median bias = 0.95 ppm
std dev. =0.57 ppm
median bias = -0.088 ppm
Credits: SRON, Utrecht

## Slide 7: Payload Implementation
Credits: TASiF
Payload Components
CO2 Imager (CO2I): 3 band (1 NIR, 2 SWIR) co-located push-broom imaging spectrometer
NO2 Imager (NO2I): VIS band implemented as fourth band in CO2I instrument
Multi-Angle Polarimeter (MAP) for aerosol observations
CLoud IMager (CLIM) for low cloud & cirrus detection

## Slide 8: Multi Angle Polarimeter (TASiUK)
Multi-angle polarimeter (MAP) implementation:
Compact push broom imager:
40 viewing angles (+/- 60º), plus 8 more @larger angles
3 polarisations (0º, 60º, 120º)
Spatial resolution: 4x4 km2 and sampling < 1x1 km2
6 pol. spectral bands (+1 for co-reg with CO2I)
MAP OU STM in mechanical testing
Credit © TAS-UK
Credits:
TAS-UK
MAP Band | Wavelength
VNIR-1 | 410 nm
VNIR-2 | 443 nm
VNIR-3 | 490 nm
VNIR-4 | 555 nm
VNIR-5 | 670 nm
VNIR-6* | 753 nm
VNIR-7 | 865 nm
CDR
Required total DoLP error <0.0035
22-23 May calibration meeting 50 experts!

## Slide 9: Copernicus CO2M Mission – Status
Project status:
Constellation of 3 satellites
Each satellite >270 km swath
First satellite Acceptance Review 08-2027
Second satellite Acceptance Review 02-2028
Third satellite is scheduled in 2029
Credits: EMPA
Copernicus data is made freely available to any person and organisation around the world
EUMETSAT performs operational data processing
Product | Spatial | Precision
CO2 | 4 km2 | 0.7 ppm
CH4 | 4 km2 | 10 ppb
NO2 | 4 km2 | 1.5 1015 molecules cm-2
Vegetation SIF | 4 km2 | 0.7 mW m-2 sr-1 nm-1
Aerosol params | 16 km2 | 0.05 AOD, 500 m LH
Cloud fraction | 1% | Water clouds & cirrus
More info  https://doi.org/10.3389/frsen.2023.1217568

## Slide 10: Nominal and pitched (“sun-glint”-pointing) platform orbits for CO2M
Nominal Orbit
Pitched Platform Orbit
*) Cox-Munk model for water (glint) reflectance at 7 m/s averaged wind-speed.
*)
*)
Platform pitch angle at 0 deg
(all 41 views +-60 degrees)
Platform pitch angle at 50 deg forward looking
(all 29 valid views +-60 degrees)

## Slide 11: Simulation of CO2M MAP level-0 data – detector level

## Slide 12: Simulation of CO2M MAP L1 data – L1B to L1C co-registration to CO2I grid
The CO2M MAP L1B
2 granules
(total 6 minutes)
Nadir pointing
4 views out of 48 are shown
The CO2M MAP L1C
2 granules
(total 6 minutes)
Nadir pointing
45 Co-registered views

## Slide 13: EUMETSAT CO2M MDPS scientific processing tasks
Below this level: everything is co-registered or provided at the CO2I/NO2I spectrometer footprint
CO2M
Mission Data Processing System
Make one
“hyper-GHG/NO2-instrument”
out of three!

## Slide 14: EUMETSAT CO2M MDPS scientific processing tasks
Below this level: everything is co-registered or provided at the CO2I/NO2I spectrometer footprint
CO2M
Mission Data Processing System
Make one
“hyper-GHG/NO2-instrument”
out of three!

## Slide 15: CO2M MAP level-2 aerosol product for pathlength correction
EUM2022713 v1A 28 April 2025
The GRASP (Generalized Retrieval of Aerosol and Surface Properties) is used for the simultaneous retrieval of both aerosol and surface properties.
Aerosol retrieval performed in the VNIR, is used for an atmospheric correction in the SWIR for the CO2 retrieval.

## Slide 16: CO2M MAP level-2 aerosol product for pathlength correction
EUM2022713 v1A 28 April 2025
MAP Band | Wavelength
VNIR-1 | 410 nm
VNIR-2 | 443 nm
VNIR-3 | 490 nm
VNIR-4 | 555 nm
VNIR-5 | 670 nm
VNIR-6* | 753 nm
VNIR-7 | 865 nm
The GRASP (Generalized Retrieval of Aerosol and Surface Properties) is used for the simultaneous retrieval of both aerosol and surface properties.
Aerosol retrieval performed in the VNIR, is used for an atmospheric correction in the SWIR for the CO2 retrieval.

## Slide 17: CO2M MAP level-2 aerosol product for pathlength correction
EUM2022713 v1A 28 April 2025
MAP Band | Wavelength
VNIR-1 | 410 nm
VNIR-2 | 443 nm
VNIR-3 | 490 nm
VNIR-4 | 555 nm
VNIR-5 | 670 nm
VNIR-6* | 753 nm
VNIR-7 | 865 nm
+
CO2I SWIR1/2 background reflectance
SWIR 1: 1620-1627.5 nm
SWIR 2: 2034.9-2037.5 nm
The GRASP (Generalized Retrieval of Aerosol and Surface Properties) is used for the simultaneous retrieval of both aerosol and surface properties.
Aerosol retrieval performed in the VNIR, is used for an atmospheric correction in the SWIR for the CO2 retrieval.

## Slide 18: Outlook for AQ
In the frame of the Copernicus CO2 Monitoring and Verification Support capacity (CO2-MVS) all CO2M products up to level-2 are provided with a latency of better than 24h and availability of better than 95% to CAMS.
We received recently a request from the EC to evaluate the possibility to provide NO2, and (if possible) MAP Level-2 Aerosol product to CAMS with a latency between 3 and 5 hours.
Feasibility study ongoing at EUMETSAT
(results expected in Sep/Oct 25)

## Slide 19: THANK YOU