## Slide 1: Key features of the latest Ozone CCI Total Ozone Algorithm
C. Lerot, R. Spurr, M. Van Roozendael, D. Loyola, M. Koukouli, D. Balis, J.-C Lambert, J. Granville
CEOS ACC meeting #9 (EUMETSAT), 18-19 April 2013

## Slide 2: Motivation and content
CCI total ozone algorithm key features
Soft-calibration of level-1 reflectances
Improvement of European inter-sensor consistency
Conclusion and outlook
Overall motivation: demonstrate new European multi-sensor level-2 and level-3 data sets with improved consistency (targeting GCOS compliance)

## Slide 3: Direct-fitting Algorithm (GODFIT v3)
Algorithm developed for retrieving total ozone from nadir hyperspectral instruments in the Huggins bands (325-335 nm).
Direct fitting approach – closer to the physics than DOAS
Baseline for ESA CCI data sets  www.esa-ozone-cci.org
DOAS residuals
Direct-fitting residuals

## Slide 4: Algorithm’s key features (1)
T°-shift adjustment scheme: the a-priori T°-profile is shifted in the retrieval.
Shift parameter adjusted in the fit
A priori temperature profile
Actual temperatures used in the forward model
q(z) = t(z) + S
Cloud correction:
  one effective scene, at one effective altitude (weighted average of surface and cloud top height)
  Internal closure mode  the effective scene albedo is retrieved simultaneously to ozone.

## Slide 5: Algorithm’s key features (2)
Semi-empirical Ring correction. The filling-in factors are expressed as:
This formulation includes:
Source and loss terms due to inelastic scattering
Absorption by ozone
smoothing of the ozone absorption by RRS process
r0 is fitted to observations, Aout and Ain are tabulated after fits to pre-calculated filling-in factors using LIDORT_RRS.
Total O3: 500 DU
SZA= 85°
VZA= 50°
RAA= 10°
Albedo = 0.8
Probability of RRS

## Slide 6: Algorithm’s key features (3)
Polarization correction  based on pre-calculated LUTs of correction factors using VLIDORT
Impact on absolute reflectance (325 nm)
Impact on ozone structures

## Slide 7: Algorithm’s key features (4)
A priori O3 profile climatology:
  Stratosphere: Total-O3 classified profile climatology TOMSv8.
  Troposphere: OMI/MLS climatology (longitudinally resolved – 60°N - 60°S).
A-priori tropospheric content is important for ghost column correction, especially in case of strong cloud contamination.

## Slide 8: Algorithm’s key features (5)
The impact of a potential switch to Serdyuchenko et al. data has been assessed (ACSO contribution):
  The retrieved O3 columns would be 1 to 2.5 % larger, depending on the effective temperature
  The fit quality is similar
 Difficult to select one “best” data set
Ozone absorption cross-sections
Current baseline: Brion, Daumont and Malicet.

## Slide 9
Suite of new RT tools developed by RT Solutions (Rob Spurr)  performance enhancement by approximately a factor 4-5 while maintaining good accuracy (<< 1%).
Based on principal component analysis (PCA) of optical properties, single-scattering and approximate 2-stream RT code
Paper by Spurr et al. in JQSRT.
Performance enhancement using PCA
Accuracy of the method as a function of the number of PCA eigen vectors

## Slide 10
Soft-calibration of level-1
reflectances
Calibration limitations and instrumental degradation lead to inconsistencies between level-2 total O3 data sets derived from raw level-1 data sets.
 Identification of artificial structures in the level-1 spectra, characterization of their main dependences (Time, SZA, VZA, …) and empirical correction.

## Slide 11
Soft-calibration of level-1
reflectances
Impact of GOME degradation on retrieved albedo
GOME degradation
Impact on
Retrieved albedo (clear sky)

## Slide 12
Soft-calibration of level-1
reflectances
Comparison of instrumental degradation
Ratio of measured to simulated reflectances
GOME
SCIAMACHY
GOME-2

## Slide 13
Soft-calibration of level-1
reflectances
Characterization of spectral features in reflectances
Simulated/Level-1 reflectance
GOME2 vs SCIAMACHY (raw L1)
GOME2 vs SCIAMACHY (Soft-calibrated l1)

## Slide 14
GOME-2
Soft-calibration of level-1
reflectances
Time dependence of spectral features
in SCIAMACHY and GOME-2 spectra
SCIAMACHY

## Slide 15
Current level-2 operational products
Improvement of inter-sensor consistency (1)
SCIAMACHY – GOME (%)
GOME-2A – GOME (%)
O3-CCI level-2 products

## Slide 16
Improvement of inter-sensor consistency (2)
Time
Time
Time
GOME/ERS-2
SCIAMACHY/ENVISAT
GOME-2/METOP-A
Best overall consistency obtained with merged SBUV data set

## Slide 17: Conclusion and outlook
CCI total ozone reprocessing  GOME, SCIAMACHY and GOME-2(A) instruments processed using common state-of-the-art direct-fitting (scientific) algorithm
New soft-calibrations scheme
Improved inter-sensor consistency in comparison to current level-2 data sets
Outlook
  Algorithm transfer to OMI is ongoing
  Plans for CCI Phase-2  improvement of cloud correction, improvement of soft calibration, OMI addition, data base update (e.g. TOMS v9), work on combined column/profile algorithm