## Slide 1
David Haffner, SSAI
P.K. Bhartia, NASA-GSFC
Atmospheric Composition Constellation Meeting (ACC-9)
18-19 April 2013, EUMETSAT
Key Features of the Latest TOMS Total Ozone Algorithm

## Slide 2
Based on Dave & Mateer (1967)
SBUV V1-6 TOMS V1-8 OMI (NASA algorithm) Suomi/NPP OMPS NM (same as TOMS V8)
Spectral Fitting Algorithms
SBUV continuous scan (Joiner & Bhartia, 1997) GOME-DOAS OMI-DOAS WFDOAS BOAS BIRA/Direct Fit
Optimal Estimation Algorithms
GOME & OMI (Liu et al., 2005, 2010) SBUV V8.6 (Bhartia et al., 2012) Suomi/NPP OMPS NP (same as SBUV V8.6) TOMS V9 (similar to SBUV V8.6)
Backscatter UV Total O3 Algorithms

## Slide 3
Based on Dave & Mateer (1967)
SBUV V1-6 TOMS V1-8 OMI (NASA algorithm) Suomi/NPP OMPS NM (same as TOMS V8)
Spectral Fitting Algorithms
SBUV continuous scan (Joiner & Bhartia, 1997) GOME-DOAS OMI-DOAS WFDOAS BOAS BIRA/Direct Fit
Optimal Estimation Algorithms
GOME & OMI (Liu et al., 2005, 2010) SBUV V8.6 (Bhartia et al., 2012) Suomi/NPP OMPS NP (same as SBUV V8.6) TOMS V9 (similar to SBUV V8.6)
Backscatter UV Total O3 Algorithms

## Slide 4: Objectives for V9 TOMS
Provide Error Bars to users
  A frequent request
Supply information to estimate systematic error
  Provide the correct layer Efficiency Factors (EF)
Extend retrievals to 88° SZA
  Report errors on challenging retrievals
  Improve quality of these retrievals
Simplify the entire algorithm
  V8 performed well, but execution was far from seamless
    Pair switching & complex correction for profile effect
    1512 a priori profiles tedious to construct
Quality as good as V8, within error bars
Rodger’s Optimal Estimation a natural choice
  Originally considered just for high SZA, worked well elsewhere

## Slide 5
Total O3 calculated from retrieved TOMS profiles
OE uses 3 λ for O3 information
  312.5, 317.5, 331 nm, flexibility to add more (305-315 nm ideal)
  Brion et al. O3 x-secs
216 a priori profiles
  mean and covariance calculated from MLS & sondes or GMI Model
  profiles have no total ozone dependence
OE provides error bars, efficiency factors, and DFS
LER model + corrections for clouds and terrain
R-λ aerosol correction
SO2, aerosol contamination flagged when extreme
Overview of the Basic Algorithm
March 1989
63° 0° -63°
VZA
Notes:   313,318,331 = high, medium, low sensitivity
  OE cov   total ozone dependence : Methods are similar
  Here Negative VZA inidcates West, away from Sun
  312.5 and other L in 305-315 region have good total ozone information if their profile sensitivity can be accounted for in the retetrieval

## Slide 6
Profiles retrieved at 11 layers
Provides total ozone with a consistent profile
Profile retrieval reduces profile shape related error at shorter wavelengths (benefits SO2 est.)
Despite lack of total ozone dependence in a priori, V9 retrieves total O3 close to V8.
    Total ozone dependent profiles used in V8 provided the information that OE gets from covariance matrices.
V9 TOMS Retrieves Profiles
retrieved
a priori
V9 retrieved 225 DU V8 retrieved 224 DU
V9 a priori 343 DU
66S, 74.5E
70° SZA

## Slide 7: Total Ozone Comparisons with TOMS V8 and SBUV V8.6 in March 1989
March 1989
V9 agrees with V8 within error bars (1-2%) to 84° SZA
V9 reduces error at SZA > 70° (based on SBUV V8.6)
V9 bias must be removed

## Slide 8
TOMS Efficiency Factors
85° SZA
V9
V8
0.5
1.0
1.5
1
10
100
1000
54° SZA
Efficiency Factors (EF)
Column Integrating Kernel (CIK)
Integrating Kernel (IK)
V9
V8
elements of CIK
sum over columns of IK
(a.k.a. Averaging Kernel)
Lower atm. EFs are Rayleigh-Limited in UV
Ideal efficiency
V8 EFs wrong at high SZA
Notes: Add’l wavelengths wont help with Trop

## Slide 9
TOMS errors vary by factor of 10.
Most dependence is w/ SZA, not O3, VZA.
Reason: EFs reduce dramatically in lower atmosphere as path length increases.
Less info. from measurements  greater reliance on a priori  larger uncertainty.
Error Dependence with SZA
June 21, 1988
Column Error
Column Amount

## Slide 10
Important to consider when monitoring ozone minima
Error Bars for O3 Hole Conditions
Column Error in Sep 29, 1987 Ozone hole
Column Amount
Errors increase sharply at high SZA
With error bars we can properly qualify measurements made at extreme SZA.
Errors are important to consider when tracking ozone minima.

## Slide 11
Overall Geometry Dependence of Error
SZA dominated
VZA dominated
Efficiency Factor 0
1% error at 45 N
March, 1989
2% error at 80 N
Error increases quickly thereafter.
Notes: SZA larger on swath LHS (afternoon orbit)

## Slide 12
Must correct aliasing of aerosol absorption aerosols into ozone enhancement.
Assume linear dependence of Reflectivity with wavelength
  Follows study by Dave (1977)
Measure LER at 340 and 380 nm
Linearly extrapolate R to O3-absorbing λs
Retrieve O3 with wavelength dependent R
Approach fails for thick aerosols  flag
Aerosol Correction

## Slide 13
Use LER surface model exclusively
First retrieve O3 at 1 atm sfc presure
Linear R-lambda method corrects Rayleigh error for both terrain and clouds
Terrain: 1) zero EFs and profile below Psfc 2) adjust total ozone
Clouds: 1) retain profile through cloud 2) lower EFs below OCP with est. Rc 3) adjust total ozone
Corrections for Terrain and Cloud Height
Notes: Uncertainty in profile in cloud

## Slide 14
V9 TOMS provides error bars.
V9 TOMS is in good agreement with V8 TOMS. Compares well with V8.6 SBUV.
Can extend retrievals to 88° SZA.
Errors originate mostly in lower atmosphere where Rayleigh scattering limits retrieval of O3 information (significant at high SZA, i.e. O3 hole).
V9 provides consistent profiles.
Algorithm offers flexibility.
Conclusions
Notes: Calibration adjustment necessary.

## Slide 15
Dave, J.V., and Mateer, C. L.: A Preliminary Study on Possibility of Estimating Total Atmospheric Ozone from Satellite Measurements, J. Atmos. Sci., 24, 414-427, 1967.
Joiner, J. and Bhartia, P.K.: Accurate determination of total ozone using SBUV continuous spectral scan measurements, J. Geophys. Res.-Atmos., 102, 12957-12969, 1997.
Liu, X., Chance, K., Sioris, C.E., Spurr, R.J.D., Kurosu, T.P., Martin, R.V., and Newchurch, M.J.: Ozone profile and tropospheric ozone retrievals from the Global Ozone Monitoring Experiment: Algorithm description and validation, J. Geophys. Res.-Atmos., 110, D20307, doi:10.1029/2005JD006240, 2005.
Liu, X., Bhartia, P.K., Chance, K., Spurr, R.J.D., and Kurosu, T. P.: Ozone profile retrievals from the Ozone Monitoring Instrument, Atmos. Chem. Phys., 10, 2521-2637, 10.5194/acp-10-2521-2010, 2010.
Bhartia, P.K., McPeters, R.D., Flynn, L.E., Taylor, S., Kramarova, N.A., Frith, S., Fisher, B., and Deland,M.: Solar Backscatter UV (SBUV) total ozone and profile algorithm, Atmos. Meas. Tech. Discuss., 5, 5913-5951, doi:10.5194/atmd-5-5913-2012, 2012.
References