## Slide 1: LSI-VC-18 2025 KARI’s Works on ARD
Taeheon KIM, KARI
Agenda Item 3.1
LSI-VC-18
Ispra, Italy
2-5 September, 2025

## Slide 2
KARI’s Global Collaboration Efforts:
  Contributing to CEOS ARD standardization through active participation in CEOS LSI-VC WGCV, VH-RODA, JACIE, and other key international workshops
  Developing K-ARD(Analysis Ready Data for KOMPSATs or Korea) to meet the specific requirements of KARI’s high-resolution satellite imagery
Development of Prototype Software
  Research initiated in 2023 to develop a K-ARD prototype aligned with CEOS ARD standards
  Now under development based on the completed design, focusing on KARI-operated optical satellites KOMPSAT-3/3A and SAR satellite KOMPSAT-5
  Focused ARD study on EO SR product and SAR products (NRB, POL, ORB, GSLC; excluding InSAR)
Overview: Current Activities
※ SR (Surface Reflectance), NRB (Normalised Radar Backscatter), POL (Polarimetric Radar), ORB (Ocean Radar Backscatter), and GSLC (Geocoded Single-Look Complex)

## Slide 3
Overview: KARI’s LEO Mission
LEO
Not Working
Working
Under Development
KOMPSAT-1
1999
EO 6.6m
KOMPSAT-2
2006
EO 1m
KOMPSAT-3
2012
EO 0.7m
KOMPSAT-3A
2015
EO 0.55m
KOMPSAT-5
2013
SAR 1m
CAS-1
2019
EO 0.5m
KOMPSAT-7
Q4 2025
EO 0.3m
KOMPSAT-7A
2026
EO 0.3m
KOMPSAT-6
Q1 2026
SAR 0.5m
CAS-2
2026
EO 0.5m

## Slide 4
Background
Growing Demand for Efficient Data Utilization
  Increasing number of domestic satellites and wide use of EO/IR/SAR sensor
  Rising need for efficient data processing and standardization
Introduction of CEOS ARD
  CEOS introduced the concept of Analysis Ready Data (ARD)
  Provides standardized satellite imagery usable without additional preprocessing
The Need for K-ARD
  CEOS ARD mainly focuses on medium- to low-resolution imagery
  High-resolution satellites like KOMPSAT series require a tailored ARD framework
  Development of advanced image correction modules is also necessary to address these requirements
KARI’s Initiative
  Developing prototype software for high-resolution satellite imagery (K-ARD)

## Slide 5
Goal & Application
Goal of K-ARD
  Establish ARD specification tailored to Korea’s environment while aligning with international standards
  Verify the application of ARD to domestic satellite imagery through software development
  Provide ARD-processed satellite imagery to the public within the next few years
Application Area of K-ARD
  K-ARD provides standardized imagery with geometric, radiometric, and atmospheric corrections and is expected to support the following application areas:
Application Area | Example Applications
Time-series analysis | Monitoring agricultural field changes, Tracking urban expansion
Land cover and land use mapping | Observing forest area changes, Classifying agricultural zones
Climate change monitoring | Monitoring vegetation index changes, Detecting land degradation
Hydrological studies | Monitoring river level changes, Mapping flood-prone areas
Disaster detection (floods, droughts, wildfires) | Detecting inundated areas, Early warning for droughts, Assessing wildfire damage

## Slide 6
Methodology
It analyzes the sensor characteristics and specifications of satellites operated by KARI and prepares K-ARD product specifications based on international standards.

## Slide 7
Methodology
Software is being developed to generate and verify satellite imagery products in accordance with the K-ARD specification

## Slide 8
ARD Compliance Assessment
Compliance review conducted for KARI’s LEO satellites based on CEOS ARD
  SAR (KOMPSAT-5 or 6): Four products (NRB, POL, ORB, GSLC) reviewed → all Thresholds confirmed satisfiable via tailored ARD module development
  EO (KOMPSAT-3/3A or 7): Target Product SR reviewed → all Thresholds confirmed satisfiable (except 4.1 Geometric Correction requirement) → Identification of issue in High-resolution imagery
SAR Products Self Assessment table
EO SR Product Self Assessment table

## Slide 9
K-ARD for EO Imagery

## Slide 10
K-ARD for EO Imagery
Sensor model-based improved relative geometric correction
  Conventional: matching points searched across entire target image → higher chance of mismatches
  Improved (Sensor model-based): matching points searched only within predicted local neighborhood → more accurate and efficient matching

## Slide 11
K-ARD for EO Imagery
Deep learning-based cloud detection
  Adopted a Deeplabv3+ architecture with a ResNet-50 backbone for cloud segmentation in KOMPSAT-3/3A imagery
  Generate ~4,000 augmented patches (1024 x 1024) from 162 original images to enhance training diversity
  Achieved significant improvement compared to traditional cloud detection method (Threshold-based)
 | Thick Cloud | Thin Cloud | Cloud Shadow
Ground Truth | 12.49% | 0.11% | 4.30%
Deep-learning (ours) | 11.77% | 0.78% | 4.30%
Threshold-based | 9.69% |  | 3.50%
 | Thick Cloud | Thin Cloud | Cloud Shadow
Ground Truth | 9.35% | 6.09% | 12.12%
Deep-learning (ours) | 8.97% | 5.26% | 13.26%
Threshold-based | 6.44% |  | 3.20%

## Slide 12
K-ARD for EO Imagery
Radiometric and atmospheric correction
  6S model(LUT-based algorithm): radiative transfer model simulating solar radiation through the atmosphere
  Removes atmospheric scattering/absorption from TOA signal to derive SR
  Atmospheric correction converts DN values → SR (provided as GeoTIFF)
Uncorrected
Corrected
※ 6S (Second Simulation of the Satellite Signal in the Solar Spectrum)

## Slide 13
K-ARD for SAR Imagery

## Slide 14
K-ARD for SAR Imagery
SAR NRB
  NRB(Normalized Radar Backscatter) : Backscatter imagery with RTC(Radiometric Terrain Correction) applied
  Gamma naught( ) imagery
  Land, sea, shadowing, foreshortening, and layover (etc.) information provided as mask imagery
  Local Incidence Angle imagery generated based on DEM
  Gamma-to-sigma ratio imagery provided for Sigma-naught( ) conversion
SAR NRB Image
SAR NRB Mask
SAR NRB LIA
SAR NRB to ratio

## Slide 15
K-ARD for SAR Imagery
SAR ORB
  ORB(Ocean Radar Backscatter) : Provide sigma-naught () backscatter imagery for ocean observation, corrected to geoid reference
  Sigma naught( ) imagery
  Land, sea, shadowing, foreshortening, and layover (etc.) information provided as mask imagery
  Ellipsoidal Incidence Angle imagery (calculated from Earth ellipsoid)
  Gamma-to-sigma ratio imagery provided for Gamma-naught( ) conversion
SAR ORB VV
SAR ORB Mask
SAR ORB EIA
SAR ORB VH

## Slide 16
K-ARD for SAR Imagery
SAR POL
Polarimetric Decomposition | Product | Band | Description
CovMat | HH | Red | High backscatter observed over horizontally aligned surface
 | HV(VH) | Green | High return due to volume scattering
 | VV | Blue | High reflection from urban areas and man-made structure
Yamaguchi CovMat | Ps | Blue | Single-bounce backscatter from smooth ground surface
 | Pd | Red | Double-bound backscatter observed in dense building regions
 | Pv | Green | Volume scattering generated within vegetation
 | Helix | Gray scale | Scattering signal from multiple/asymmetric reflection patterns
Cloude-Pottier (H-A-Alpha) | Entropy | Gray scale | Signal representing scattering entropy
 | Anisotropy | Gray scale | Signal indicating the degree of directional scattering
 | Alpha | Gray scale | Signal representing the mean scattering angle

## Slide 17
K-ARD for SAR Imagery
SAR GSLC
  Geolocation provided with original resolution and phase information preserved
  InSAR coherence & differential phase generated by: - Multiplying GSLC pair () as complex conjugates - Normalizing by local mean intensity - Applying local averaging window
GSLC Intensity(Complex image)
GSLC1 Intensity
GSLC2 Intensity
Complex coherence
InSAR differential phase

## Slide 18
K-ARD Product Structure
SAR/EO product file and folder structure
  K-ARD product folder structure defined as intuitive from user perspective
  Structure advantageous for tile-based time-series visualization; designed as distribution folder structure
  Folder structure aligned with image naming sequence of K-ARD products
KARD
SAR
Tile Num.
Subgrid ID
Imaging Date
Satellite
Name
SAR
Product
KARD
EO
Tile Num.
Subgrid ID
Imaging Date
Satellite
Name
SAR Folder Hierarchical Structure
EO Folder Hierarchical Structure

## Slide 19
K-ARD Tiling Design
K-ARD tiling scheme defined on the basis of the MGRS tile system
  Sub-grid tile size adjusted to EO and SAR swaths, following MGRS-based tile indexing rules
  Tile sub-grid divided four times by quadtree method (equal-interval quartering)
  Tile naming: MGRS tile index + sub-grid level (e.g., 52SCG1330)

## Slide 20
K-ARD Tiling Design
Determination of product GSD based on tile size
  GSD defined as an integer multiple of the grid size
  EO GSD set according to Level-4(6.25km) specification
  SAR GSD set depending on acquisition mode (Level-4 and Level-2 combined)
  Upper-left coordinate of the orthorectified image set to an integer multiple of the GSD for exact pixel alignment with grid boundaries

## Slide 21
Near Term Activities
Near Term Activities
  Software Integration and Development for ARD processing: ~ ’26/04
  Software Testing and Verification for ARD processing: ~ ‘26/10

## Slide 22
Thank you for your attention!