## Slide 1
CEOS WGCV Plenary
May 16 to 19, 2017
U.S. Department of the Interior
U.S. Geological Survey
Global DEM Update / Discussion
Dean Gesch (gesch@usgs.gov)
U.S. Geological Survey, Earth Resources Observation and Science Center (EROS), Sioux Falls, South Dakota, USA

## Slide 2
1985
2020
1988
ETOPO5 10 km
2000
SRTM flight
2009
ASTER GDEM v1 30 m
2015
ASTER GDEM v3 30 m
1996
GTOPO30 1 km
2005
SRTM 90 m 30 m
2011
ASTER GDEM v2 30 m
TanDEM-X 12 m
2016
ALOS World 3D 5 m
2017
NASA-DEM 30 m
GMTED2010 250 m, 500 m, 1 km
→ WGCV / Terrain Mapping Subgroup
→ GEO Global DEM Task
→ ISPRS WG IV/3 – Global DEM Interoperability
Activities:
  - SRTM workshop / PE&RS special issue
  - ASTER GDEM evaluation / IGARSS session
  - ISPRS sessions (2008, 2010, 2012, 2014, 2016)
Key Participants:
  - J-P. Muller (UCL), R. Crippen & M. Kobrick (NASA/JPL), T. Tadono (JAXA), D. Gesch (USGS), C. Carabajal (NASA/GSFC), M. Bernard (SPOT/Airbus), J. Slater (NGA)

## Slide 3
Which global DEM is the best?
Shuttle Radar Topography Mission (SRTM)
PRISM / ALOS World 3D
ASTER Global Digital Elevation Model (GDEM)
TanDEM-X / WorldDEM

## Slide 4
Shuttle Radar Topography Mission
SRTM
Archive
Distribution
Applications
Archive
Distribution
Applications

## Slide 5: SRTM – Mission Overview
11-day Space Shuttle Endeavour mission in February 2000
Based on SIR-C/X-SAR imaging radar flown in April and October 1994
Joint NASA – NGA project to produce digital topographic data
  Data points spaced every 1-arc-second (30-meters) for 80% of Earth’s land surface
  Absolute vertical accuracy specification: 16 meters (at 90% confidence)
(http://www2.jpl.nasa.gov/srtm/index.html)

## Slide 7
SRTM – Mission Overview
SRTM collected nearly 80% of the Earth’s land surface (60ºN to 56ºS latitude)

## Slide 8
https://lpdaac.usgs.gov/sites/default/files/public/measures/docs/NASA_SRTM_V3.pdf

## Slide 9
“SRTM Plus” Digital Elevation Model
(SRTM NASA Version 3)
LPDAAC Release November 20, 2013
SRTM Version 2
with voids
“SRTM Plus”
(Voids filled)
N36 E78: Southwest China
Shuttle Radar Topography Mission
DEM was void-filled primarily
with the ASTER GDEM.
A novel error-detector was used
to avoid cloud glitches in GDEM.
The USGS GMTED2010 or
National Elevation Dataset (NED)
was then used as the secondary fill.
A modified “Delta Surface Fill”
algorithm produced the
seamless DEM merger at
one-arc-second postings.
(Released at 3-arc-seconds)
Crippen / Kobrick, JPL
Elevation shown as brightness

## Slide 10
Southeast Panama
SRTM Version 2
GDEM
“SRTM Plus”
Voids &
Water-Mask Errors
Clouds &
Shoreline Errors
Clean Shoreline,
No Clouds
“SRTM Plus”: Synergism of inputs for a superior DEM
“SRTM Plus” also includes a ‘NUM’ (number) file that identifies the data source
and number of data takes (ASTER scenes or SRTM swaths) for each pixel.
Crippen / Kobrick, JPL

## Slide 11
ASTER Global Digital Elevation Model (GDEM)
1-arc-sec (30-m) data for land areas ±83°
  Release dates:
    Version 1 – 2009
    Version 2 – 2011
    Version 3 – 2017?

## Slide 12: Methodology
ASTER GDEM
ASTER coverage (~1.5 million scenes in summer 2008)
Deeper red indicates more data accumulated.
Generation of a seamless tile of DEM using all ASTER data ever acquired over the tile
A seamless Tile of DEM
GEOSS
Both US and Japan committed to contribute to GEOSS at Capetown Summit 2007.
Contribution to
Global coverage
Automated processing
ASTER scene
(60km x 60km)
Tile (1 arc degree square)
1. Stereo-correlate entire ~ 1.5 million scene ASTER Archive; 2. Cloud mask to remove cloudy pixels;
3. Stack all DEMS & remove residual bad values and outliers; 4. Partition data into 1º x 1º tiles ---
SRTM3 coverage
(Courtesy of B. Bailey)
Notes: These 3 components of land remote sensing also are important parts of an “energy flow” known as the energy path concept. The energy path concept describes the flow of energy from its source to the points where it is detected and recorded by the remote sensing system – or sensor.
(read each of the steps list – then discuss each step with the graphic on the next slide.)

## Slide 13
(Courtesy of T. Tachikawa)

## Slide 14
Question: What is a deep, dark secret about global DEMs?
Answer: Grid spacing ≠ true spatial resolution!

## Slide 15
Smith and Sandwell, 2003
Guth, 2006
Pierce et al., 2006

## Slide 16
(Courtesy of T. Tachikawa)

## Slide 17
(Courtesy of T. Tachikawa)

## Slide 18
Resolution
GDEM1
GDEM2
SRTM
121 m
82 m
77 m
Res =
West Virginia: Keyser-Romney area
But at its best, GDEM2 nearly matches SRTM 1-arc-second data.
9x9 kernel
5x5 kernel
(Courtesy of R. Crippen)

## Slide 19
Global Multi-resolution Terrain Elevation Data (GMTED2010)
A global DEM to replace GTOPO30:
  Multiple elevation layers at three grid spacings: 30-arc-sec (1 km), 15-arc-sec (500 m) 7.5 arc-sec (250 m)
  Derived from “best available” higher resolution data:
    SRTM (void-filled), 1-arc-second
    Canadian Digital Elevation Data (CDED), 0.75 and 3-arc-second
    U.S. National Elevation Dataset (NED), 1 and 2-arc-second
    Digital Terrain Elevation Data (DTED®), 3-arc-second
    SPOT Reference3D®, 15-arc-second
    Australia GEODATA, 9-arc-second
    University of Bristol Greenland radar altimeter DEM, 30-arc-sec
    University of Bristol Antarctica ERS-1 radar altimeter and ICEsat laser altimeter DEM, 30-arc-second

## Slide 20: GMTED2010 Source Data
(Courtesy of J. Danielson)
Notes: GOS
Harvesting requirements – clearing house for metadata?
Data Requests and Planned Acquisitions

## Slide 21: GMTED2010 Spatially Referenced Metadata
Metadata fields and values captured at full resolution from the input source data
(Courtesy of J. Danielson)
Notes: GOS
Harvesting requirements – clearing house for metadata?
Data Requests and Planned Acquisitions

## Slide 22: GMTED2010 vs. GTOPO30
Min.
Max.
Mean
Std.Dev.
Median
Sample
Breakline
Min.
Max.
Mean
Std.Dev.
Median
Sample
Breakline
Min.
Max.
Mean
Std.Dev.
Median
Sample
Breakline
“Representative Elevation”
30 arc-sec
(1-km)
30 arc-sec
(1-km)
15 arc-sec
(500-m)
7.5 arc-sec
(250-m)
A mix of systematic subsampling, median value generalization, breakline emphasis generalization, bilinear resampling, and vector-to-raster interpolation
Notes: GOS
Harvesting requirements – clearing house for metadata?
Data Requests and Planned Acquisitions

## Slide 23
GMTED2010 - Public Release in August 2011
https://lta.cr.usgs.gov/GMTED2010
http://topotools.cr.usgs.gov/GMTED_viewer/
http://earthexplorer.usgs.gov/
GMTED2010 Viewer
Earth Explorer
(Courtesy of J. Danielson)

## Slide 24
TanDEM-X
(TerraSAR-X add-on for Digital Elevation Measurement)
TanDEM-X is an extension of the TerraSAR-X mission with a second satellite flying in close formation
  X-band SAR interferometry system
  Flying in formation since 2010, collected data for global DEM for four years
  Completion of global DEM in 2016

## Slide 25
TanDEM-X
Mission objective:
  Global DEM at 0.4-arc-second (12-m) grid spacing
    90-m free version to be available
  Accuracy specifications:
    Absolute vertical: 10 m (linear error at 90% confidence)
    Relative vertical (point-to-point within 1°x1° tile):
      2 m (slopes < 20%)
      4 m (slopes > 20%)

## Slide 27
WorldDEM DSM

## Slide 28
WorldDEM DTM

## Slide 29
ALOS World 3D
(AW3D)
PRISM (Panchromatic Remote-sensing Instrument for Stereo Mapping)
  On board ALOS (Advanced Land Observing Satellite)
  Stereo-optical image data (2.5-m resolution)
    Stereo triplets: nadir, +23.8°, -23.8°

## Slide 30
ALOS World 3D
(AW3D)
PRISM collected 3 million scenes (<30% cloud cover) across the globe in 2006-2011
Global DEM (DSM) specifications:
  Grid spacing = 0.15-arc-sec (5-m)
    30-m free version is available
  Absolute vertical accuracy = 5 m (RMSE)
  Absolute geolocation accuracy = 5 m (RMSE)
  Production uses stacking (averaging) method
  Completion of global DEM in 2016

## Slide 31
(Courtesy of T. Tadono)
PRISM Stereo Scenes for AW3D

## Slide 32
Data are distributed commercially by NTT DATA Corporation and RESTEC
ALOS World 3D – Current Coverage

## Slide 33
ICESat (Ice, Cloud, and land Elevation Satellite) -
GLAS (Geoscience Laser Altimeter System)
Operated 2003 – 2009 (±86 degrees latitude)
70-m laser footprint spaced every 170 m along profile
  Better than 10-cm vertical accuracy in best cases, usually around a meter or better in many cases
Used extensively for validation of global DEMs
  SRTM, ASTER GDEM, GMTED2010, PRISM (AW3D), TanDEM-X
Used for production processing of global DEMs
  PRISM (AW3D), TanDEM-X, NASADEM

## Slide 34: ICESat / GLAS
Convergence of ICESat’s orbital paths near the poles resulted in close spacing of laser profiles allowing for generation of gridded continuous surface DEMs
ICESat full waveform data can be processed to derive multiple surfaces within the laser footprint (ground level and vegetation canopy top), which has been exploited for global forest height mapping
Antarctica 500-m DEM
Greenland 1-km DEM
(Lefsky, 2010)
(Simard et al., 2011)

## Slide 36
(Courtesy of P. Morin)
4-m vertical accuracy
Based on 2012 – 2016 imagery
Digital surface model (DSM)
Alaska release in 2016
Arctic release in 2017
Unrestricted data

## Slide 38
Comparison of Global DEMs
DEM | Grid spacing (m) | Absolute vertical accuracy specification (m) |  | 
 |  | RMSE | LE90 | LE95
SRTM | 30 | 9.7 | 16 | 19.07
ASTER GDEM | 30 | 10.2 | 16.78 | 20
TanDEM-X (WorldDEM) | 12 | 6.08 | 10 | 11.92
PRISM (AW3D) | 5 | 5 | 8.22 | 9.8
RMSE = Root Mean Square Error
(RMSE is equivalent to the standard deviation [1σ] when errors are normally distributed and the mean error = 0)
LE90 = Linear Error at 90% confidence = RMSE * 1.6449
LE95 = Linear Error at 95% confidence = RMSE * 1.96
References:
Greenwalt and Shultz, 1962
Maune et al., 2007

## Slide 39
(Courtesy of R. Crippen)
NASADEM - A New NASA Digital Topographic Data Set
Jet Propulsion
Laboratory
SAR processing (updated)
Continental Adjustment
Raw radar echoes
Updated strip DEMs
‘New’ SRTM Global DEM
Artifact removal
Modified GDEM2
ASTER GDEM2
Merge corrected DEMs
NASADEM + associated products:
Slope, Aspect, Curvature, Images,
Errors, Correlation
Current SRTM
Global DEM
IceSAT
Data Set
SRTM Water
Body Data
Key:
Pink: New data set or process
Yellow: Existing data set or process
Process
Void-fill
SRTM
Metric Data
(mostly) void-
filled SRTM (ver3)
NED, CDED, et al
Remaining
void map
Acquire new
ASTER DEMs
Artifact removal
New ASTER DEMs
Modified DEMs
LPDAAC
NASADEM

## Slide 40
SRTM
Reunion Island
(Courtesy of R. Crippen)

## Slide 41
GDEM
Reunion Island
(Courtesy of R. Crippen)

## Slide 42
NASADEM
Reunion Island
(Courtesy of R. Crippen)
- Complete re-processing of SRTM radar data
- To be completed and released in 2017
- 30-m freely available void-filled DEM
- Includes error map and derivative products

## Slide 43: NASADEM Project Overview
Create an improved global NASA DEM and associated products
  Reprocess SRTM raw sensor data
  Merge with recent elevation data
  Release at one arcsecond
SRTM processing changes
  Improve phase unwrapping
  Reduce height ripples
  Use ICESat as control
New / additional data layers
  Height error layer (precision est.)
  Correlation
  DEM slope/aspect and curvature
  Veg bias estimates (experimental)
Deliver provisional products to LPDAAC by continent with potential update at project end
Planned 1 arcsec
Existing 3 arcsec
Andes Mountains in Chile and Bolivia
DEM height ripples over Australia from unmeasured boom motion.
Criss-cross pattern comes from merging SRTM strips. Difference of original SRTM & ripple removal demo.
(Courtesy of S. Buckley)

## Slide 44: NASADEM Products
Product* | Brief Description | Delivery Format | Approx. # Files | Uncompressed & Compressed Size | 
Void-Filled DEM | Elevations in 1x1-degree tile | 16-bit signed int, meters | 15,000 | 370 GB | 105 GB
NUM Files | Identifying data source, # inputs | 8-bit | 15,000 | 185 GB | 3 GB
Topographic Slope | Derived from void-filled DEM | 16-bit unsigned int, hundredth degree | 15,000 | 370 GB | –
Slope Aspect | Derived from void-filled DEM | 16-bit unsigned int, hundredth degree | 15,000 | 370 GB | –
Profile Curvature | Derived from void-filled DEM | 16-bit unsigned int, hundredth 1/meter | 15,000 | 370 GB | –
Plan Curvature | Derived from void-filled DEM | 16-bit unsigned int, hundredth 1/meter | 15,000 | 370 GB | –
Radar Images | Per image, subswath & tile | 8-bit | 175,000 | – | 195 GB
Radar Incidence Angle | Per image, subswath & tile | 16-bit unsigned int, hundredth degree | 175,000 | – | 391 GB
Merged Radar Images | Per tile | 8-bit | 15,000 | – | 55 GB
Radar Image Times | For each image tile | ASCII text file | 1 | Several MB | 
Merged Radar Image NUMs | Number of images merged per pixel | 8-bit | 15,000 | – | 55 GB
Height Error | Height precision estimate | 16-bit unsigned int, millimeters | 15,000 | 370 GB | –
Radar Correlation | Per image, subswath & tile | 16-bit unsigned int | 175,000 | Several hundred GB | 
ICESat Single Shot Data | Control, assessment | ASCII text file | 2 | Several GB | 
Vegetation Bias Maps | One for each DEM tile | 16-bit signed int, meters | 15,000 | 370 GB | –
SRTM-Only DEM | Wrt ellipsoid, unaltered water hgts | 32-bit floating point, meters | 15,000 | 740 GB | –
* Bold refers to products also produced as part of MEaSUREs 2006 project
(Courtesy of S. Buckley)

## Slide 45: Expected Delivery Dates to LPDAAC (as of Jan 2017)
Feb 2017
May 2017
Mar 2017
Jul 2017
Aug 2017
Island Groups: Sep 2017
Remaining products: Sep 2017
(Courtesy of S. Buckley)
Recent info (R. Crippen, JPL):
On target for 2017 completion
AW3D 30-m is primary fill source, GDEMv3 is secondary
North of SRTM footprint (> 60°N) may be filled if time allows (AW3D, GDEM, possibly CDED)

## Slide 46: Future Missions
ICESat-2 (scheduled for late-2018 launch)
  ATLAS: Advanced Topographic Laser Altimeter System
    14-m laser footprints spaced very closely (0.7 m) along profile
    Centimeter-level vertical accuracy; ground and canopy products
GEDI (scheduled for 2019 launch)
  Global Ecosystem Dynamics Investigation
  Lidar on board the International Space Station
  Targeting forests between 50°N and 50°S latitude
NISAR (scheduled for 2020 launch)
  NASA-ISRO Synthetic Aperture Radar
  Dual L-band and S-band polarimetric SAR with 12-day repeat pass interferometry capability

## Slide 47: Characteristics Common to Global DEMs
Voids
  Stereo-optical sources:
    Clouds
    Areas of low image contrast (low illumination, shadows, smooth / homogenous surfaces)
  IFSAR:
    Steep terrain causing shadowing, foreshortening, layover
    No radar return from smooth surfaces
  Fix voids by:
    Interpolation
    Fill with other data sources
    Additional data collection (stacking / averaging)

## Slide 48: Characteristics Common to Global DEMs
“First return” – DSM
  Processing required to get to bare earth DTM
Vertical accuracy varies spatially
  By land cover conditions
  By slope and relief conditions
Effective spatial resolution
  Often true resolution is much less than grid spacing
  Influenced by data processing algorithms (e.g., kernel size in image matching, window size for smoothing functions)

## Slide 49: Interdependence of Global DEMs
Incremental improvement as newer global DEMs make use of existing DEMs in production processes for:
  Systematic offset adjustment
  Calibration
  Anomaly detection
  Reference data for QA/QC
  Accuracy assessment
Links:
  SRTM used DTED®
  ASTER GDEM used SRTM
  TanDEM-X uses ICESat and SRTM
  AW3D uses ICESat, SRTM, and ASTER GDEM

## Slide 50
Which global DEM is the best?
Shuttle Radar Topography Mission (SRTM)
PRISM / ALOS World 3D
ASTER Global Digital Elevation Model (GDEM)
TanDEM-X / WorldDEM
The DEM should be “fit for use”:
-Vertical accuracy (absolute & relative)
- DSM vs. DTM
- True resolution
- Date (stack / avg.)
30 m
90 m
30 m
12 m
30 m
90 m
5 m
30 m

## Slide 51
Thank You
Questions?
&
Discussion
gesch@usgs.gov