## Slide 1: NSSC Update of EO Missions and CAL/VAL
Xiaolong DONG
National Space Science Center
Chinese Academy of Sciences
(NSSC,CAS)
CEOS WGCV-43
INPE@ São José dos Campos, SP, Brazil
April 10-13, 2018

## Slide 2
Planning, Development, Management & Operation
of Space Science Missions
(2011~)
NSSC,CAS
National Space Science Center
Chinese Academy of Sciences
Research & Development of
Space Science and Frontier Technology（1958~)

## Slide 3
Space Science Study Center
Mission Management Center
Satellite Operation Center
Space Science Mission Planning, Development and Operation
Research and Development of Space Science and Frontier Technology
Assurance
and Test Center
SKL of
Space Weather
CSKL of
Space Integrated Electronics
CSKL of Space Situational Awareness
CSKL of Microwave Remote Sensing
Department of
Space Science
Department of
Space Technology
Department of
Space Environment
Department of
Microwave
Remote Sensing
GNSS Occultation & Reflection Sounder
Radar & Radiometric Techniques
CAS General System Department for Lunar and Deep Space Explorations

## Slide 4
National Program for Fengyun Meteorological Satellite 2011-2020
7 satellites will be launched within this decade
2012FY-2F(Op)
2010FY-3B (R&D)
2013FY-3C(Op)
2017FY-3D(Op)
2014FY-2G(Op)
2016FY-4A (R&D)
2019 FY-3E(Op)
2020FY-RM(Op)
2019FY-4B (Op)
2020FY-3F(Op)
2021FY-4C(Op)
2018FY-2H(Op)
2021 FY-3G(Op)

## Slide 5
Chinese ocean satellite missions in the future
HY-2A(2011)
HY-3B(2020)
HY-3C(2022,GEO ocean color)
HY-3A(2019)
CFOSAT (2018,Joint mission)
HY-1C(2018)
In-orbit
Approved
Experimental
Considered
HY– 1A
HY-3D(2025,GEO SAR)
HY– 1B
HY-1D(2019)
HY-1E(2023, new)
HY-1F(2024,new)
HY-2B(2018,polar)
HY-2C(2019,low inclined A)
HY-2D(2020, low inclined B)
HY-2E(2022,polar)
HY-2F(2023, low inclined C)
GF-3(2016)
HY-2G(2024,low inclined D)
HY-2H(2022,new generation)
HY-XX(2020,Salinity)
ocean color constellation
ocean monitoring and surveillance satellties
ocean dynamic environment constellation
HY–2A(2011)

## Slide 6
NSSC: Contributions to Oceanographic and Meteorological Satellites
Oceanography and Meteorology
  HY-2 (A, B, C and Follow-on): ALT+ACMR
  COSM: MICAP
  FY-3 and follow-on:
  MWHS/MWHTS(MWHS-II), GNOS,TOU
  SEM (space environment monitoring package)
  CFOSAT: radar scatterometer
  FY-4 (optical and microwave):
  Microwave imager, space environment package

## Slide 7: NSSC 2017 EO mission update
FY-3D launched on Nov 15, 2017
CFOSAT SCAT flight model delivered
HY-2B DFRA, ACMR flight model delivered
TanSAT handover
TG-2 InRA in orbit commissioning completed

## Slide 8
CFOSAT update
Payloads:
  SWIM: multiple beam radar for ocean surface wave spectrum (Ku band, by CNES)
  SCAT: rotating fan-beam scatterometer of ocean surface wind vector (ku band, by NSSC)
Schedule
  delivery of flight model: 2017.06-07
  Launch schedule: September 2018

## Slide 9
HY-2 update
HY-2A：in orbit >5yrs (2011.08.16)
  New version of ALT data
HY-2B：flight model delivered
  DFRA: dual frequency radar altimeter：Ku (13.58GHz) & C (5.25GHz)
  ACMR: atmospheric correction microwave radiometer: 18.7，23.8，37GHz
  SCAT: radar scatterometer: Ku-band (RF switch network & receiver
HY-2C：flight model started
Launch Plan:
  HY-2B: 2nd half of 2018
  HY-2C: 1st half of 2019 (inclined orbit)

## Slide 10
COSM update
Chinese Ocean Salinity Mission
Mission requirements:
– 0.1psu, 200km, monthly
– With Simultaneous observation of ocean surface roughness and SST
Schedule
– 2011~2014: grounddemonstration
on different payload technology
– 2015~2006: mission definition, preliminary design, risk mitigation
– 2017: pre-study acceptance
– 2018: kick-off implementation
– Planned launch: 2021
2 payloads:
MICAP: microwave imager combined active passive (L, C, K band) (NSSC)
MiR2D: microwave 2-D interferometric imager (CAST-Xian)

## Slide 11
11
ok
Microwave
Temperature
Sounder (MWTS)
4 channel (FY-3A/B)
13 channels (FY-3C/D)
Microwave
Humidity
Sounder (MWHS)
5 channel (FY-3A/B)
15channels with channels@118 GHz (FY-3C/D)
Infrared
Atmospheric Sounder
(IRAS)
20 channels
Microwave
Radiation Imager
10 channels
The FY-3A/B/C/D Instrument Suite
GNSS
GNSS-Occultation
Sounder (GNOS)
(GPS, Beidou)
(FY-3C/D)
TOU
Total Ozone Unit
(FY-3A/B/C)
Notes: 11
11
11
11

## Slide 12
FY-3 update
FY-3A/B
  MWHS: Microwave humidity Sounder
  5 Channels: 150GHz: H, V-pol; 183GHz: 3channels for vapor
  FY-3A ended (launched 2008)
  FY-3B in good status (from 2010)
FY-3C/D
  MWHTS: Microwave Humidity and Temperature Sounders
  15Channels: 90GHz, 150GHz, 118GHz, 183GHz
  FY-3C: MWHTS, GNOS in good status since 2013
  FY-3D: launched on November 15, 2017

## Slide 13: HY-2 Follow-On Pathfinder Mission: Tiangong-2 Interferometric Imaging Radar Altimeter
Interferometric Imaging Radar Altimeter (InIRA)
  Ku-band (13.58GHz) wide swath inteferometric radaer altimeter
  Flown on Chinese Tiangong-2 space laboratory
  Launched on September 15, 2016
Objectives:
  wide-swath sea surface height at mesoscale and sub-mesoscale, sea waves and sea winds.
  Inland waters, e.g., lakes and rivers, coasts.

## Slide 14
Antennas of Tiangong-2 InIRA
Tiangong-2
space laboratory
Shenzhou XI manned spaceflight
Parameters of Tiangong-2 InIRA | 
Frequency | Ku band
Bandwidth | 40MHz
Range resolution | 200m~30m
Azimuth resolution | 30m
Swath | 30-35km
Orbit error | 20cm
Vertical accuracy of sea surface | 25cm absolute vertical accuracy in a 5km × 5km raster
Vertical accuracy of land surface | 1~5m absolute vertical accuracy in a 200m × 200m raster
Accuracy of wave direction | 15º

## Slide 15
Calibration Experiment (Collaboration with AOE, CAS)
Reflector | Number | RCS(dBsm) | S-C-R
0.8m triangle | 1 | 35.50 | 4.5
1.0m triangle | 9 | 39.37 | 8.37
1.2m triangle | 1 | 42.54 | 11.54
1.5m triangle | 9 | 46.38 | 15.38
2.0m rectangular | 2 | 60.92 | 29.92
Background NRCS：-3dB；
InIRA surface resolution： 50m X 50m
1st Experiment
2nd Experiment

## Slide 16
1st Experiment reflector distribution

## Slide 17
1
2
3
4
No | InIRA (m) (WGS84 ) | GPSm (85高程基准)
1 | 1281.77488920 | 1275.683
2 | 1299.21366239 | 1290.444
3 | 1298.86098894 | 1289.867
4 | 1300.20181014 | 1290.641
No | InIRA relative (m) | GPS relative (m) | Bias (m)
1-2 | -17.4388 | -14.7610 | -2.6778
1-3 | -17.4388 | -14.1840 | -3.2548
1-4 | -18.4269 | -14.9580 | -3.4689
2-3 | 0.3527 | 0.5770 | -0.2243
2-4 | -0.9881 | -0.1970 | -0.7911
3-4 | -1.3408 | -0.7740 | -0.5668
Bias：-1.8306m，
Std：1.465m
1st Experiment DEM result

## Slide 18
2nd Experiment reflector distribution

## Slide 19
挖坑固定
钢钎固定
底座固定

## Slide 20
Phase Center determiantion

## Slide 21
2nd Experiment Imaging of relfectors

## Slide 22
 | InRA（m） | Static GPS（m） | Bias （m） | RCS relative(dB)
P1（1.5m） | 1277.9139 | 1274.3707 | 3.5432 | 8.494
P2（1.5m） | 1285.6256 | 1282.2367 | 3.3889 | 8.734
P3（1.5m） | 1279.3402 | 1279.0957 | 0.2445 | 6.568
P4（2.0m） | 1271.8319 | 1273.5137 | -1.6818 | 23.43
P5（1.5m） | 1275.6960 | 1275.4807 | 0.2153 | 8.405
P6（1.5m） | 1276.4786 | 1276.6887 | -0.2101 | 11.90
P7（1.5m） | 1272.0699 | 1272.8907 | -0.8208 | 12.67
P8（2.0m） | 1270.6294 | 1269.6437 | 0.9857 | 19.08
P9（1.5m） | / | / | / | 9.586
P10（1.5m） | 1280.6327 | 1280.6147 | 0.0180 | 14.01
P11（1.5m） | 1282.5860 | 1284.3187 | -1.7327 | 11.38
Absolute bias ≤1.0m

## Slide 23
(-95.95,-3.5)
Tiangong-2 InIRA Image: Pacific Ocean
Ocean waves
Eastern Pacific Ocean at about 1800km west of Ecuador, South America
Observation time:
2016.09.23, 10:14
Notes: 20160923235109_000_0MC_ROM_1tg156_ampHRa

## Slide 24
Amazon River
Peru
Brazil
Amazon River
N
S
Rainforest
Amazon River
Tiangong-2 InIRA Image: Inland river
Amplitude
DEM
Brazil
Amazon River
Rainforest
Colombia
Amazon rainforest at the junction of Brazil, Peru and Colombia
Image Size: 79.3km x 33.6km
Latitude and longitude of image center: (70.0533W, 4.2122S)
Observation time: 2016.09.23, 10:56
Notes: 20160923105609_000_0MC_ROM_1南美tg3_ampHRs

## Slide 25
Tiangong-2 InIRA Image: Sea surface topography (spatial resolution 2km  2km)
19
South Pacific
Notes: I:\TG2_Results\TS_TG02_IALT_PLS_SCI_20160924011611_20160923233510_20160923235109_000_0MC_ROM_1\FullAperture_Precise_Orbit\156

## Slide 26: Wave Spectrum by InIRA

## Slide 27: Preparation of CFOSAT calibration
Amazon forest sigma 0 statistics for Ku-band
Amazon forest sigma 0 incident angle profile regression
NWP ocean calibration preparation

## Slide 28: T/V calibration/Test of FY-3D MWHTS
FY-3D satellite was launched at Nov 2017
Prelaunch calibration was conducted at the same vacuum as the previous tests;
Multi-angle Cal. Configuration was designed for testing if the scanning angle variations would lead to the calibration precision, which was found by comparing in-orbit measurements with simulated TB by RTM, such as RTTOV or CRTM.

## Slide 29
Essential calibration coefficients such as cold bias, hot bias and nonlinearity coefficients and calibration results like calibration residual error, sensitivity and calibration accuracy of MWHTS are all obtained and analyzed in MWHTS’s six observing positions.
The measured sensitivity values of channel 2 is 1.5K while the measured sensitivities of the others range from 0.18 K to 0.57K.
The calibration accuracies of channel 2 is 1.6K while the calibration accuracies of the others range from 0.22 K to 0.64K.
The problems met in data processing such as radiation leakage at channel 14 and response lag at channel 15 for special channels are minutely analyzed.
Moreover, the measurements of the T/V test with fast changing instrument temperatures are analyzed and the applicability of nonlinearity coefficients obtained in T/V test for in-orbit calibration is verified.
Summarily, MWHTS meets the basic design requirements, and the changing of MWHTS observing position does not impact the calibration nonlinearity coefficients and calibration residues.
Radiation leakage analysis of channel 14
Response lag of channel 15 when observing the Earth target

## Slide 30: Postlaunch calibration/Validation of FY-3 MWHS
Calibration consistency study on FY-3A,3B,3C microwave radiometers were supported.
Combining with FY-3D launched last year, a series of sounders and imagers database will be recalibrated by cross- or inter- calibration, and finally a set of consistent datasets will support the studies on climate and related applications.
Zou, C.-Z., and W. Wang (2011), Intersatellite calibration of AMSU-A observations for weather and climate applications, J. Geophys. Res., 116, D23113, doi:10.1029/2011JD016205
FY-3 Satellite | Interval of the measurements | Calibration Precision | Period (s)
MWHS/MWHTS | FY-3A:2008.6.4--2014.5.5 |  | 8/3
 | FY-3B:2011.11---- |  | 8/3
 | FY-3C:2013.9---- | 0.88-2.09K | 8/3
MWRI | FY-3A:2008.6.4 |  | 1.7
 | FY-3B:2011.11.11-- |  | 1.7
 | FY-3C:2013.9.29-- | 2.23-8.72 | 1.7
MWTS | FY-3A:2008.6.4--2012.12.21 |  | 16
 | FY-3B:2011.11--2014.1.22 |  | 16
 | FY-3C:2013.9--2014.5 |  | 8/3
The same plans are planning for HY-2 satellite for microwave scanning radiometer, altimeter and scatterometer.
Atmospheric Correction MR cross-cal. with JMR shows below.
Before cal.
After cal.

## Slide 31
Channel | Central wavelentgh (nm) | Band width (nm)
1 | 308.680.15 | 1.0+0.3, -0.0
2 | 312.590.15 | 1.0+0.3, -0.0
3 | 317.610.15 | 1.0+0.3, -0.0
4 | 322.400.15 | 1.0+0.3, -0.0
5 | 331.310.15 | 1.0+0.3, -0.0
6 | 360.110.25 | 1.0+0.3, -0.0
Picture of FY-3A/TOU:optical assembly and eletronical unit
Spectral propterties
Parameter | Value
Detector | Multiplier Tube detector (PMT)
FOV | 3.6°×3.6°
Spatial Resolution | 50km at Nadir
Swath width | 2908km
Number of samples/scan | 31 points in 8.16s
Operation modes | 1. Normal scan 2. Wavelength monitoring 3. Radiometric Calibration
Scientific objectives | Total column ozone, Aerosol, volcanic SO2
Instrument Characteristics
FY-3 TOU cross-validation （HM Wang, NSSC)
It has a single, fixed Ebert-Fastie monochromator with a fixed grating and an array of exit slits

## Slide 32
Comparisons for clear sky earth’s radiance and solar irradiance for FY-3B/C
FY-3A/TOU: 5th and 6th channel ‘s higher about 17-20%,caused by reflectivity of satellite coat
FY-3B/TOU: all channels have good agreement, about 2%
FY-3C/TOU: atmospheric radiance mode work well, but solar irradiance mode has problem,

## Slide 33
Comparison of total ozone between FY-3B/TOU and Brewer (Finland).
Mean deviation: 1.45%，RMS Deviation: 2.65%，
R2: 0.9866
Chart: FY-3A/TOU与Metop-B/GOME-2 L1B交叉比对 (2013年8月6-11日间)
Comparison of total ozone between FY-3B/TOU and Metop-B/GOME-2.
R2:0.9937
(Results by Wang Weihe,CMA)

## Slide 34
FY-3A/TOU vs NPP/OMPS L1B (2013.10.1-13）
y = 1.1216x + 0.0075 R²= 0.9711
0.4
0.35
0.3
0.25
0.2
0.15
0.1
0.05
0
0
0.4
OMPS (μW/cm2/nm/sr)
0.1 0.2 0.3
TOU (μW/cm2/nm/sr)
308 nm
y = 1.059x + 0.0064 R²= 0.9883
0
0.2
0.4
0.6
0.8
1
1.2
0
0.5
1
1.5
OMPS
TOU
312 nm
y = 1.1071x + 0.0187 R²= 0.9883
0
0.5
1
1.5
2
2.5
3
0
2
2.5
OMPS (μW/cm2/nm/sr)
0.5 1 1.5
TOU (μW/cm2/nm/sr)
317 nm
y = 1.1477x + 0.0194 R²= 0.9884
0
0.5
1
1.5
2
2.5
3
3.5
0
3
OMPS (μW/cm2/nm/sr)
1 2
TOU (μW/cm2/nm/sr)
322 nm
y = 1.0427x + 0.0314 R²= 0.9861
0
1
2
3
4
5
6
7
0
6
OMP (μW/cm2/nm/sr)S
2 4
TOU (μW/cm2/nm/sr)
331 nm
y = 0.9476x + 0.069
R²= 0.9806
9
8
7
6
5
4
3
2
1
0
0
2
8
10
OMPS (μW/cm2/nm/sr)
4 6
TOU (μW/cm2/nm/sr)
360 nm

## Slide 35: FY-3C/TOU vs Metop-B/GOME-2 L1B (2016.11.1-5)
y = 1.5274x + 0.0052 R²= 0.9974
0
0.5
1
1.5
2
2.5
0
2
FY-3C/TOU
(μW/cm2/nm/sr)
312 nm
0.5 1 1.5
MetopB/GOME-2 (μW/cm2/nm/sr)
y = 1.6111x + 0.007 R²= 0.9968
4.5
4
3.5
3
2.5
2
1.5
1
0.5
0
0
3
FY-3C/TOU
(μW/cm2/nm/sr)
1 2
MetopB/GOME-2 (μW/cm2/nm/sr)
317 nm
y = 1.7127x - 0.0151 R²= 0.9965
6
5
4
3
2
1
0
0
4
FY-3C/TOU
(μW/cm2/nm/sr)
322 nm
1 2 3
MetopB/GOME-2 (μW/cm2/nm/sr)
y = 1.665x - 0.0648 R²= 0.9957
9
8
7
6
5
4
3
2
1
0
0
6
FY-3C/TOU
(μW/cm2/nm/sr)
2 4
MetopB/GOME-2 (μW/cm2/nm/sr)
331 nm
y = 1.713x - 0.0223 R²= 0.9942
12
10
8
6
4
2
0
0
8
FY-3C/TOU
(μW/cm2/nm/sr)
360 nm
2 4 6
MetopB/GOME-2 (μW/cm2/nm/sr)

## Slide 36: FY-3C/TOU vs Metop-B/GOME-2 L1B (2016.7.15-20)
Almost all R2>0.95
y = 1.4523x - 0.0228 R²= 0.9693
1.6
1.4
1.2
1
0.8
0.6
0.4
0.2
0
0
FY-3C/TOU
(μW/cm2/nm/sr)
0.5 1
MetopB/GOME-2 (μW/cm2/nm/sr)
312 nm
y = 1.5171x - 0.0491 R²= 0.96
3.5
3
2.5
2
1.5
1
0.5
0
0
2
FY-3C/TOU
(μW/cm2/nm/sr)
317 nm
0.5 1 1.5
MetopB/GOME-2 (μW/cm2/nm/sr)
y = 1.645x - 0.1164
R²= 0.953
5
4.5
4
3.5
3
2.5
2
1.5
1
0.5
0
0
3
FY-3C/TOU
(μW/cm2/nm/sr)
1 2
MetopB/GOME-2 (μW/cm2/nm/sr)
322 nm
y = 1.6133x - 0.2752 R²= 0.9466
10
9
8
7
6
5
4
3
2
1
0
0
6
FY-3C/TOU
(μW/cm2/nm/sr)
2 4
MetopB/GOME-2 (μW/cm2/nm/sr)
331 nm
y = 1.6756x - 0.3019 R²= 0.9559
0
14
12
10
8
6
4
2
0
8
FY-3C/TOU
(μW/cm2/nm/sr)
360 nm
2 4 6
MetopB/GOME-2 (μW/cm2/nm/sr)

## Slide 37
2013/2/1
2013/6/1
2013/10/1
2014/6/1
2014/10/1
2015/2/1
Equation slope
2014/2/1
Date
TOU 312
TOU 331
TOU 360
(1) FY-3A/TOU vs Metop-B/GOME-2
< 6.6 μW/cm2/nm/sr
1.6
1.4
1.2
1
0.8
TOU 317 TOU 322
TOU/GOME-2

## Slide 38
20140223
20140319
20140604
20140709
TOU
(2) FY-3C/TOU vs NPP/OMPS
The slope of equation (Radiance to Radiance)
1.2
1
0.8
0.6
312 nm
317 nm
20140413 20140513
OMPS
322 nm 331 nm
360 nm
308 nm

## Slide 39
TOU
312 nm
317 nm
Metop-B/GOME-2
322 nm 331 nm
360 nm
(3) FY-3C/TOU vs Metop-B/GOME-2
The slope of equation (Radiance to Radiance)
1.8
1.6
1.4
1.2
1
0.8
0.6

## Slide 40: Full polarized calibration method and standard
full-polarized calibration target was tested and applied for digital-correlation microwave polarimeter.

## Slide 41: Active calibration Load for Low Frequency MWR
L and C band active calibration loads ColdFET were tested with a LN cold target, and shown that the TB were at
L- ColdFET
C- ColdFET
Stability of L-ColdFET to LN
L noise TB & physical temp.
C noise TB & physical temp.
Stability of C-ColdFET