## Slide 1: Radiometric calibration network for vicarious calibration of Earth observing imagers in the reflected solar
K. Thome
NASA/GSFC

## Slide 2: RadCalNet architecture overview
Architecture developed has three main parts
1) Test sites provide data to RadCalNet
2) Centralized processing of data
3) Distribution of top-of-atmosphere reflectance
RadCalNet - Radiometric Calibration Network

## Slide 3: RadCalNet – New Candidate sites
Current RadCalNet Sites
Baotou, China
Railroad Valley Playa, USA
>20 years working experience on site
6 radiometers, sun photometer, met station
Dry lakebed
La Crau, France
CIMEL photometer (12 bands)
Pebbles and low vegetation
Site used since 1987 for calibration and instrumented since 1997
Baotou, China (two sitest)
Three automated spectrometers + sun photometer
Artificial target (white, black, and gray)
Operational since 2015
Sandy desert site added in 2017
Gobabeb, Namibia
Sun photometer similar to La Crau) and met station
Sparse dry grass and gravel/sand
Operational since 2017

## Slide 4: Test sites provide pre-processed input data to RadCalNet
Standardized RadCalNet processing stream
Standardized output
Site-specific output
Site-specific output
Standardized input from RadCalNet sites
Sites perform QA on their data
RadCalNet does not standardize collection and processing schemes of sites
Sites have developed additional RadCalNet dedicated processing

## Slide 5: Predict nadir-viewing top-of-atmosphere reflectance and uncertainties
Calibration
& QC
& Processing
L1
QC
& Processing
L2
Calibration
& QC
& Processing
L1
QC
& Processing
L2
Surface Reflectance
30 minute intervals
9 am to 3 pm local standard time
Nadir view
10 nm intervals from 400 nm to 1000 nm
Atmospheric Data
Pressure
Temperature
Aerosol
Water Vapor
Ozone
Uncertainty
RadCalNet Inputs
RADCALNET
QC
& Processing
RADCALNET portal
Hyperspectral TOA reflectance @ 30 min interval for nadir view
RadCalNet Outputs
TOA Reflectance with Uncertainties
30 minute intervals
9 am to 3 pm local standard time
Nadir view
10 nm intervals from 400 nm to 1000 nm

## Slide 6: Teams work to evaluate SI-traceability and error budgets
Relying on process outlined in NPL Uncertainty Analysis for Earth Observation course (www.meteoc.org/training.html)
Sites have responsibility for their own quality assurance and providing uncertainties for inputs
Uncertainty budgets include:
  Instrumentation effects
  Data sources
  Spatial homogeneity of site
  Radiative transfer code
  Sampling
  Processing assumptions
Analysis performed using a combination of literature, laboratory results, Monte Carlo analysis, image analyses

## Slide 7: Per data point uncertainties
Monte Carlo results based on input uncertainties to radiative transfer code modeling of predicted top-of-atmosphere radiance
High aerosol loading with large sized aerosols for small solar zenith angle and six surface reflectance values
Applied Optics
Vol. 61, Issue 6, pp. 1357-1368 (2022)
https://doi.org/10.1364/AO.442170

## Slide 8: User statistics
Recent drop in number of users due to need for users to update their information

## Slide 9: RadCalNet data has been openly available since Summer 2018
Currently 418 users with numbers continuing to increase
Global distribution

## Slide 10: Data quality control
Temporal evolution of reflectances
  RVUS site
  LCFE site
Annual BOA reflectances histogram
2100
550
440
870
1600

## Slide 11: Collection 2022 Preparation
Lessons learned from past three years led to decision to reprocess
Input files revised/updated at site owner’s discretion
  BTCN, BSCN – instrument temperature correction applied ~2021-present
  GONA, LCFR – new calibration applied ~2020-present
  RVUS – now uses MODTRAN 6, reprocessed entire archive
Output files reprocessed to new version:
  Radiative Transfer Code changed to MODTRAN 6.0.2r2
  Atmospheric CO2 amount no longer treated as constant
 | Input | Date Range | Output
BSCN | v00.03 v00.04 | 2017_177 – 2020_287 2020_290 – 2021_332 | v04.03 v04.04
BTCN | v00.03 v00.04 | 2016_096 – 2020_263 2021_097 – 2021_332 | v04.03 v04.04
GONA | v00.04 v00.06 | 2017_200 – 2020_064 2020_068 – 2022_056 | v04.04 v04.06
LCFR | v00.02 v00.04 | 2015_006 – 2019_260 2019_283 – 2021_300 | v04.02 v04.04
RVUS | v00.05 | 2013_091 – 2022_058 | v04.05

## Slide 12: RadCalNet Data Re-Processing Status
Reprocessing to v04 output of entire data archive is complete and under review by the RadCalNet working group
  RadCalNet Working Group meeting April 14 to evaluate progress of re-processing
Expected release to public in late April 2022
Current v04 processing totals (as of March 18, 2022)
Site | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | Total
RVUS | 193 | 237 | 225 | 222 | 264 | 246 | 246 | 263 | 250 | 48 | 2194
LCFR | - | - | 117 | 139 | 151 | 114 | 155 | 115 | 96 |  | 887
BTCN | - | - | - | 52 | 76 | 108 | 102 | 30 | 85 |  | 453
GONA | - | - | - | - | 136 | 160 | 286 | 215 | 222 | 20 | 1039
BSCN | - | - | - | - | 15 | 41 | 73 | 41 | 80 |  | 250

## Slide 13: Documentation Updates
G5-RadCalNetGuidance-Peer-ReviewAndComparison_V2.pdf
Has been uploaded on the portal
  https://www.radcalnet.org

## Slide 14: Acceptance process for new sites
RadCalNet WG members contribute to the review
Process overseen by WGCV
Through an acceptance panel reporting to WGCV

## Slide 15: RadCalNet – New Candidate sites
Pinnacles, Australia (CSIRO)
Baotou, China
Planned installation of sun photometer similar to La Crau) and met station
CSIRO team is in contact with NPL and CNES related to data processing and data quality assessment
Sand dunes in Nambung National Park, north of Perth, Australia

## Slide 16: RadCalNet – New Candidate sites
Dunhuang, China (CMA)
Baotou, China
Radiometers, sun photometer, met station
30x30 km area of Gobi Desert covered with sandy soil and gravel
Used for vicarious calibration since 2008

## Slide 17: RadCalNet – New Candidate sites
Golmud, China (AIR/CAS)
Baotou, China
Initial field campaigns completed. Automated instrumentation to be deployed.
5x5 km area of Gobi Desert covered with sandy soil and gravel
Radiance / W m-2 um-1 sr-1
Wavelength / nm

## Slide 18: Thank you to RadCalNet Team
Baotou, China
Brian Wenny
Nigel Fox, Emma Woolliams,
Agnieszka Bialek
Aime Meygret,
Patrice Henry,
Sebastien Marcq
Marc Bouvet (Chair), Philippe Goryl
Jeffrey Czapla-
Myers
Lingling Ma
Chuanrong Li
Beatrice Berthelot