## Slide 1: WGCV-52 Presentation Template and Guidance
Xiaolong DONG, NRSCC/NSSC
Agenda Item 2.5
WGCV-52, ESA/ESRIN, Italy
5th - 9th June 2023

## Slide 2
MSSG covers EO sensors operated in microwave spectrum, except SAR
MWR, SCAT, ALT, GNSS-RO/R
  Microwave Radiometers (sounders, imagers) (MWR)
  Radar Scatterometers (surface and volume) (SCAT)
  Radar Altimeters (ALT)
  GNSS-Radio occultation and reflectrometry (GNSS-RO/GNSS-R)
With current focuses on
  Radar Scatterometers (Active Microwave)
  Microwave Radiometers (Passive Microwave)
Recent Focuses of MSSG

## Slide 3
Completed tasks:
  Radar Scatterometers (Active Microwave)
CEOS task CV-20-05: Standards and Metrics for Scatterometers and Wind Retrievals
(ISO-TS initiated in TC-211 plenary in May, 2023)
  Microwave Radiometers (Passive Microwave)
ISO/TS 19159-4:2022 (published in November 2022)
Geographic information — Calibration and validation of remote sensing imagery sensors and data — Part 4: Space-borne passive microwave radiometers (ISO TC-211 19159-series)
Recent Tasks of MSSG
On-going tasks:
  CV-23-05 Retrieval and validation with high winds with combined active-passive microwave measurements (2025 Q2)
  CV-23-06 Retrieval and validation of sea surface atmospheric pressure with microwave remote sensing (2025 Q2)

## Slide 4
Progress of task CV-23-05
CV-23-05: Retrieval and validation with high winds with combined active-passive microwave measurements
Task lead:
Prof. Wenming Lin
Nanjing University of Information Science and Technology (NUIST)

## Slide 5
An extreme wind warning is issued when sustained winds of 32.7 m/s or greater are expected.
Extreme sea surface winds may lead to storm surge, transportation disruptions, injury or death, damage to ships and coastal buildings, and etc.
Monitoring of sea surface extreme winds using satellite-based microwave sensors is of great significance to the Disaster Risk Management authorities in protecting lives and safeguarding property, also to support understanding the turbulent air-sea fluxes, the biogeochemistry and gas fluxes under extreme wind conditions.
The current satellite scatterometer or radiometer-derived extreme winds are far from the “truth”, requiring a re-calibration or re-process task in order to achieve a consistent multi-mission extreme winds.
Introduction
Progress of task CV-23-05

## Slide 6
Best track
NOAA flight trajectory
ASCAT high and extreme winds are much lower than the SFMR reference wind speed (other SCATs’ winds are with similar results, see lower right panel)
Progress of task CV-23-05

## Slide 7
Windsat wind retrieval issues under TC conditions?
ASCAT-A & Windsat winds inconsistent in the range 10-15 m/s when collocated with SFMR
Progress of task CV-23-05

## Slide 8
  To re-calibrate microwave radiometer brightness temperature, radar scatterometer and synthetic aperture radar (SAR) normalized radar cross section (NRCS, 0) product, and to derive a good inter-calibrated high and extreme sea surface wind product from all the mentioned satellite wind sensors.
  To validate the high and extreme winds using collocated NOAA hurricane hunter Stepped Frequency Microwave Radiomater (SFMR) winds as reference.
  To better understand the intrinsic characteristics (e.g., the true spatial scale of each wind source) of the satellite-derived high and extreme winds.
Objective
Progress of task CV-23-05
Towards a consistent multi-mission extreme sea surface wind product

## Slide 9
Task content
  Reference aspect:
  Collocations in storm-centric coordinates: improve storm centre location.
  Spatial representativeness: Look for suitable SFMR upscaling for each SAR, scatterometer & radiometer.
  Satellite aspect:
  Analyze the sensitivity of each sensor measurement under high and extreme wind conditions, improve the radiation and scattering models.
  Re-calibration of radiometer brightness temperature, and radar NRCS.
  Re-calibration and/or re-process the extreme winds from the mentioned sensors.
  High and extreme wind validation using the reference data.
Progress of task CV-23-05

## Slide 10
  Reference aspect:
SFMR upscaling effects at SFMR 1-sec sampling
SFMR upscaling effects at 12.5 km sampling
Spatial scale is a relevant aspect in the verification of satellite-derived winds.
Progress of task CV-23-05

## Slide 11
Ku-VV up-wind
C-VV up-wind
0.1 dB sigma-0 change corresponds to 3.6 m/s wind speed change
Progress of task CV-23-05
  Satellite aspect:
  sensitivity of 0 to high and extreme winds

## Slide 12
C-band cross-polarization backscatter is sensitive to the extreme winds
Progress of task CV-23-05

## Slide 13
Task team
  Nanjing University of Information Science and Technology (NUIST); (Task lead & SAR extreme winds);
  National Space Science Center (NSSC); (Rain effect for extreme winds)
  Royal Netherlands Meteorological Institute (KNMI); (SCAT extreme winds)
  National Ocean Satellite Application Center (NSOAS); (SCAT and RAD extreme winds);
  National Satellite Meteorological Center (NSMC/CMA); (C- and Ku- combined wind)
  National Oceanic and Atmospheric Administration (NOAA); (SFMR reference winds)
  Other potential contributers
Progress of task CV-23-05

## Slide 14
Adjusted ASCAT winds (fitting) consistent with SFMR (as expected)
Original ASCAT winds
Adjusted ASCAT winds
Progress
Portabella, et al., 2022
Progress of task CV-23-05

## Slide 15
Progress
Improved emissivity model
Improved emissivity model + retrieval using low frequency channels, leading to improved estimation of extreme winds (compared to SFMR) (Yin, et al., 2023)
Progress of task CV-23-05

## Slide 16
Error analysis (triple collocation) of multi-mission winds & reference data
Improve the radiation and/or scattering models
Joint SFMR/SAR/SCAT & RAD (statistical & spatial) analysis bring added value
Spatial analysis (RMW, wind radii, etc.) is needed to further validate the satellite-derived winds
Seek for user feedback
Progress of task CV-23-05
Main development issues
Next step
Team meeting for detailed workplan and deliverables

## Slide 17
Progress of task CV-23-06
CV-23-05: Retrieval and validation of sea surface atmospheric pressure with microwave remote sensing
Task lead:
Dr. Zijin ZHANG
National Space Science Center, CAS

## Slide 18
Surface pressure data have important applications in numerical weather prediction (NWP), tropical cyclone forecasting and analysis, global climate change studies.
Currently, ocean surface atmospheric pressure data are mainly provided by buoys and ship measurements. The spatial coverage of in situ data for use by weather forecasters is very poor.
Only remote sensing techniques can obtain surface pressure data with large spatial coverage and high density sampling over oceans. However, no on-orbit sensor is designed for ocean surface pressure observation, and there are no operational surface pressure retrieval products.
Stations reporting surface pressure
Progress of task CV-23-06
Introduction

## Slide 19: Overview of Existing Techniques
19
Instrument | Frequency Band | Accuracy | Disadvantages
Grating spectrometer (Mitchell and O’Brien, 1987) | O2 A band (759-771 nm) | 1~2 hPa (Clear Sky) | Only available in daytime and clear-sky
Global Positioning System radio occultation （Healy, 2013） | L-band L1:1.57542 GHz L2: 1.227 GHz | 1~2 hPa | Horizontal resolution is several hundred kilometers
Airborne differential absorption radar (L. Millan 2014; Lin and Hu 2005) | 50-56 GHz O2 bands | 4~7 hPa | Continuous, large-scale and wide swath observations are not available
Microwave Scatterometer (Patoux et al., 2008; Zhang et al., 2011) | 14.6 GHz (SASS) 13.4 GHz (QuikSCAT) | 1~3 hPa (clear-sky、cloudy and rainy conditions) ~ 20 hpa (hurricanes and typhoons) | Performance during extremely high wind conditions (wind speed >28 m/s) are not satisfactory Data cannot be obtained in real-time
Progress of task CV-23-06

## Slide 20
Retrieving surface atmospheric pressure from spaceborne passive microwave observations
Surface pressure sounding is achieved by microwave radiometers due to their ability to measure the total columnar oxygen absorption.
In the oxygen absorption band (50-70 GHz, 118 GHz) , the total columnar atmospheric absorption is strongly related to column oxygen mass. Oxygen is uniformly mixed in the atmosphere; therefore, the column oxygen mass is directly proportional to the surface pressure.
SNPP/ATMS (50-60 GHz )
FY-3C/MWHTS(118 GHz)
Progress of task CV-23-06

## Slide 21: Advantages of the new technique
21
Advantages:
All weather capability
Day and night capability
High spatiotemporal resolution (<3h, ~16km by multi-satellite joint observation)
Wide swath observations (several thousand km): fast, continuous and stable global observations capability
Applications:
Prediction and forecasting for disasters and extreme weather;
Numerical weather prediction (NWP);
Global climate change studies;
Progress of task CV-23-06

## Slide 22
  To develop and optimize the retrieval models and algorithms for sea surface pressure by passive microwave observations.
  To validate and assess the sea surface pressure data products using collocated in situ measurement data.
  To deliver the all-weather sea surface pressure data product from passive microwave observations.
Objective
Progress of task CV-23-06
Towards all-weather quality ocean surface atmospheric pressure product

## Slide 23
Task team (TBC)
  National Space Science Center (NSSC); (Task lead & retrieval algorithm)
  Shanghai Typhoon Institute (TC data analysis);
  National Satellite Meteorological Center (NSMC/CMA); (MWHT/MWHT data)
  National Ocean Satellite Application Center (NSOAS); (SCAT wind data);
  Hong Kong Observatory (in situ data)
  Other potential contributors
Progress of task CV-23-06

## Slide 24: Development of retrieval algorithms
A backpropagation neural network (BPNN) based retrieval algorithm was established and used to retrieve surface pressure from the input TB data.
The priori information is not required as input of the algorithm. Ocean surface atmospheric pressure data can be rapidly and directly retrieved from radiometric observations.
Progress of task CV-23-06
Progress

## Slide 25: Assessment of the retrieval accuracy
-
Brightness temperature data of spaceborne microwave radiometer - input of the algorithm
- Spatial resolution (nadir): 32 km (SNPP/ATMS and FY-3D/MWTS-II), 16 km (FY-3D/MWHTS, FY-3D/MWHTS)
- Temporal resolution: 2 times/day
ECMWF reanalysis surface pressure data or NCEP GDAS/FNL surface pressure analysis fields– to develop and test the algorithm
- Spatial resolution: 0.25º☓ 0.25º
- Temporal resolution: 6 hours
- The last eight days data of each month are used for independent testing.
In situ surface pressure data (buoys, ships and dropsondes) – to test the algorithm
Progress of task CV-23-06

## Slide 26: Preliminary assessment of by comparing the retrievals from SNPP/ATMS data with ERA-Interim reanalysis
Retrievals correlate well with the ERA-Interim reanalysis surface pressure data.
Retrieval results using the SNPP/ATMS ascending data in August 16, 2016.
Progress of task CV-23-06
Progress

## Slide 27: Preliminary assessment by comparing the retrievals from SNPP/ATMS data with NCEP GDAS/FNL analysis data
27
Retrievals correlate well with the NCEP GDAS/FNL surface pressure analysis data.
The TC structure described by the retrieved surface pressure fields agree well with that described by the NCEP GDAS/FNL 10m wind speeds.
Retrievals
NCEP analysis
Retrievals
NCEP analysis
Retrieved surface pressure shown using contour, and NCEP GDAS/FNL 10m wind speeds shown using shade for tropical storm Jebi at 0604 UTC (top) and 1835 UTC (bottom)1 August 2013.
Progress of task CV-23-06

## Slide 28: Preliminary assessment by comparing the retrieved surface pressure and pressure gradients from FY-3C/MWHTS data with NCEP 10m wind analysis data
28
Retrieved surface pressure (top) shown using contour, surface pressure gradients (bottom) shown using vector and NCEP GDAS/FNL 10m wind speeds shown using shade for typhoon lekima (1909).
The TC structural features described by the retrieved surface pressure fields agree well with that described by the NCEP 10m wind speeds.
The retrieved surface pressure gradients correlate well with surface winds.
Progress of task CV-23-06

## Slide 29: Preliminary assessment by comparing the retrievals from SNPP/ATMS data with in situ data
TC centers
TC core area
(<2o radius from center)
Progress of task CV-23-06

## Slide 30: Preliminary assessment by comparing the retrievals from FY-3C/MWHTS data with in situ data
TC centers
TC core area
(<2o radius from center)
Progress of task CV-23-06

## Slide 31: Summary of the preliminary assessment comparison results between retrievals and In situ data
Data source | RMSE (hPa) |  |  |  |  |  | 
 | Clear sky | Cloudy | Rainy | TC centers |  |  | TC core area
 |  |  |  | TD and TS | TY and HU | STY and Major HU | 
SNPP/ATMS | 1.97 | 2.97 | 3.41 | 4.26 | 6.38 | 9.61 | 3.13
FY-3C/MWHTS | 1.93 | 3.01 | 3.54 | 3.62 | 7.98 | 9.68 | 4.43
50-60 and 118 GHz microwave radiometer has a similar surface pressure sounding ability？
(Requires further validation because the FOVs of SNPP/ATMS and FY-3C/MWHTS are not overlap)
Progress of task CV-23-06

## Slide 32
Comparison of retrievals using FY-3D/MWTS-II and FY-3D/MWHTS data
50-60 and 118 GHz microwave radiometer, which has a better surface pressure sounding ability？
Using the joint passive microwave observations of 50-60 and 118 GHz for surface pressure retrieval, can retrieval accuracy be improved?
FY-3D/MWTS-II (50-60 GHz )
FY-3D/MWHTS(118 GHz)
Their FOVs are partially overlap
The oxygen absorption characteristics are different
Progress of task CV-23-06

## Slide 33: Comparison the retrievals from FY-3D/MWTS-II and FY-3D/MWHTS data with ERA-Interim reanalysis
33
MWTS-II
MWHTS
MWTS-II
MWTS-II
MWHTS
MWHTS
Progress of task CV-23-06

## Slide 34: Compare the retrievals from FY-3D/MWTS-II and FY-3D/MWHTS data with ERA-Interim reanalysis
34
For clear-sky condition, the retrieval performance are similar;
For cloudy and rainy conditions, the retrieval performance of MWTS-II is better than MWHTS
MWTS-II
higher information content
less sensitive to cloud and rain
Progress of task CV-23-06

## Slide 35: Comparison of the retrievals from FY-3D/MWTS-II and FY-3D/MWHTS data with NCEP analysis data
35
1750 UTC, 15 Sep 2019
0614 UTC, 16 Sep 2019
1731 UTC, 16 Sep 2019
Retrievals using MWTS-II data for hurricane Humberto (AL092019).
Retrievals using MWHTS data
NCEP GDAS analysis
For tropical depressions, the performance are similar.
For tropical storms, typhoons and hurricanes, the retrieval performance of MWTS-II is slightly better than MWHTS.
MWTS-II
Higher surface pressure information content
Less sensitive to cloud and rain
Lower spatial resolution
Progress of task CV-23-06

## Slide 36: Combined retrieval with the 50-60 and 118 GHz observations for surface pressure retrieval
Channels used for joint retrieval were selected based on the information content;
The weighted average method was used to match the FY-3D/MWHTS observations (~16km) to the FY-3D/MWTS-II (~32 km) resolution level;
Sensor | Central Frequency (GHz) | BW (MHz) | Sensitivity (K) | Information content of single channel | Cumulative information content
MWTS-II +MWHTS | 51.76 | 400 | 0.28 | 1.7164 | 1.7164
 | 50.3 | 180 | 0.37 | 0.2517 | 1.9681
 | 118.75±5.0 | 2000 | 0.27 | 0.0932 | 2.0613
 | 118.75±3.0 | 1000 | 0.27 | 0.0543 | 2.1155
 | 52.8 | 400 | 0.21 | 0.0344 | 2.1500
 | 54.4 | 400 | 0.19 | 0.0285 | 2.1785
 | 54.94 | 400 | 0.19 | 0.0148 | 2.1932
 | 53.596 | 400 | 0.18 | 0.0085 | 2.2017
 | 118.75±2.5 | 200 | 0.49 | 0.0071 | 2.2088
 | 118.75±1.1 | 200 | 0.52 | 0.0035 | 2.2123
 | 55.5 | 330 | 0.23 | 0.0028 | 2.2152
 | 118.75±0.8 | 200 | 0.65 | 0.0021 | 2.2172
Using the 60 and 118.75 GHz oxygen absorption bands together for surface pressure retrieval, more surface pressure information can be obtained;
The selected channel set is mainly composed of channels centered at the wing of the oxygen absorption band；
Progress of task CV-23-06

## Slide 37: Comparison of the retrievals from FY-3D/MWTS-II + FY-3D/MWHTS data with ERA-Interim reanalysis
Data source | RMSE (hPa) |  | 
 | Clear sky | Cloudy | Rainy
MWTS-II | 1.95 | 2.77 | 3.47
MWHTS | 1.98 | 2.91 | 3.53
MWTS-II+MWHTS | 1.86 | 2.34 | 3.20
MWTS-II+MWHTS achieves better retrieval accuracy.
Using the 50-60 and 118 GHz passive microwave observations together for surface pressure retrieval, more surface pressure information can be obtained, and better retrieval accuracy can be achieved.
Progress of task CV-23-06

## Slide 38
Ocean surface atmospheric pressure data with high spatiotemporal resolution can be retrieved from satellite passive microwave observations for both low and high wind conditions. In situ comparison demonstrates that the retrieval accuracy is better than 2.0 hPa for clear-sky, 3.0 hPa for cloudy, and 3.5 hPa for rainy, 6.0 hPa for TD and TS centers, 8.0 hPa for TY and HU centers, and 10.0 hPa for STY and Major HU centers, respectively; a joint retrieval algorithm is proposed to retrieve surface pressure over oceans using the observations of FY-3D/MWTS-II and FY-3D/ MWHTS together, which shows better retrieval accuracy;
Further optimization of the retrieval model and algorithm still needed;
Validation methodology and data sets need to be developed.
Progress of task CV-23-06
Main development issues
Next step
Team organizing meeting for detailed workplan and deliverables

## Slide 39
Promote the ISO TS on calibration and retrievals of sea surface wind by radar scatterometry, which is the further deliverable of task CV-20-05.
CAL/VAL for GNSS-R.
Other work in preparation

## Slide 40
Thanks!
dongxiaolong@mirslab.cn