## Slide 1: WGCV-53 New Space Calibration Monitoring System
N. Fox, S Hunt UKSA
Agenda Item 1.10
WGCV-53, Córdoba, Argentina
5th - 8th March 2024

## Slide 2: “New Space” Mission Data Quality
Users need to know the extent “new space” missions are fit for quantitative applications
  Activities such ESA EDAP & NASA CSDA
  Discussion fora such as JACIE & VH-RODA
Proposal at VH-RODA 22 (via I. Zuleta) to develop a community matchup comparison system to publish biases of missions wrt references
CEOS New space initiative – response to WGCV-52 ACT-18/19
VH-RODA 2022, ESRIN

## Slide 3: Supporting UK National Activity
Application
Application
Application
Data Centre
Platform
Facility
EO DataHub Platform
Processing
QA

## Slide 4: Match-up “Data Cube”
Product Lookup
Identified Overpasses
Match-up Query
Match-up Dataset
Product Catalogue
Match-up Products
Match-up Index
Data Reader Plugin
Catalogue API Plugin

## Slide 5: Cal/Val Pipeline
Evaluate comparison samples, compensating for observation differences
1
Optimises sensor model calibration parameters to best agree to reference
2
Validates performance though comparison to independent references
3
Matchup
Pre-processing
Comparison Samples
Harmonisation
Sensor Model
Apply
Harmonisation
Harmonised Comparison Samples
Validation
Harmonisation Coefficients
To users
Calibration
Validation
Match-up Datasets

## Slide 6: Proposed Calibration Monitoring System
Build from NPL’s matchup database and cal/val pipeline to answer need from “new space” users – develop a CEOS calibration monitoring system
  Provide location for ”new space” missions to deliver set of products for defined cal/val sites
  Analyse and develop a web dashboard to share results
Started with an initial implementation:
  Sensors – Sentinel-2, Landsat-8, now looking for engagement with commercial providers
  CEOS References – RCN GONA, RCN RRV, Hypernets GONA, with PICS L4 coming later (setting up model will take a little longer)
    Potentially add to list but maintain a minimum core to constrain effort
    Look to have result from a combined comparison of sites

## Slide 8: Considerations for Development
Code to be open sourced
  Gives transparency for users and vendors
  Enables community development
Missions able to join on a voluntary basis
  Software effort on the vendor side – e.g., reader/catalogue plugins
  Matchup products to be delivered to platform, but not intended to be redistributed
Deployment strategy
  Should be set up to run automatically to minimise on-going effort

## Slide 9: Conclusions & Next Steps
Apply NPL’s cal/val pipeline to answer need from “new space” vendor/users – proposed as a CEOS calibration monitoring system
Seeking volunteer Beta test from Newspace to trial integration. Interest from vendors at VH-RODA
Looking to be in position to have live demo site this year