## Slide 1: WGCV 53 SRIX4Veg-II Calperum, South Australia
Cindy Ong, CSIRO
Agenda Item 3.2
WGCV-53, Córdoba, Argentina
5th - 8th March 2024

## Slide 2: SRIX4Veg-II
11-15 March 2024 (next week)
Hosted by TERN & CSIRO
UAV teams
  A: NPL/ESA
  B: TERN
  C: GA
  D: DES
  E: OSS/DCCEEW
  F: MAITEC
Field measurement team
  CSIRO
UAV imagery from 17 May 2022 flown by TERN/UTAS

## Slide 3: SRIX4Veg-II
Slide 3
Site
TERN/LPV supersite Calperum (https://www.tern.org.au/tern-observatory/tern-ecosystem-processes/calperum-mallee-supersite/, https://www.tern.org.au/site-of-the-month-calperum-mallee-supersite/) across 9000 km2 ~270 km E of Adelaide, close to Renmark;
13 years measuring fundamental carbon, water, energy and nutrient pools and fluxes;
                One eddy-covariance flux tower
                Soil water content, temperature and electrical conductivity probes
                Phenocams
                Groundwater bores with nested piezometers
                18 x 1 ha Surveillance monitoring plots
                Airborne LiDAR and hyperspectral imagery calibrated using SLATS star transects, leaf sampling, tree structure and LAI measurements
Mallee semi-arid ecosystem, fringing the River Murray floodplains on Calperum Station, South Australia;
Comprises undulating mallee woodlands and riverine vegetation alongside the river;
Image credit: TERN
Pinnacles
Calperum
Adelaide

## Slide 4: Pre-Fieldwork Workshop

## Slide 5: Site Characteristics
SASMDD0013 (River Gum)
Rounded Noon flower Black box Eucalyptus Slender Ice-plant Giant Red Burr Ruby Saltbush

## Slide 6: Experimental Setup
UAV acquisition area
Reference/Instrument
100 m
UAV flight path

## Slide 7: Target Spaceborne Sensor
Imaging Spectroscopy VNIR-SWIR, 30 m
EnMAP, PRISMA, DESIS, CHIME, SBG
EnMAP (12 & 13 Mar), PRISMA (9 & 14 Mar) & DESIS (9 & 12 Mar) data requested
  Campaign is not specifically for validation of spaceborne sensors
90x90 m or 3x3 pixel acquisition area
Similar surrounding cover type up to 150x150 m or 5x5 pixel

## Slide 8: Reference & Instrumentation Set-up
3x3m reflectance tarp (mounted on low platform)
0.5x 0.5m Permaflect (mounted on low platform)
0.25 x 0.25m Spectralon (tripod)
Gazebo
Safety area
Stop and stare
Stop and stare
Slow traverse
Slow traverse
sun
CIMEL
LI-COR
PAR
Sky Camera &
Weather station
Microtops
Irradiance ASD
Las Tiesas, Barrax Spain measurements of the tarp in July 2022 for SRIX4Veg I

## Slide 9: Scheduling
 |  |  |  | OWN PROTOCOL |  |  |  | Conducting SRIX4Veg protocol |  |  |  |  |  |  |  | 
Date/Time | Sun Elevation | 10 |  | 11 |  | 12 |  | 13 |  | 14 |  | 15 |  |  |  | 
 |  | Sunday |  | Monday |  | TUESDAY |  | WEDNESDAY |  | THURSDAY |  | Friday |  |  |  | 
 |  | SRIX team | Set up site & practice & testing | QUEUING | FLYING | QUEUING | FLYING | QUEUING | FLYING | QUEUING | FLYING | QUEUEING | FLYING |  |  | Conducting own protocol/method
 |  |  |  |  | SETUP |  |  |  |  |  |  |  |  |  |  | Conducting SRIX4Veg protocol
8:00 |  |  |  |  |  | B,D | SETUP | A,B | SETUP | D,A | SETUP |  |  |  |  | Onsite preparing to fly
8:30 |  |  |  |  | PRACTICE |  |  |  |  |  |  |  |  |  |  | 
9:00 | 23.19 |  |  |  |  | F,A | B | C,D | A | E,B | D |  | CONTINGENCY |  | SRIX4Veg-II Teams: | 
9:30 | 29.19 |  |  |  |  |  | D |  | B |  | A |  |  |  | A: NPL/ESA | 
10:00 | 34.97 |  |  |  |  | C,E | F | E,F | C | F,C | E |  |  |  | B: TERN/U Tas | 
10:30 | 40.53 |  |  |  |  |  | A |  | D |  | B |  |  |  | C: GA | 
11:00 | 45.73 |  |  |  |  |  | C |  | E |  | F |  |  |  | D: DES | 
11:30 | 50.41 |  |  |  |  |  | E |  | F |  | C |  |  |  | E: OSS/DCCEEW | 
12:00 | 54.36 |  |  |  |  |  | BREAK |  | BREAK |  | CONTINGENCY |  |  |  | F: MAITEC | 
12:30 | 57.28 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13:00 | 58.90 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13:30 | 59.00 |  |  | A,B |  | D,A |  | B,D |  |  |  |  |  |  |  | 
14:00 | 57.56 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14:30 | 54.78 |  |  | C,D | A | E,B | D | F,A | B |  | PACKDOWN |  | PACKDOWN |  |  | 
15:00 | 50.94 |  |  |  | B |  | A |  | D |  |  |  |  |  |  | 
15:30 | 46.34 |  |  | E,F | C | F,C | E | C,E | F |  |  |  |  |  |  | 
16:00 | 41.19 |  |  |  | D |  | B |  | A |  |  |  |  |  |  | 
16:30 | 35.67 |  |  |  | E |  | F |  | C |  |  |  |  |  |  | 
17:00 | 29.88 |  |  |  | F |  | C |  | E |  |  |  |  |  |  | 
 |  |  |  |  | PACKDOWN |  | PACKDOWN |  | PACKDOWN |  |  |  |  |  |  | 

## Slide 10: Final Preparation & Post Inter-comparison
Final preparation meeting (7 March 2024)
Post inter-comparison workshop
  Advancing Earth Observation (AEO) Forum in Adelaide, South Australia 10-12 September 2024
  Interest from most teams