## Slide 1: WGCV-55 Report from ESA WS on Surface Reflectance Characterisation and Validation
Fabrizio Niro (Serco/ESA), Nigel Fox (NPL)
Agenda Item 2.11, WGCV-55
Hyderabad, India, 8-10 July 2025

## Slide 2: Background and Context
SR is a common product of all satellite optical imaging sensors and a key input for a wide range of applications.
Harmonizing SR products across missions is hence essential to ensure interoperability and consistency.
Despite of that, inconsistencies remain:
  Lack of consensus on terminology
  Disparities in algorithms and Ca/Val practices
  Scarcity of reference datasets.
Niro et al., 2021
Readiness level of a generic validation framework for satellite optical imaging sensors when considering various products level: L1 TOA, L2A BOA and L2B geophysical products.

## Slide 3: Workshop objectives
To move forward, ESA organized a WS in Lille gathering experts involved in current ESA projects on SR retrieval / validation
Objectives
  Review current SR retrieval methods and reference datasets
  Identify gaps and limitations, e.g., for CHIME and S-2/3 NG Cal/Val
  Recommendations and roadmap for ESA’s strategy for SR validation.
GRASP, Lille, France (21–22 May 2025)

## Slide 4: Agenda
Agenda included contributions from:
  GROSAT: build set of reference data over AERONET sites using the GRASP algorithm
  Eradiate: develop new open-source 3D RTM to support Cal/Val applications
  3DREAMS: study effect of surface heterogeneity and 3D effects on surface/aerosol retrievals
  FRM4VEG: working towards community practices for SR, LAI, fAPAR validation
  HYPERNETS: establish a hyperspectral ground-based network for SR validation
Reports/feedback from RadCalNet (M. Bouvet, ESTEC) and AERONET (Elena Lind, NASA)

## Slide 5: Discussion topics
The discussion revolved around the following main topics:
  Definitions and terminology
  Retrieval algorithms and models
  Validation Methods
  Reference datasets

## Slide 6: Definitions and Terminology
Consensus on two basic SR quantities:
  HDRF only measurable quantity, though not an intrinsic surface property, as it depends on illumination / environmental conditions.
  BRF surface-inherent property, but not directly measurable in the field, it can be derived by fitting a set of HDRF measurements + BRDF model
Recommendations:
  Ground-based data: HDRF + atmospheric state + tools to derive BRF  Rationale: HDRF unchanged, BRF can improve as modelling evolves
  Satellite data: ideally both HDRF and BRF, as a minimum HDRF + a toolbox to derive BRF

## Slide 7: Retrieval algorithms and models
Joint retrieval essential to resolve surface/aerosol radiative coupling, limitations :
  Legacy BRDF models (e.g., RPV, RTLS), developed for coarse resolution, e.g., AVHRR, MODIS.
  Underlying assumptions (1D, uniformity), break down at 10m under strict uncertainty requirements (<3%).
Demonstrated impact of 3D effects in retrieving surface / aerosol properties at high resolution.
Recommended to perform 3D RTM simulations for better characterising adjacency effects over RadCalNet, HYPERNETS, Cal/Val Park

## Slide 8: Validation Methods
Challenge of spatial upscaling.
  Uncertainty associated to transformation of FRM to the satellite pixel not fully characterised and often driving the overall budget
  Drones high spatial-temporal sampling, bridging gap point measurement to satellite pixel.
Recommend to address this issue with modelling approaches, and UAV, with a focus on RadCalNet, HYPERNETS sites.
Goal is the detailed characterisation of spatial mismatch uncertainty
Origo et al., 2025
Bialek et al., 2025: FRM Maturity of HYPERNETS Land

## Slide 9: Proposed BRF Validation protocol
Building on a protocol initially defined for a laboratory experiment:
  Artificial target (5mx5m) mimic vegetation reflectance pattern, i.e. hot spot
  From dimensional specs and optical properties simulate BRF using 3D RTM
  Measure the target (HDRF) in the field with UAV-based spectrometer survey
  From measured HDRF retrieve BRF and compare it to the simulated BRF
  Traceable uncertainty budget for BRF validation under controlled conditions
Leroy et al., 2025

## Slide 10: Reference datasets and networks
Two main networks:
  HYPERNETS, designed for BOA, need expand spatial and spectral coverage, notably in the SWIR for land sites, to meet users’ needs (CHIME).
  RadCalNet, designed for TOA, few sites, mostly in bright/arid homogeneous sites, ideal for radiometric Cal/Val, less for evaluating performances of AC
Recommended to ensure sustained funding to networks, while expanding geographical coverage with focus on vegetated sites
RTM-based datasets (GROSAT): uncertainty needs to be more thoroughly characterized.

## Slide 11: Way forward
Develop an ESA project (FRM4SR) in the medium term.
  Goal: to enhance FRM maturity of SR products validation.
  The pragmatic approach is to build on the efforts from past and on-going ESA projects, exploiting synergies across them.
  Continued engagement with networks is essential and should be facilitated through a dedicated WG that meets regularly.
Raise international awareness about the inititative
  Work towards endorsement at CEOS-WGCV level, similarly to what was done in the frame of SRIX4VEG
  Liaison and synergy to the CEOS ad-hoc group on SR quality should be established to ensure commonality of strategies

## Slide 12: Thank You!