## Slide 1: Surface Water and Ocean Topography Mission Provides heights of the world’s oceans and inland waters
Data Information
Observations of:
  Coastal sea level and ocean heights at unprecedented resolution over a swath
  Heights, widths, and slopes of rivers wider than 30m
  Heights, extents, and storage changes of all lakes larger than 1 hectare
Global coverage below 78 degrees latitude
21-day orbit cycle yielding observations of any given location every 10 days on average
Applications Areas
Water resource management and reservoir monitoring
Coastal and inland flooding
Maritime and river operations and commerce
Coastal zone management
Matthew Bonnema, NASA JPL
WGCV-56 / LSI-VC-19 Joint Meeting
April 23rd 2026

## Slide 2: SWOT - Global River Measurements

## Slide 3: SWOT - Global Measurements of Ocean

## Slide 4: SWOT - Global Measurements of Lakes

## Slide 5: SWOT - Data Products
Data Product Short Name | Data Product Description
L1B_LR_INTF | Low rate interferogram
L1B_HR_SLC | High rate single-look complex (SLC)
L2_LR_SSH | Low rate sea surface height (SSH), significant wave height, and wind speed
L2_HR_PIXC | High rate pixel cloud (PIXC) geolocated heights and backscatter
L2_HR_RiverSP | High rate river single pass product providing water surface elevation, slope, width, and derived discharge
L2_HR_LakeSP | High rate lake single pass product providing water surface elevation, area, and derived storage change
L2_HR_Raster | High rate raster product providing rasterized water surface elevation and inundation extent
Level 1 Radar Products
Level 2 Ocean Product
Level 2 Surface Water Products

## Slide 6: SWOT - Data Products - ARD
Data Product Short Name | Data Product Description
L1B_LR_INTF | Low rate interferogram
L1B_HR_SLC | High rate single-look complex (SLC)
L2_LR_SSH | Low rate sea surface height (SSH), significant wave height, and wind speed
L2_HR_PIXC | High rate pixel cloud (PIXC) geolocated heights and backscatter
L2_HR_RiverSP | High rate river single pass product providing water surface elevation, slope, width, and derived discharge
L2_HR_LakeSP | High rate lake single pass product providing water surface elevation, area, and derived storage change
L2_HR_Raster | High rate raster product providing rasterized water surface elevation and inundation extent
Level 1 Radar Products
Level 2 Ocean Product
Level 2 Surface Water Products

## Slide 7: SWOT - Data Products - ARD
Data Product Short Name | Data Product Description
L1B_LR_INTF | Low rate interferogram
L1B_HR_SLC | High rate single-look complex (SLC)
SWOT ARD Self Assessmnet (Preliminary):
Focused on Interferometric Radar [InSAR]
Potential for Ocean Radar Backscatter [ORB]
Not meeting requirements, but working to determine delta
Interested in discussing ARD for higher level water products

## Slide 8: SWOT - Data Products - Water ARD
Data Product Short Name | Data Product Description
L1B_LR_INTF | Low rate interferogram
L1B_HR_SLC | High rate single-look complex (SLC)
L2_LR_SSH | Low rate sea surface height (SSH), significant wave height, and wind speed
L2_HR_PIXC | High rate pixel cloud (PIXC) geolocated heights and backscatter
L2_HR_RiverSP | High rate river single pass product providing water surface elevation, slope, width, and derived discharge
L2_HR_LakeSP | High rate lake single pass product providing water surface elevation, area, and derived storage change
L2_HR_Raster | High rate raster product providing rasterized water surface elevation and inundation extent
Level 1 Radar Products
Level 2 Ocean Product
Level 2 Surface Water Products
Potential water ARD products?

## Slide 9: SWOT - Data Products - Water ARD

## Slide 10: Resources, Tips, & Tutorials! PO.DAAC Cookbook: SWOT Chapter
https://podaac.github.io/tutorials/quarto_text/SWOT.html
© 2024 California Institute of Technology. Government sponsorship acknowledged.
© 2024 California Institute of Technology. Government sponsorship acknowledged.

## Slide 11: SWOT_L2_HR_PIXC (netCDF)
Description: Point cloud of water mask pixels (“pixel cloud”)
Spatial Extent Format: Tile (64x64 km2)
Select Variables: geolocated heights, backscatter, geophysical fields, and flags
Subcollections: N/A
© 2024 California Institute of Technology. Government sponsorship acknowledged.
Example river pixels
Colorado River near Austin, TX

## Slide 12: SWOT_L2_Raster (netCDF)
Description: Geographically fixed rasterized water surface elevation and inundation extent.
Spatial Extent Format: Scene (128x128 km2)
Select Variables: water surface elevation, area, water fraction, backscatter, geophysical information
Subcollections:
SWOT_L2_Raster_100m
SWOT_L2_Raster_250m
© 2024 California Institute of Technology. Government sponsorship acknowledged.
Scene near Austin, TX

## Slide 13: SWOT_L2_RiverSP (shapefile)
Description: Vectors of river reaches (~10 km long) and nodes (~200 m spacing) in prior river database.
Extent Format: continent-scale swath
Variables: water surface elevation, slope, width, derived discharge*
Subcollections:
SWOT_L2_RiverSP_reach
SWOT_L2_RiverSP_node
*included ~2 years after launch
© 2024 California Institute of Technology. Government sponsorship acknowledged.
Node file
Reach file
Colorado River near Austin, TX

## Slide 14: SWOT_L2_LakeSP (shapefile)
Description: Vectors of lakes in prior lake database and detected features not in the prior river or lake databases.
Extent Format: continent-scale swath
Select Variables: water surface elevation, area, derived storage change
Subcollections:
SWOT_L2_LakeSP_obs
SWOT_L2_LakeSP_prior
SWOT_L2_LakeSP_unassigned
© 2024 California Institute of Technology. Government sponsorship acknowledged.
Lake Brownwood, TX

## Slide 15: Surface Water and Ocean Topography Mission Provides heights of the world’s oceans and inland waters
Data Information
Observations of:
  Coastal sea level and ocean heights at unprecedented resolution over a swath
  Heights, widths, and slopes of rivers wider than 30m
  Heights, extents, and storage changes of all lakes larger than 1 hectare
Global coverage below 78 degrees latitude
21-day orbit cycle yielding observations of any given location every 10 days on average
Applications Areas
Water resource management and reservoir monitoring
Coastal and inland flooding
Maritime and river operations and commerce
Coastal zone management
Matthew Bonnema, NASA JPL
CEOS SIT-41 WQ Workshop
April 13th 2026

## Slide 16: SWOT - Catchment to Coast Products
Data Product Short Name | Data Product Description
L1B_LR_INTF | Low rate interferogram
L1B_HR_SLC | High rate single-look complex (SLC)
L2_LR_SSH | Low rate sea surface height (SSH), significant wave height, and wind speed
L2_HR_PIXC | High rate pixel cloud (PIXC) geolocated heights and backscatter
L2_HR_RiverSP | High rate river single pass product providing water surface elevation, slope, width, and derived discharge
L2_HR_LakeSP | High rate lake single pass product providing water surface elevation, area, and derived storage change
L2_HR_Raster | High rate raster product providing rasterized water surface elevation and inundation extent
Surface water fluxes and stores
River and lake bathymetry
Presence and depth* of inundation
Coastal pressure gradients, currents
SWOT measures the elevation and extent of water surfaces, providing information about the movement of Earth’s water

## Slide 17: SWOT - Coastal Zone Applications
Recently funded project using SWOT to improve coastal water quality models and forecasts