## Slide 1: Discussion: Expressing Uncertainty Information
Cody Anderson, USGS (WGCV Chair)
WGCV-56 / LSI-VC-19 Sioux Falls, SD, USA
20-23 April, 2026

## Slide 2: Per-Pixel Uncertainty

## Slide 3: Landsat 8 OLI L1TP Per-Pixel Radiometric Uncertainty Components
Primary Components
  SI Traceability (Calibration) Uncertainty
  Noise Interpolation Propagation
  Interpolation Modeling Uncertainty
  Coupled Geometric–Radiometric Uncertainty
  Bad Pixels / Saturation / Defective Detectors

## Slide 4: Primary Components
SI Traceability (Calibration) Uncertainty
  Includes: integrating sphere, diffuser BRDF, stray light, nonlinearity, calibration transfer chain
  Provides a scene-independent baseline (with two values depending on radiance level)
Noise Interpolation Propagation
  Instrument noise propagated through interpolation
  Derived from per-detector noise model and interpolation kernel

## Slide 5: Primary Components
Interpolation Modeling Uncertainty
  Error due to interpolation not perfectly reconstructing the underlying signal
  Strongly scene-dependent (edges, aliasing, high spatial frequency content)
Coupled Geometric–Radiometric Uncertainty
  Radiometric error due to pixel location uncertainty
    Proportional to the product of image gradient x geometric uncertainty

## Slide 6: Primary Components
Bad Pixels / Saturation / Defective Detectors
  Includes:
    Saturated pixels (analog or digital)
    Defective detectors
  These do not have a valid uncertainty estimate and are masked and propagated through the interpolation kernel
  Typically flagged and propagated through interpolation
  Represent unknown / invalid uncertainty (nodata) rather than a quantified percent

## Slide 7: Ranking by Impact for a “typical scene” in descending order
1. Interpolation Modeling Uncertainty (~1.7% – 46%, median ~3%)
Largest contributor in most real scenes
Dominates in:
  edges
  urban areas
  high-frequency terrain
Often exceeds SI traceability uncertainty.

## Slide 8: Ranking by Impact for a “typical scene” in descending order
2. SI Traceability Uncertainty (~1.7% – 2.8%, median ~2.2%)
Baseline floor of uncertainty
Dominates in:
  homogeneous regions
  bright uniform targets

## Slide 9: Ranking by Impact for a “typical scene” in descending order
3. Coupled Geometric–Radiometric Uncertainty (~0% – 29%, median ~0.9%)
Scene-dependent
Large near:
  coastlines
  boundaries
  high gradients

## Slide 10: Ranking by Impact for a “typical scene” in descending order
4. Noise Interpolation Propagation (~0.03% – 24%, median ~0.3%; highest values occur in very low signal regions)
Usually smallest contributor
Only significant when:
  low signal (dark targets)
  low SNR

## Slide 11: Ranking by Impact for a “typical scene” in descending order
5. Bad Pixels / Saturation
Not expressed as percent uncertainty
Represents:
  unknown radiometric value
  invalid uncertainty
Should be:
  masked
  excluded from analysis

## Slide 12: Thanks Cody Anderson, USGS – WGCV Chair chanderson@usgs.gov