## Slide 1
Inchul Shin Satellite Planning Division National Meteorological Satellite Center
Korea Meteorological Administration
KMA Implementation Plan
for Climate products

## Slide 2
Outline
Introduction : Current GEO Satellite & Future KMA’s satellites
1.1 Current satellite products
1.2 Product validation & Quality monitoring
1.3 GEO-KOMPSAT-2A
Implementation plan of KMA
Evaluation of effect of GSICS Correction
3.1 GSICS correction results
3.2 SST, INS improvements
Summary and Plan

## Slide 3: 1. Introduction : Current GEO Satellite(COMS)

## Slide 4: 1. Introduction : COMS Products(1)
1. COMS public service started officially on April 1 2011.
NMSC has provided COMS L1 images and 16 products.
  - COMS 16 products are validated with ground based
  observation data or other satellites derived products etc. and
  reported periodically.
2. Obtaining more frequent satellite observation data over KP than before.
  - 4 times (00, 15, 30, 45min.) an hour over ENH region and 8 times and
  hour over Korean Peninsula(KP), being able to monitor intensively.
  - It is significantly effective to monitor heavy rain cloud which develops
  locally or is coming from west sea of KP during summertime.
3. More distinctive satellite images over KP with COMS. - Since COMS is located at 128.2E, COMS image has smaller shadow
area and lower SZA over KP for MTSAT image.

## Slide 5: 1.1 Introduction : COMS Products(2)
RI
CTTP
Cloud
Clear sky
AMV
SSI
CLA
CSR
Fog
CLD
Ancillary data
Level 1B
Image Processing
Archiving &
Distribution
CMDPS
CMDPS
Preprocessing System
Validation
  □ confidently cloudy
  ■ cloudy
  ■ probably cloudy
  ■ probably clear
  ■ confident clear
LST
SST
UTH
AI/AOD
OLR
INS
NMSC/KMA
TPW

## Slide 6: 1.2 Product Validation & Quality Monitoring -
Product
Observation data
Collocation
Quality monitoring
Statistical index
Algorithm Improvement
Daily Monthly
Seasonal
Algorithm Theoretical Basis Document
COMS
MODIS

## Slide 7
1.3 GEO-KOMPSAT-2A
Development of GEO-KOMSAT-2A : - launch in 2018 - 16 channels : 4 visible, 2 near-infrared and 10 infrared channels - 52 meteorological products : Cloud, Precipitation, AMV, Aerosol, Land surface
- Continuous monitoring of meteorological phenomena through the succession of COMS mission
- Development of Advanced MI(AMI) and Space Weather Sensor
Mission
- Continuing the COMS Meteorological Mission
- Improving the Severe Weather Monitoring
- Improving the support of the NWP model
- Intensifying the environment & climate monitoring
    · Various surface information retrieval
    · Establishing long-term observation data

## Slide 8
COMS MI vs. GEO-KOMPSAT-2A (AMI)
4 times spatial resolution
COMS
VI 1km
IR 4km
Geo-KOMPSAT-2A
VI 0.5~1km
IR 2km
4 times tempral resolution
COMS
1 channel
(achromatic)
O
4 channels
5 channels
Geo-KOMPSAT-2A
4 channels
(color)
2 channels
10 channels
16 channels
VI
SWIR
IR
COMS
16 products
Cloud/Precipitation (519)
Radiation/aerosol (516)
Atmospheric Motion/Conditions(36)
Geo-KOMPSAT-2A
52 products
1 FD
2 NH
…....
Every 2 min Korea
1 Hr
4 Korea
4 FD
10 NH
3 times number of channels
3.5 times number of products
Surface information(311)

## Slide 9: 2. Implementation Plan of KMA
Timeframe | …. | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | ….
Plan of SCOPE-CM | Phase Ⅰ | Phase Ⅱ |  |  | Phase Ⅲ |  |  |  |  |  | 
Satellite |  |  |  |  |  |  |  |  |  |  | 
KMA Step |  |  |  |  |  |  |  |  |  |  | 
 |  | : COMS Generation Selected ECVs generating (GSICS-based) - Preparation for GeoKompsat-2a |  |  |  |  |  | : GeoKompsat-2a Generation - Selected ECVs generating - Continuous management - Selection and generating of supplementary ECVs |  |  | 
COMS
GeoKompsat-2A
Step-1
Step-2
KMA’s ECVs to participate immediately for SCOPE-CM
Primary ECVs for SCOPE-CM of KMA (PESK)
KMA’s ECVs to participate prospectively for SCOPE-CM after GK-2a launch
Secondary ECVs for SCOPE-CM of KMA (SESK)

## Slide 10: 2. Implementation Plan of KMA
PESK
SESK
· Sea Surface Temperatrue
· Outgoing Longwave Radiation
· Insolation
· Albedo
· Precipitation
· Snow Cover/Sea Ice
Algorithms: In operation
Similar algorithms with other
GEO satellites
Similar input data with other
GEO satellites
Algorithm:
  In development (Albedo)
  Improvement needed
  (Precipitation, Snow cover/ Sea ice)
Different algorithms and inputs
with other GEO satellites
To participate immediately for SCOPE-CM
To participate prospectively for SCOPE-CM after GK-2a launch

## Slide 11
Primary ECVs for SCOPE-CM of KMA(PESK) |  |  |  | 
Parameters | Sea Surface Temperature Outgoing Longwave Radiation Insolation |  |  | 
Step-1 ( ~2017) Action Items | Step 1-1 (3 years) | GSICS→FCDRs→TCDRs continuous generating Evaluation of effect of GSICS correction QC./QA, algorithm improvement |  | 
 | Step 1-2 (3 years) | Inter-satellite comparison of products EUMETSAT-KMA operating collaboration Preparation for GeoKompsat-2a / Future Korean LEO satellite |  | 
Step-2 (2018~ ) Action Items | Obtaining consistency and continuity between COMS and GeoKompsat-2a TCDRs Continuous improvement of TCDRs Continuous collaboration with SCOPE-CM working group |  |  | 
Parameters | SST |  | OLR | INS
Accuracy (objective) | 0.5 –0.8 ℃ |  | 10 W/m2 | 70-100 W/m2
Spatial Resolution | 1-5 km2 |  | 15 km2 | 15 km2
Temporal Resolution | 2 daily |  | daily | daily
PESK Implementation Plan, KMA

## Slide 12: SESK Implementation Plan, KMA
Secondary ECVs for SCOPE-CM of KMA(SESK) |  |  | 
Parameters | Albedo Precipitation Snow Cover/Sea Ice |  | 
Step-1 ( ~2017) Action Items | Preparation for GeoKompsat-2a / Future Korean LEO satellite Algorithm development |  | 
Step-2 (2018~ ) Action Items | GSICS→FCDRs continuous generating FCDRs→TCDRs generating Evaluation of effect of GSICS correction QC./QA, algorithm improvement Inter-satellite comparison of products Obtaining consistency and continuity between COMS and GeoKompsat-2a TCDRs Continuous collaboration with SCOPE-CM working group |  | 
Parameters | Albedo | Precipitation | Snow Cover/Sea Ice
Accuracy (objective) | Albedo>0.15 : 10~20% Albedo<0.15 : 0.015~0.15 | 40-80% (> 10mm/h) | -Snow Cover: <3% false alarms, >75% hit rate forest, >90% for other areas -Sea Ice: 10-15%
Spatial Resolution | 15 km2 | 8 km2 | -Snow Cover: 3 km2 -Sea Ice: 10 km2
Temporal Resolution | daily | daily | daily

## Slide 13: 3. GSICS Processing Results – (IR channels)
IR1 channel
IR2 channel
SWIR channel
WV channel
2012
2013
2012
2013
2012
2013
2012
2013

## Slide 14: 3. GSICS Processing Results – (VIS channels)

## Slide 15
Spring
COMS SST: using COMS L1b
NEW SST: after GSICS correction
Summer
Autumn
Winter
Data: 01/04/2011~31/03/2012
Improvement of SST after GSICS Correction

## Slide 16
2011, April, July
2011.04 (before)
2011.07 (before)
2011.04 (after)
2011.07 (after)
Improvement of SST after GSICS Correction

## Slide 17
RMSE : 90.8045
Bias : 16.2023
RMSE : 95.5762
Bias : 6.4493
Cloudy Sky
Partially Cld.
ALL Sky
RMSE : 89.677
Bias : 2.102
RMSE : 95.772
Bias : 2.523
RMSE : 106.137
Bias : -1.016
COMS
INS
after
GSICS
Correction
Improvement of Insolation after GSICS Correction
Data: 01/04/2012~31/03/2013

## Slide 18
2012.04~2013.03 |  | All | Cloudy | Partially
Original | RMSE (W/m2) | 95.832 | 91.182 | 104.964
 | Bias (W/m2) | 12.136 | 21.979 | 5.308
After GSICS Correction | RMSE (W/m2) | 95.772 | 89.677 | 106.137
 | Bias (W/m2) | 2.523 | 2.102 | -1.016
2011.04~2012.03 |  | All | Cloudy | Partially
Original | RMSE (W/m2) | 95.576 | 90.806 | 103.952
 | Bias (W/m2) | 6.449 | 16.202 | -3.527
After GSICS Correction | RMSE (W/m2) | 95.772 | 89.677 | 106.137
 | Bias (W/m2) | 2.523 | 2.102 | -1.016
Results
Improvement of Insolation after GSICS Correction

## Slide 19
SST accuracy was improved after GCIS correction
Insolation estimation bias was improved after GSICS correction without new cloud factor generation
Resulted positive effect of GSICS-based FCDRs toward TCDRs
These positive effect of GSICS should be continuously monitored.
1
2
3
4
1
2
3
4
4. Summary

## Slide 20
Thank you

## Slide 21
Area : 0-45°N, 105-160°E
Period : 2011.4.1.~2013.3.31.
Buoy SST data
Validation data
Area : 30-40°N, 120-130°E, 37 stations
Period : 2011.4.1.~2013.3.31.
Pyranometer data

## Slide 22
 | MI(COMS) |  | AMI(GEO-KOMPSAT-2A) | 
Channels | 5 |  | 16 | 
Spatial resolution(km) | 1/4(VIS/IR) |  | 0.5,1/2(VIS/IR) | 
True color image | X |  | O | 
Temporal resolution(min) | 25(Full Disk) |  | 10(Full Disk) | 
Products | 16 |  | 52 | 
Data rates(Mbps) | 2.6 |  | ~70 | 
Design life(year) | 7 |  | 10 | 
Utilization | Weather forecasting |  | + NWP + Climate model | 
Loaded satellites | U.S.A. | GOES-8~15 | GOES-R(ABI) | 2015
 | Japan | MTSAT-2 | Himawari-8/9(AHI) | 2014/2016
GEO-KOMPSAT-2A payload

## Slide 23
FPM | Band name | AMI(Geo-KOMPSAT-2A) |  | ABI(GOES-R) |  | AHI(Himawari-8/9) |  | MI (COMS) | 
 |  | Center Wavelength (µm) | Resolution (km) | Center Wavelength (µm) | Resolution (km) | Center Wavelength (µm) | Resolution (km) | Center Wavelength (µm) | Resolution (km)
VNIR | VIS0.4 | 0.47 | 1 | 0.47 | 1 | 0.46 | 1 |  | 
 | VIS0.5 | 0.51 | 1 |  |  | 0.51 | 1 |  | 
 | VIS0.6 | 0.64 | 0.5 | 0.64 | 0.5 | 0.64 | 0.5 | 0.675 | 2
 | VIS0.8 | 0.856 | 1 | 0.865 | 1 | 0.86 | 1 |  | 
 | NIR1.3 | 1.378 | 2 | 1.378 | 2 |  |  |  | 
 | NIR1.6 | 1.61 | 2 | 1.61 | 1 | 1.6 | 2 |  | 
 | NIR2.2 |  |  | 2.25 | 2 | 2.3 | 2 |  | 
MWIR | IR3.8 | 3.9 | 2 | 3.9 | 2 | 3.9 | 2 | 3.75 | 4
 | IR6.3 | 6.185 | 2 | 6.185 | 2 | 6.2 | 2 |  | 
 | IR6.9 | 6.95 | 2 | 6.95 | 2 | 7.0 | 2 | 6.75 | 4
 | IR7.3 | 7.34 | 2 | 7.34 | 2 | 7.3 | 2 |  | 
 | IR8.7 | 8.5 | 2 | 8.5 | 2 | 8.6 | 2 |  | 
LWIR | IR9.6 | 9.61 | 2 | 9.61 | 2 | 9.6 | 2 |  | 
 | IR10.5 | 10.35 | 2 | 10.35 | 2 | 10.4 | 2 | 10.8 | 4
 | IR11.2 | 11.2 | 2 | 11.2 | 2 | 11.2 | 2 |  | 
 | IR12.3 | 12.3 | 2 | 12.3 | 2 | 12.3 | 2 | 12.0 | 4
 | IR13.3 | 13.3 | 2 | 13.3 | 2 | 13.3 | 2 |  | 
GEO-KOMPSAT-2A payload
16 channels

## Slide 24
Development & utilization
of GK-2A data
 | No. | Products |  | No. | Products
cloud/ rainfall | 1 | Cloud detection | radiation/ Aerosol | 27 | Visibility
 | 2 | Cloud Top Temperature |  | 28 | O3 total
 | 3 | Cloud Top Pressure |  | 29 | Radiances
 | 4 | Cloud Top Height |  | 30 | Upward Shortwave Radiation(TOA)
 | 5 | Cloud type |  | 31 | Downward Shortwave Radiation(Surface)
 | 6 | Cloud phase |  | 32 | Absorbed Shortwave Radiation(Surface)
 | 7 | Cloud Amount |  | 33 | Downward Longwave Radiation(Surface)
 | 8 | Cloud Optical Depth |  | 34 | Upward Longwave Radiation(Surface)
 | 9 | Cloud Particle Size Distribution |  | 35 | Upward Longwave Radiation(TOA)
 | 10 | Cloud Liquid Water | ATM motion/ condition | 36 | Atmospheric Motion Vector
 | 11 | Cloud Ice Water Path |  | 37 | Vertical Temp. Profile
 | 12 | Cloud Layers/Heights |  | 38 | Vertical Moisture Profile
 | 13 | Fog |  | 39 | Derived Stability Indices
 | 14 | In-flight icing |  |  | Total Precipitable Water
 |  |  |  | 40 | Atmospheric Motion Vector
 | 15 | Convection initiation |  | 41 | Tropopause folding turbulent flow
 | 16 | overshooting top/enhanced thermal couplet detection | surface | 42 | Sea Surface Temperature
 | 17 | Rainfall Intensity |  | 43 | Land Surface Temperature
 | 18 | probability of rainfall |  | 44 | Fire/Hot Spot Characteristic
 | 19 | rainfall potential |  | 45 | Vegetation Index
radiation/ aerosol | 20 | Aerosol detection |  | 46 | Vegetation Fraction: Green
 | 21 | Asian dust detection |  | 47 | Surface Emissivity
 | 22 | Volcanic Ash: Detection and Height |  | 48 | Surface Albedo
 | 23 | SO2 Detection |  | 49 | Snow Cover
 | 24 | Aerosol Optical Depth |  | 50 | Snow Depth
 | 25 | Asian dust Optical Depth |  | 51 | Ice Cover
 | 26 | Aerosol Particle Size |  | 52 | Current
Schedule of meteorological data processing system

## Slide 25
Sea ice
Hong and Shin, 2010 (J. Climate)
Hong, 2010 (Rem. Sens. Environ.)
Concentration, Small-scale roughness and refractive index of sea ice surfaces (June. 2011) using AQUA/AMSR-E data
Climate monitoring using LEO satellites

## Slide 26
Climate monitoring using LEO satellites
Volumetric soil water content (g/cm3) using Hong’s algorithm
AMSR-E level 3 products.
Hong and Shin, 2011 (J. Hydrol.)
Soil moisture