## Slide 1: Pico do Fogo, Cape Verde, 2014-2015
Methods and Technologies
Quantitative estimate based on deterministic physical models.
Unsupervised merge of data borne by multispectral payloads from Very-high-temporal to High-spatial resolution
Inherited from ESA’s GlobVolcano and EC FP7 project
Photo by S. Day (2015)
Continuous estimate of mass flows to forecast flow limiting lengths
Specific stakeholder’s request

## Slide 2: Variable Resolution Datasets
High-temporal resolution (≈3700 images): Radiant Fluxes by SEVIRI onboard MSG-3 and MSG-1, every 15 minutes, night and day
10:00
10:15
10:30
10:45
11:00
11:15
11:30
11:45
12:00
12:15
12:30
12:45
13:00
13:15
15:15
15:30
15:45
16:00
16:15
16:30
16:45
17:00
17:15
17:30
17:45
18:00
18:15
18:30
Ground-based: RSAM (1-min integration)
High Spatial resolution (8 exploitable scenes, 30x30 m2): Radiant flux monitoring by EO 1-ALI and Landsat 8-OLI, daytime scenes
Very-High Spatial resolution (2+1 scenes): characterization of the source (NIR, 2.8x2.8 m2)
Moderate resolution (157 scenes, 1x1 km2): Radiant flux monitoring by MODIS onboard TERRA and AQUA, nightscenes

## Slide 3: Multiple spatial resolutions
SEVIRI - 11,400,000 m2 (Fogo, Cape Verde)
> 46,000,000 m2 (Bardarbunga, Iceland)
MODIS
1,000,000 m2
OLI, ALI
900 m2
Pleiades
8 m2

Limiting Flow Length - Alert Thresholds for Fogo
  ER > 20 m3/s by Gratz Number, or
  30 < ER< 40 m3/s by flow Front Strength
Radiant flux Qr  Effusion rate Er
Simple cooling bar model, neglecting convection and conduction losses
ER = QR [lava (Cplava Tstop+CL ) ]-1 m3/s
with lava density
Cplava specific heat capacity
 mass fraction of crystals grown
CL latent heat of crystallization

## Slide 4
Fogo, November 23rd to December 27th, 2014

## Slide 5: Fogo, December 10th to December 27th, 2014
  Flow length: with ~30% combined vesicles and rubble porosity both equations predicted a ~ 5 km limiting length of the Portela - Bangeira flow
  By December 6th the flows were unlikely to escape Cha das Caldeiras.
  This was confirmed by December 14th onwards by Hi-Res ALI

## Slide 6
Until 08-02-2015, by High- and Moderate-Spatial Resolution

## Slide 7
Cumulative volumes (F=0) until February 8, 2015

## Slide 8
Anywhere: All-in-one 2014 by 15-minute MSG (full disk)

## Slide 9
ETNA (05/07)  19/09/2014
STROMBOLI 06/08  19/09/2014 HOLUHRAUN 31/08  (02/03/2015)
Anywhere: All-in-one 2014 by 5-minute MSG Rapid Scan

## Slide 10
Anywhere: All-in-one 2015 by 15-minute MSG (full disk)

## Slide 11
Piton de la Fournaise, Réunion Island - ongoing

## Slide 12
Piton de la Fournaise, Réunion Isl. (EO1-ALI , Sep. 2, 2015)
EO1 - ALI
Terra-MODIS
MSG3-SEVIRI

## Slide 13
Volcano Pilot, area of focus “C”
Precise questions can be answered precisely
MS HR was better suited than VHR to the technical needs that arose on Fogo
Response without monitoring ?
In crisis management, temporal resolution is ways more critical than spatial resolution