## Slide 1: WGISS / WGCV Joint Meeting JAXA Agency report
K. Tanada,
Y. Ikehata,
A. Kuze
Agenda B.2
WGISS-WGCV
16-17 October 2024
Sioux Falls, South Dakota, USA

## Slide 3: History and Launch Schedule
March 2023: ALOS-3 (Optical) was lost due to H3 Test Flight #1 (TF1) rocket failure
Feb 17, 2024: H3 TF2 rocket launch (successful)
May 29, 2024: EarthCARE (Hakuryu) launched by Space X Falcon 9, JAXA provides Cloud Profiling Radar (CPR). (Successful)
July 1, 2024: ALOS-4 (Daichi 4) (SAR) by H3 F3 (successful)
FY2024: GOSAT-GW (GHG spectrometers and microwave radiometer) launched by H-IIA

## Slide 4: EarthCARE (2024.5 launched)
EarthCARE successfully launched on May 28th, 2024 UTC.
L1 & L2 products are planned to be released in Jan. 2025 and Mar. 2025, respectively.
CPR provided by JAXA/NICT is the world’s first W-band Doppler radar (94GHz) which can observe the vertical structure of clouds, as well as the ascending and descending movement of clouds.
The CPR is sensitive to thick cloud, while the ATLID is sensitive to thin cloud. Combining the CPR and the ATLID allows observation of a wider range of cloud types
4 sensors simultaneous observation (CPR, ATLID, MSI, BBR)
Vertical distribution of the CPR Doppler velocity for a tropical cyclone in the northeast Pacific
(22 UTC, 22 August 2024)

## Slide 5: AOS Collaboration (2029~?)
JAXA GPM + EarthCARE community has agreed to join the AOS project with PMM (Precipitation Measurement Mission) / KuDPR (Ku-band Doppler Precipitation Radar) in inclined orbit with following new/advanced functions improved from GPM/DPR
AOS delivers globally distributed measurements​ over a range of temporal scales
Polar-orbiting observatories will provide measurements central to understanding aerosol-cloud interactions for climate and aerosol studies
PMM/AOS-Storm will enable observations of convective storms/precipitation over varying times of day
Architecture contingent on funding
Atmosphere Observing System

## Slide 6: GOSAT-GW / AMSR3 (JFY 2024~)
GOSAT-GW will carry two instruments, AMSR3 & TANSO-3
AMSR3, developed by JAXA, will succeed AMSR series observations adding new high-frequency channels for solid precipitation retrievals and water vapor analysis in NWP.
TANSO-3, led by Japanese Ministry of the Environment (MOE), will improve observation capability of greenhouse gases from GOSAT-2/TANSO-2. (Choose grating spectrometer to enable spatially detailed observation)
Target launch is JFY2024 (Apr. 2024 - Mar. 2025)
AMSR3 sensor in production. Photo: AMSR3 Main Reflector at Tsukuba Space Center
AMSR3 specifications: https://www.eorc.jaxa.jp/AMSR/satellite/gosat-gw_en.html
Additional 166 & 183 GHz channels to enable monitoring of global precipitation (rain & snow) and contribute to water vapor analysis in NWP
Additional 10.25 GHz channels with improved NEDT to enable robust SST retrievals in higher spatial resolution
AMSR3 Features
  AMSR series (AMSR-E, AMSR2, AMSR3: Microwave channels of 6.9-89GHz) achieve continuous observation +22 years

## Slide 7: GCOM-C CAL-VAL
VNR-NP
11 channel three telescopes
VNR-POL
Polarization two telescopes (670nm and 865nm)
InfraRed Scanner (SGLI-IRS)
(4 SWIR, 2 TIR channels)
Visible and Near-infrared Radiometer
(SGLI-VNR)
Second-generation Global Imager (SGLI)
Global environmental minoring by NUV-TIR optical imagers
Long-term timeseries of 60N-60S monthly mean Chl-a anomaly by multiple sensors
SeaWiFS
OCTS
VIIRS
Aqua MODIS
Terra
OLCI
SGLI (2018~)
GLI
SGLI channel specification | Specification of SGLI spectral bands |  |  |  |  |  | 
swath | CH |  |  | Lstd | Lmax | SNR@Lstd | IFOV
km |  | nm |  | W/m2/sr/m K: Kelvin |  | - K: NET | m
1150km (VNR: push-broom electric scan) | VN01 | 380.0 | 10.6 | 60 | 240-241 | 624-675 | 250 /1000
 | VN02 | 412.5 | 10.3 | 75 | 305-318 | 786-826 | 250 /1000
 | VN03 | 443.2 | 10.1 | 64 | 457-467 | 487-531 | 250 /1000
 | VN04 | 489.8 | 10.3 | 53 | 147-150 | 858-870 | 250 /1000
 | VN05 | 529.6 | 19.1 | 41 | 361-364 | 457-522 | 250 /1000
 | VN06 | 566.2 | 19.8 | 33 | 95-96 | 1027-1064 | 250 /1000
 | VN07 | 672.0 | 22.0 | 23 | 69-70 | 988-1088 | 250 /1000
 | VN08 | 672.1 | 21.9 | 25 | 213-217 | 537-564 | 250 /1000
 | VN09 | 763.1 | 11.4 | 40 | 351-359 | 1592-1746* | 250 /1000*
 | VN10 | 866.8 | 20.9 | 8 | 37-38 | 470-510 | 250 /1000
 | VN11 | 867.1 | 20.8 | 30 | 305-306 | 471-511 | 250 /1000
 | PL01 | 671.9 | 20.6 | 25 | 293 | 609 | 1000@nadir
 | PL02 | 866.2 | 20.3 | 30 | 396 | 646 | 1000@nadir
1400km (IRS: whisk-broom) | SW01 | 1055 | 21.1 | 57 | 289.2 | 951.8 | 1000
 | SW02 | 1385 | 20.1 | 8 | 118.9 | 347.3 | 1000
 | SW03 | 1635 | 195.0 | 3 | 50.6 | 100.5 | 250 /1000
 | SW04 | 2209 | 50.4 | 1.9 | 21.7 | 378.7 | 1000
 | TI01 | 10793 | 756 | 300K | 340K | 0.08K | 250/500/1000
 | TI02 | 11956 | 759 | 300K | 340K | 0.13K | 250/500/1000
https://suzaku.eorc.jaxa.jp/GCOM_C/data/prelaunch/index.html
GCOM-C characteristics | 
Launch Date | 23 Dec. 2017 (data available since 1 Jan 2018)
Orbit | Sun-synchronous (descending local time: 10:30am), Altitude: 798km, Inclination: 98.6deg
Global Change Observation Mission – Climate, "SHIKISAI"

## Slide 8: GCOM-C CAL-VAL SGLI Lunar CAL by GIRO
The temporal change, bch, is estimated by the multiple regression with the lunar phase angle, gn
    (d: days from launch, ch: SGLI channels)
bch is updated half-yearly, and Lchorig is corrected to LchL1B in the Level-1B processing
  LchL1B = Lchorig / (1.0 + bch d)
Time series of SGLI/GIRO trend (Normalized by 2018/2/1)
Urabe et al. (2020). DOI: 10.3390/rs12010069;
Urabe et al. (2019) DOI: 10.1109/IGARSS.2019.8897892
VNR
IRS
GCOM-C SGLI lunar calibration is regularly updated by the monthly (phase angle ~+7) lunar observation operations (by the pitch maneuver; 80 times from Jan. 2018 to Feb. 2024) with GIRO
All SGLI lunar observation data (GIRO input/output files) have been submitted to GLOD
SGLI/GIRO
VNR 380nm~865nm
0.85
1.01
2024/02
2018/01
SGLI/GIRO
SWIR 1.05m~2.21m
0.90
1.02
2024/02
2018/01
VN02: 412 nm
Internal-lamp CAL
Normalized by 31 Jan 2018
Solar CAL
Lunar CAL
1.03
0.89
1.00
Normalized by 31 Jan 2018
VN05: 530 nm
Internal-lamp CAL
Solar CAL
Lunar CAL
1.03
0.89
1.00
Because of the diffuser reflectance change especially in shorter wavelengths, the difference among the on-board CAL results becomes large (e.g., VN02), however, it is small (less than about 0.5%) in other wavelengths.
Post-launch calibration comparison (lunar, solar, internal lamp)

## Slide 9: ALOS-4
(2) Demo Successful achievement of the world's fastest optical inter-satellite communication at a speed of 1.8 Gbps between the Laser Utilizing Communication System (LUCAS) and the Advanced Land Observing Satellite-4 (ALOS-4).(Oct 8, 2024)
(1) First images from Advanced Land Observing Satellite-4 “DAICHI-4” (ALOS-4) / Phased Array type L-band Synthetic Aperture Radar-3 (PALSAR-3)
- Extended swath width to 200 km with world's highest resolution (3 m) –(July 31, 2024)
Enlarged images of the vicinity of Mount Fuji and downtown Tokyo by PALSAR-3

## Slide 10: GOSAT Series CAL-VAL
GOSAT (2009-)
Satellite Condition & Calibration
Enough fuel, healthy four batteries are healthy
15-year solar irradiance calibration data set
Level 1 V300.300 (released in March 2023)
Best-estimate radiance spectra using TSIS-HSRS
JAXA Level 2 Partial Column product V3
GOSAT (15-year ) and GOSAT-2 (6-year)
GOSAT-2 (2018-)
Intense target observations
using flexible and wider angle pointing
Calibration
6-year monthly lunar calibration with phase of 7 deg.
Level 1 V221 (released in March 2024)
Updated Best-estimate radiance spectra
GOSAT-GW (to be launched in FY2024)
Total Anthropogenic and Natural emissions mapping SpectrOmeter-3 (TANSO-3)
Adding NO2 as an emission proxy for CO2.
Imaging Spectrometers
+ Advanced Microwave Scanning
Radiometer 3 (AMSR-3)
July 2024 16th Joint campaign in NV GHG V-Calibration Portal