## Slide 1: WGDisasters 24 Flood Pilot
Marcelo Uriburu Quirno, CONAE, Guy Schumann, RSS Hydro, Alexia Tsouni, NOA, William Straka, SSEC University of Wisconsin-Madison
Agenda Item 21
WGDisasters-24
Bariloche, Argentina
30 Set-2 Oct 2025

## Slide 2
Guy Schumann, RSS Hydro

## Slide 3: RSS-Hydro’s FloodSENS satellite EO ML model
Maps flooded areas even with cloud cover by using machine learning to reconstruct obscured regions.
Enhances flood detection accuracy by integrating diverse Earth Observation data, including optical imagery and DEM-derived information, and more recently looking at full multi-mission data integration and downscaling.
Utilizes a fully automated machine learning algorithm for efficient processing and continuous improvement in flood mapping.
Trained on extensive data, FloodSENS achieves consistent accuracy and demonstrates its ability to reliably map floods across various global environments.
Offers customizable map features, including flood depth and uncertainty, and leverages 3D visualization for enhanced understanding of flood impacts.
https://www.innovationnewsnetwork.com/partner/floodsens-enhancing-disaster-resilience-through-ai-powered-flood-mapping/

## Slide 4: South Korea Flood Event July 2025
https://disasterscharter.org/activations/flood-in-korea-republic-of-activation-974-

## Slide 5: Multi-Sensor Daily Flood Maps during events
Multi-mission development (PhD student: Chloe Campo)
Optical, SAR, Passive Microwave, GNSS-R
Mix between ML & traditional signal processing workflows
At least daily downscaled mapping during an event
Docker & Containers: flexibility & security
Deploy in space on constellations & cloud
https://disasterscharter.org/activations/flood-in-korea-republic-of-activation-974-

## Slide 6: The Current and Future Global Flood Inundation Mapping Systems from Multiple-Source Satellite Imagery
William Straka, Cooperative Institute for Meteorological Satellite Studies (CIMSS) - University of Wisconsin - Madison
"The contents of this message are mine personally and do not necessarily reflect any position of the National Oceanic and Atmospheric Administration."

## Slide 7
Image courtesy of noaa.gov

## Slide 8: Satellite based soil moisture monitoring
Soil moisture is important in the forecasting and monitoring of drought conditions as well as helping forecast areas where wildfires are likely to occur as well as helping indicate where impending drought or flood conditions are before other indicators see the event.
There are several satellite based soil moisture products that are available from active and passive microwave instruments, scatterometers (ex. ASCAT) and imagers (ex. VIIRS) on polar orbiting satellites
These include the Soil Moisture Operational Products System (SMOPS), which is a blended product including multiple types of instruments; Soil Moisture Active Passive (SMAP); AMSR2/GCOM-W1 surface soil moisture (LPRM) L3 product and VIIRS Vegetation Health Product (VVHP, right image below)
Owing to the type of product, these are fairly coarse (4km and greater)
Notes: it would be good to mention here that there is a 1km research products, combining microwave imager and optical imager, have been developed and under evaluation.

## Slide 9: Satellite based soil moisture monitoring
VIIRS Vegetation Health Product
AMSR2/GCOM-W1 surface soil moisture product
Notes: it would be good to mention here that there is a 1km research products, combining microwave imager and optical imager, have been developed and under evaluation.

## Slide 10: Satellite based precipitation products
There are several satellite based precipitation algorithms, which can be used to estimate rainfall amounts where there is limited or no radar coverage.
Other products are able to measure the total precipitable water, which are useful to show where atmospheric river and moisture transport are occuring
Most algorithms use microwave or infrared sensors from both geostationary and polar orbiting satellites. However, they are at very coarse resolution as compared to ground based weather radars
Some examples of these include CMORPH2 and GSMaP (precipitation) and MIMIC-TPW (moisture advection).
GSMaP and other precipitation algorithms being used by hydrological models as input

## Slide 11: Satellite based precipitation products
GSMaP
MIMIC-TPW

## Slide 12: SAR FLOOD PRODUCTS
Synthetic Aperture Radar (SAR) provides very high-resolution flood mapping, though at lower temporal resolution, is able to see flooding even during times of extended cloud cover or nighttime that frequently occurs during flooding and inhibits optical flood detection.
Similar to what happens in the optical flood algorithms, the transmitted radar signals on flat water surfaces are reflected back with a significantly weak signal back to the satellite.
There are multiple satellite missions (Sentinel-1, Radar Constellation Mission, JAXA’s ALOS satellites, etc). Most of these have low-repeat cycles and are often restricted datasets.
Most SAR flood products are RGB-type products, delineating flood/no-flood by different colors. However, there are several SAR flood extent products that are being produced or in development by various agencies (NR-Can, NOAA NESDIS, NOAA’s National Water Center)

## Slide 13: Flood monitoring capabilities from satellites - SAR
Provides extremely high resolution flood mapping (10m or less) even at night and through clouds
Low latency mapping (16+ day repeat, depending on location and constellation)
Limited availability (data are restricted from some agencies)
Some operational processing (Copernicus Emergency Management Service (EMS), NRCan, ISRO) as well as some products under development.
Copernicus Emergency Management Service (EMS)
Sentinel-1A/B acquired by ESA/Copernicus, Contains modified Copernicus Sentinel data 2022
RCM - NR-Can

## Slide 14: NOAA SAR FLOOD PRODUCT OVERVIEW
  Currently uses Sentinel-1, RADARSAT -2, and the RADARSAT Constellation Mission (RCM) imagery and has been tested on TerraSAR-X and SAOCOM. Plans to extent application with NISAR (once launched)
  Algorithm is called RAdar Produced Inundation Diary (RAPID). The RAPID is a near-real-time (NRT) inundation mapping system using satellite SAR data, providing high quality products
  Uses a 4 step process, including the use of machine learning to classify flooded regions. (Shen et al., 2019; Yang et al., 2021)
References
    Shen, X., Wang, D., Mao, K., Anagnostou, E. and Hong, Y., 2019. Inundation extent mapping by synthetic aperture radar: A review. Remote Sensing, 11(7), p.879.
    Shen, Xinyi, Emmanouil N. Anagnostou, George H. Allen, G. Robert Brakenridge, and Albert J. Kettner. "Near-real-time non-obstructed flood inundation mapping using synthetic aperture radar." Remote Sensing of Environment 221 (2019): 302-315.
    Yang, Q., Shen, X., Anagnostou, E.N., Mo, C., Eggleston, J.R. and Kettner, A.J., 2021. A high-resolution flood inundation archive (2016–the present) from Sentinel-1 SAR imagery over CONUS. Bulletin of the American Meteorological Society, pp.1-40.

## Slide 15: Flood monitoring capabilities from satellites - Optical
Can provide high temporal resolution flood monitoring
Consistent monitoring on a daily or hourly basis
Geostationary satellites can provide flood extent over the course of the day and can help with cloud clearing
Polar satellites can provide higher resolution flood monitoring in the morning and afternoon
VIIRS downscaled product from 3 October 2022
(Win McNamee/Getty Images)

## Slide 16: OPTICAL FLOOD PRODUCTS
Optical sensors can use information from visible, near infrared , and short-wave infrared (SWIR) channels, along with a series of test for cloud detection, shadow detection, snow/ice detection and combining them with water reference maps to discriminate permanent water bodies
One can combine data from various sensors, such as ABI and VIIRS, to create a daily, cloud cleared, flood product. Or one can utilize digital elevation models and other higher resolution datasets to create flood depth maps at higher spatial resolution (30 m)
This is different that RGB composites in that it gives a quantitative measurement of how much of a pixel is flooded. This can provide stakeholders a method to exploit other datasets (ex. Cropland, population) to determine impacts from a flood event

## Slide 17: OPTICAL FLOOD PRODUCTS
The disadvantage of optical flood products is that they are limited to cloud free and daytime conditions only. However, they have the advantages of providing excellent data availability with large spatial coverage, and low cost.
Currently, the NOAA VIIRS flood extent product is produced operationally and the geostationary products are being transitioned to operations.
The primary inputs are the visible (VIS), near infrared (NIR), and short-wave infrared (SWIR) channels and also use a DEM to help downscale the data and provide more accurate flood mapping.

## Slide 18: Approach: two basic steps
Water Detection:
Every satellite orbit (2x/day)
Multi-look compositing
(cloud removal)
Over 1, 2, and 3 days
In more detail:
Water Detection: Apply algorithm to all incoming surface reflectance observations (2x/day):
    MODIS instrument onboard Terra and Aqua spacecraft
    VIIRS instrument onboard NOAA-20 and NOAA-21 spacecraft
Multi-look compositing: Require multiple water observations to mark a pixel as water
False-positive masking: Remove likely cloud-shadow and terrain-shadow false positives
Identification of flood: Compare detected water to permanent water (lakes, rivers), to identify flood

## Slide 19
SAR Flood Extent and Blended LEO/GEO/SAR Flood Product:
NOAA is currently developing a SAR-based flood extent and flood depth maps utilizing multiple SAR satellites (RCM, Sentinel 1, RadarSAT 2) as well as developing a blended LEO/GEO and SAR flood mapping. This will enhance the flood project by providing the highest resolution possible flood maps as well as flooding under cloud or at night. Future efforts will explore the use of L-Band (NISAR, SAOCOM, ROSE-L, ALOS 2/4)
This work is being done in collaboration with other agencies in the CEOS WG-Disasters Flood Pilot project

## Slide 20: SWOT
Surface Water Ocean Topography (SWOT) was jointly developed by NASA and Centre National D'Etudes Spatiales (CNES) with contributions from the Canadian Space Agency (CSA) and United Kingdom Space Agency.
The primary instrument on SWOT is the Ka-band Radar Interferometer (KaRIn). There are two antennas to measure the surface water topography.
Examples uses of SWOT
  Reservoir water storage and estimates of river discharge
  Provide sea surface heights and terrestrial water heights
  While it has a narrow width, research has been done by NASA to observe the river depths after flood events. However, the passes are infrequent, meaning that it is not useful for rapid response during disasters.

## Slide 21: PreOperational/Developmental - SAR Flood example

## Slide 22: Considerations to be aware of when using the NOAA LEO/GEO Flood product
Agricultural-related flooding: Some flooding water shown in the VIIRS flood maps may not be any hazard-related flooding, but from agriculture-related activities such as rice paddy planting and aquaculture.
Tides and Marsh lands: In some regions especially coastal areas, consistent flooding may be detected in the flood maps. These floods are mostly caused by the tides or occur over marsh lands, which do not pose any social impact.
Water reference map: The current water reference map we use for global flood mapping is from global water bodies of ESA CCI and MODIS global water mask (MOD44W Version 006). It might not reflect the new reservoirs and other hydraulic projects built after 2015, which may take some normal water as flooding water.
Solar Eclipses: For granules that are flagged as an “eclipse”, the flood product will not be produced.
Flooding caused by the tides in Great Bahamas is a natural phenomenon.
The widespread flooding water in the northeast of China from May 03 to 09, 2018 was not hazard-related flooding, but the “flooded” rice paddy areas during planting season.

## Slide 23: Considerations to be aware of when using the NOAA SAR Flood products
Beam blockage: Much like ground based radar, SAR can be blocked by terrain. This is especially important in very steep valleys.
Tree canopy: C and X band radars cannot penetrate through dense foliage. L-Band radars, such as NISAR (launch ~end of March), will be able to see flood waters below trees and overgrowth
Cities : Buildings and roads are very reflective in C-Band SAR instruments, while X and S-Band instruments are not as reflective. This means it is difficult to detect flood waters within major cities
Revisit and acquisition type: Most SAR instruments only acquire data over specific regions and there is generally a large latency to get the data as well as between passes. In addition, so acquisition “modes” can be as fine as 5m, but other times as large as 100m

## Slide 24
By utilizing derived flood maps, one can create a global or regional assessment of the number of days a given area is flooded for a given year (or longer time period).
This can help assess where the most flood prone regions are and help with flood mitigation/preparedness efforts
Currently NOAA has the VIIRS daily and 5-day flood maps for (2012-2020) to begin this effort, which is freely available to users for analysis.
Satellites as a tool to assess flood risk
Notes: 5 minutes activity:
title and picture appear, text hide
we ask participants:
How do you think the strength and weakness of using satellite as the tool to assess flood risk? (Mr. Faalih or Mr Rion)
raise your hand and let us know your thought.

## Slide 25
Li, S.; Goldberg, M.D.; Sjoberg, W.; Zhou, L.; Nandi, S.; Chowdhury, N.; Straka, W., III; Yang, T.; Sun, D. Assessment of the Catastrophic Asia Floods and Potentially Affected Population in Summer 2020 Using VIIRS Flood Products. Remote Sens. 2020, 12, 3176. https://doi.org/10.3390/rs12193176
ArcGIS or similar application
Population or other socio-economic database
Tying satellite data and socio-economic information together

## Slide 26: Future work
Explore the use of AI/ML for flood detection
Continue capacity building on flood projects
Explore the use of NISAR for flood detection
Validate the 30m flood products
Consideration of including the soil moisture and precipitation community in the flood pilots, since they are part of the flood cycle.

## Slide 27
Alexia Tsouni, NOA

## Slide 28
http://beyond-eocenter.eu/index.php/news-events/763-workshop-copernicus-beyond

## Slide 29
NOA/BEYOND
FloodHub service
Sentinel-1
diachronic flood
mapping
(automated
processing
since 2018)

## Slide 30
Dr. Haris KONTOES, Research Director of IAASARS/NOA, Operational Unit BEYOND Center for Earth Observation Research and Satellite Remote Sensing
Mr. Venetidis Konstantinos, Thematic Deputy Regional Governor for Civil Protection, Climate Change Impacts, Infrastructure and Projects
Mr. Elias Dasterides, Deputy Mayor of Social Solidarity, Sports and Civil Protection, Municipality of Alexandroupoli
Dr. Kabas N. George, Depute Head of Water Directorate, Eastern Macedonia - Thrace, Decentralized Administration of Macedonia - Thrace
Konstantinos Houvardas, Head of Civil Protection Department, Region of Eastern Macedonia and Thrace
Dimitris Manos, President of the Board, Hellenic Rescue Team, Evros Prefecture Branch

## Slide 31
Alexia Tsouni, Research Associate, Operational Unit BEYOND/IAASARS/NOA, Greece
Prof. Hhristo Nikolov, Space Research and Technology Institute Bulgarian Academy of Sciences, Bulgaria
Can Bayraktar, TÜBİTAK UZAY Space Technologies Research Institute, Senior Expert Researcher, Turkey
Prof. Uriburu Quirno, Marcelo, CONAE, the National Commission on Space Activities, Argentina & CEOS
The FloodHUB services by NOA/BEYOND for the Evros River Basin:
automated floods diachronic mapping and ad-hoc flood mapping
Maritsa watershed datacube focused on floods early warning in agricultural areas
TÜBİTAK UZAY's Capabilities in Space Technologies and Opportunities for International Collaboration in Earth Observation
Remote Sensing for Floods:
Insights from the CEOS Disasters
Working Group Pilot Project

## Slide 32
https://tubitak.gov.tr/en/announcement/2520-tubitak-general-secretariat-research-and-innovation-greece-gsri-bilateral-cooperation-call-open-application
https://gsri.gov.gr/invitations/prosklisi-ypovolis-aitiseon-chrimatodotisis-sti-drasi-dimeris-epistimoniki-kai-technologiki-synergasia-elladas-tourkias-tou-programmatos-antagonistikotita-espa-2021/